## Slide 1
ECE382
Lesson 32+33+34
1

## Slide 2: Overview
Lesson Outline
  Serial vs Parallel
  Types of serial communication
  Serial Communications
    UART
    SPI
    I2C

## Slide 3: Serial Communication
Parallel versus Serial?
Serial Advantages?
Serial Disadvantages?

## Slide 4: Serial Communication
Parallel versus Serial?
Serial Advantages?
  Simple interface – less hardware, less pins, less cost
  Faster clock speed per wire (no “cross-talk”)
  Longer Distance (no “cross-talk”)
Serial Disadvantages?
  Slower
  Overhead
  On-chip hardware to encode/decode serial signal

## Slide 5: Common Types of Serial Comm
CANBus: common in cars
RS-485: single master, multiple slave
MIL-STD-1553: common in aircraft and spacecraft
UART: Similar to RS232, but uses TTL, one-to-one
SPI: common in embedded systems (e.g., cellphones)
I2C: common in embedded systems (e.g., cellphones)

## Slide 6: CAN Bus
A Controller Area Network (CAN bus) is a robust vehicle bus standard designed to allow microcontrollers and devices to communicate with each other in applications without a host computer. It is a message-based protocol, designed originally for multiplex electrical wiring within automobiles to save on copper, but is also used in many other contexts.
USAFA is doing research on the CAN bus and a Tesla car

## Slide 7: RS-485
RS-485 supports inexpensive local networks and multidrop communications links, using the same differential signaling over twisted pair
Master
Slave
Slave
Slave
This is actually diagram for how to hook up a Raspberry Pi to a 485 network

## Slide 8: MIL-STD-1553
MIL-STD-1553 is a military standard that defines the mechanical, electrical, and functional characteristics of a serial data bus. It is used in aircraft and spacecraft on-board data handling (OBDH) subsystems. It features multiple (commonly dual) redundant balanced line physical layers, a (differential) network interface, time division multiplexing, half-duplex command/response protocol, and can handle up to 30 Remote Terminals (devices).

## Slide 9: MSP430
For this class we will focus on these 3:
  SPI
    Synchronous, full duplex (2-way comm)
    Datarates: 10Mbps
    Number of slaves depends on how many available pins you have
  UART
    Asynchronous, full duplex
    Data rates: 2.3M-9600 bps
    Point to point (only 2 devices talking)
  I2C
    Synchronous, half duplex (1-way comm)
    Data rates: 5M, 3.4M, 1M, 400K, and 100K bps
    127 slaves possible
Note, these numbers are HW dependent. Not every I2C sensor can achieve 5Mbps for example … check the datasheet

## Slide 10: SPI

## Slide 11: Serial Peripheral Interface (SPI)
Simple: with each clock cycle, a single bit is transferred from the MSB of one shift register to the other
Is this a half-duplex or full-duplex protocol?
Synchronous or Asynchronous protocol?
How many clocks cycles to transfer a byte?
Signals
  MOSI: Master Out Slave In
  MISO: Master In Slave Out
  SCLK: Clock
  SS: Slave Select
TI renamed these:
  MOSI = SIMO
  MISO = SOMI
We actually did this in code for Lab 2! You could have used the SPI interface to do it.

## Slide 12: Serial Peripheral Interface (SPI)
Slave Select signal allows the master to use the same interface to interact with multiple slaves. It's usually active low
Often, if you only have one slave, you will just tie SS low
Look at all the SS wires, typically you would use a MUX to help reduce the number of uC pins you need

## Slide 13: Serial Peripheral Interface (SPI)
Configurable Elements:
  Clock frequency
  Clock polarity
  Clock phase
On the MSP430:
  MSB first or LSB first
    Depends on the external HW you are talking to
  8-bits or 7-bits per transmission
    7-bits is justified toward the LSB
  3-pin or 4-pin modes
Control Register: Page 445 of the Family User Guide
SPI: Page 436 of the Family User Guide

## Slide 14: UCA/B Control Register 0
Control Register: Page 445 of the Family User Guide

## Slide 15: Phase = 0 and Polarity = 0
bis.b #UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 0, UCCKPL = 0
Input = 0xAA
Capture
Change
10101010
AA
Read on down clock

## Slide 16: Phase = 0 and Polarity = 1
bis.b #UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 0, UCCKPL = 1
Input = 0xAA
Capture
Change
Read on up clock
10101010
AA

## Slide 17: Phase = 1 and Polarity = 0
bis.b #UCCKPH|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 1, UCCKPL = 0
Input = 0xAA
Capture
Change
10101010
AA

## Slide 18: Phase = 1 and Polarity = 1
bis.b #UCCKPH|UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 1, UCCKPL = 1
Input = 0xAA
Capture
Change

## Slide 19: Phase = 0 and Polarity = 0
bis.b #UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 0, UCCKPL = 0
Input = 0x5D
Capture
Change
01011101
5D
Read on down clock

## Slide 20: Phase = 0 and Polarity = 1
bis.b #UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 0, UCCKPL = 1
Input = 0x5D
Capture
Change

## Slide 21: Phase = 1 and Polarity = 0
bis.b #UCCKPH|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 1, UCCKPL = 0
Input = 0x5D
Capture
Change

## Slide 22: Phase = 1 and Polarity = 1
bis.b #UCCKPH|UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 1, UCCKPL = 1
Input = 0x5D
Capture
Change

## Slide 23: Universal Serial Communication Interface (USCI)
On the MSP430:
  Two Universal Serial Communication Interfaces (USCI), A and B
    Can do multiple protocols (one is SPI), defined by configuration registers
    UCA0 and UCB0
  datasheet - control registers (pp 435-448)
Page 436 or 452 of the Family User Guide

## Slide 24: Universal Serial Communication Interface (USCI)
Step 1
  Setting the UCSWRST bit in the CTL1 register [16.4.2] resets the subsystem into a known state until it is cleared. All the registers will hold their default values.
Step 2
  Set the appropriate bits in the control registers to configure our signal the way we want.
  Remember, you've got to set UCSYNC for the system to function!
    CTL0 [bit 7 phase; bit 6 polarity; bit 3 master/slave; bit 0 UCSYNC = 1 ] [16.4.1]
    CTL1 [bit 7&6 clock; bit 0 UCSWRST][16.4.2]
    UCBRx [clock speed] [16.4.3 & 16.4.4]
    STAT [16.4.5]
Step 3
  All the ports on our MSP430 are multiplexed! We need to set the PxSEL and PxSEL2
Step 4
  Clear the UCSWRST bit in the CTL1 register - releases the system to operate.
pp 437 for Block Diagram
i.e (SW reset)

## Slide 25: Example SPI Setup
1) bis.b #UCSWRST, &UCB0CTL1
2) mov #UCCKPH|UCMSB|UCMST|UCSYNC, &UCB0CTL0
bis #UCSSEL_2, &UCB0CTL1
bis #BIT0, &UCB0BR0
clr &UCB0BR1
3) bis #LCD_SCLK_PIN|LCD_MOSI_PIN|LCD_MISO_PIN, &P1SEL
bis #LCD_SCLK_PIN|LCD_MOSI_PIN|LCD_MISO_PIN, &P1SEL2
4) bic.b #UCSWRST, &UCB0CTL1

## Slide 26: Universal Serial Communication Interface (USCI)
Step 5
  Use the subsystem!
    To send a byte, just write to the TXBUF register. [16.4.6]
    To read a received byte, read from the RXBUF register. [16.4.7]
  How do you know “you’ve got mail” or last transmission is done?
    You've got to monitor the flags in the IFG2 register [16.4.9] to know when it's safe the send
  TXIFG
    Set when TXBUF is ready for a byte
    Cleared on write
    Just because the TXBUF is ready for another byte doesn't mean that the transmission is complete! It's double-buffered!
  RXIFG
    Set when RXBUF has received a complete character
    Cleared on read
    This is what you should monitor to determine a transmission has completed!

## Slide 27: Example (loopback)
bis.b #UCSWRST, &UCA0CTL1
bis.b #UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; don't forget UCSYNC!
bis.b #UCSSEL1, &UCA0CTL1 ; select a clock to use!
bis.b #UCLISTEN, &UCA0STAT ; enables internal loopback
bis.b #BIT4, &P1SEL ; make UCA0CLK available on P1.4
bis.b #BIT4, &P1SEL2
bis.b #BIT2, &P1SEL ; make UCA0SSIMO available on P1.2
bis.b #BIT2, &P1SEL2
bis.b #BIT1, &P1SEL ; make UCA0SSOMI available on P1.1
bis.b #BIT1, &P1SEL2
bic.b #UCSWRST, &UCA0CTL1 ; enable subsystem
send mov.b #0xBB, &UCA0TXBUF ; place a byte in the TX buffer
wait bit.b #UCA0RXIFG, &IFG2 ; wait for receive flag to be set (operation complete)
jz wait
mov.b &UCA0RXBUF, r4 ; read RX buffer to clear flag
jmp send ; send another byte

## Slide 28: Logic Analyzer
Sending 0xBB once (0x1011 1011) [MSB first!]
  Note how the clock default state is high and data is read on the second clock edge - consistent with our settings.

## Slide 29: UART

## Slide 30: UART
The universal asynchronous receiver-transmitter (UART) takes bytes of data and transmits the individual bits in a sequential fashion
  Although the protocol defines all kinds of things, I have ALWAYS used 8 bits, no parity, one stop bit (8N1)
Data rate: 230400 bps
The blue top spins 360 degs at 5 Hz and for every degree provides distances to obstacles up to 12m to map rooms

## Slide 31: UART
P1.1
P1.2
It is common for serial to be tied to specific HW pins
USCI_Ax for UART
USCI_Bx for I2C or SPI

## Slide 32: UART Serial Protocol
Example of 5O1 (not common at all)
  5 bits
  Odd parity (odd #1’s: 0 or even #1’s:1)
  1 stop bit
  Data bit closes to START is the LSb
Most common is 8N1
  8 bits
  N: no parity bit
  1 stop bit

## Slide 33: Setup
Remember to set the TX and RX pins too!

## Slide 34: UART Datarate Settings
Common serial data rates for a 1MHz clock
Common when using the SMCLK
9600 8N1 very common

## Slide 35: Serial CTL

## Slide 36: UART
These come from that big table above or p 424 Fam User Guide

## Slide 37: UART Setup
Steps:
  Set P1SEL/P1SEL2 for P1.1 and P1.2 for the UCA0
  Hold the USCI with UCA0CTL1 = UCSWRST;
  Set clock to SMCLK
  Set UCA0CTL/1 correctly
  Set UCA0MCTL correctly (p 424 Fam User Guide)
  Take USCI out of reset with UCA0CTL1 &= ~UCSWRST;
Example: 9600 8N1
  UCA0CTL1 |= UCSSEL_2; // select BRCLK = SMCLK
  UCA0CTL0 = 0; // 8N1
  UCA0BR0 = 104; // p 424 1MHz@9600
  UCA0BR1 = 0; // p 424 1MHz@9600
  UCA0MCTL = UCBRS0; // UCBRSx=1

## Slide 38: TX
Simple put character function:
// wait for TX to be ready for sending
void uart_putc(const int8_t c){
while (!(IFG2 & UCA0TXIFG)); // USCI_A0 TX buffer ready?
UCA0TXBUF = c; // TX
}
Now, you could easily expand this into transmitting strings or (char* or int8_t*) or char[]
You can declare char arrays like this:
  char my_str[] = “hello”; // compiler will allocate the array size
  Now C will create an array of: [‘h’,’e’,’l’,’l’,’o’,’\x00’]
    ’\x00’ is the same as 0 … it is just a string terminator and you can look for it in a for loop!

## Slide 39: RX
Simple get character (8 bits)
We won’t be using this for Lab 4
int8_t getchar(void) {
while(!(IFG2 & UCA0RXIFG)); // anything to get?
IFG2 &= ~UCA0RXIFG; // clear the flag
return UCA0RXBUF; // get the data
}
Again, you can expand this out into grabbing a string of characters, a bunch of bytes until you get a certain stop sequence, or even a fixed number of bytes
It is common in serial communications to define data packet formats uses them when you are doing TX/RX

## Slide 40: I2C

## Slide 41: I2C Sensors
I2C is common protocol for embedded systems
Common applications:
  Camera adjustments
  Inertial measurement units
  Temperature sensors
  Pressure sensors
  EEPROM
  etc
Cellphone IMU ($14)

## Slide 42: Format
I2C is a packet based protocol with a 7b address
  Allows 128 devices on network
  More complex than UART and SPI
  Popular in a variety of applications
    Memory, MUXes, ADCs, etc
  Only need 2 wires (no SS link on SPI)

## Slide 43: Initialize the I2C Subsystem
void i2c_init(void){
UCB0CTL1 = UCSWRST; // hold in reset while configuring
UCB0CTL0 = UCMST | UCMODE_3 | UCSYNC; // set to master
/**
* Set to 100kHz when sourcing from SMCLK
* where SMCLK = 1MHz
*/
UCB0BR0 = 10;
UCB0BR1 = 0;
UCB0CTL1 |= UCSSEL_2; // set clock to SMCLK
UCB0CTL1 &= ~UCSWRST; // take out of reset
}

## Slide 44: TX/RX
The transmitting data
int i2c_transfer(uint8_t addr, uint8_t *buf, size_t nbytes){
UCB0I2CSA = addr; // set slave address
UCB0CTL1 |= UCTR | UCTXSTT; // set start condition
while ((UCB0CTL1 & UCTXSTT) && ((IFG2 & UCB0TXIFG) == 0));
err = _check_ack(dev); // check for ACK … defined elsewhere
while ((err == 0) && (nbytes > 0)) {
UCB0TXBUF = *buf;
while ((IFG2 & UCB0TXIFG) == 0) {
err = _check_ack(dev);
if (err < 0) break;
}
buf++; // grab next byte
nbytes--;
}
return err; // 0: good, -1: error occurred
}
RX will be similar but not the same

## Slide 45: ICE: UART Serial LCD
Use the code examples in this lesson to:
  Setup your MSP430 for serial comm
    9600 bps 8N1
  Have the LCD display “Hello” repeatedly
  When you fill up the LCD clear it
  Take a look at the LCD datasheet
    Clear the screen
  Debugging, might be useful to blink an led or two … up to you
Getting this working will help you in Lab 4

## Slide 46
Picture of setup

## Slide 47: Serial LCD Commands
Suggest you read the LCD datasheet, here is the command summary

## Slide 48: BACKUPS