## Slide 1
ECE382
Lesson 26+27+28
1

## Slide 2: Overview
Lesson Outline
  Serial vs Parallel
  Serial Communications
    UART
    SPI
    I2C

## Slide 3: Serial Communication
Parallel versus Serial?
Serial Advantages?
Serial Disadvantages?

## Slide 4: Serial Communication
Parallel versus Serial?
Serial Advantages?
  Simple interface – less hardware, less pins, less cost
  Faster clock speed per wire (no “cross-talk”)
  Longer Distance (no “cross-talk”)
Serial Disadvantages?
  Slower
  Overhead
  On-chip hardware to encode/decode serial signal

## Slide 5: Common Types of Serial Comm
UART: Similar to RS232, but uses TTL, one-to-one
SPI: common in embedded systems (e.g., cellphones)
I2C: common in embedded systems (e.g., cellphones)
CANBUS: common in cars
RS-232: peer (one-to-one) async comm
RS-485: single master, multiple slave
MIL-STD-1553: common in aircraft and spacecraft
There are more … these are just off the top of my head 

## Slide 6: UART

## Slide 7: UART
P1.1
P1.2
It is common for serial to be tied to specific HW pins
USCI_Ax for UART
USCI_Bx for I2C or SPI

## Slide 8: Setup
Remember to set the TX and RX pins too!

## Slide 9: UART Datarate Settings
Common serial data rates for a 1MHz clock

## Slide 11: UART

## Slide 13: SPI

## Slide 14: Serial Peripheral Interface (SPI)
Simple: with each clock cycle, a single bit is transferred from the MSB of one shift register to the other
Is this a half-duplex or full-duplex protocol?
Synchronous or Asynchronous protocol?
How many clocks cycles to transfer a byte?
Signals
  MOSI: Master Out Slave In
  MISO: Master In Slave Out
  SCLK: Clock
  SS: Slave Select
TI renamed these:
  MOSI = SIMO
  MISO = SOMI

## Slide 15: Serial Peripheral Interface (SPI)
Slave Select signal allows the master to potentially use the same interface to potentially interact with multiple slaves. It's usually active low

## Slide 16: Serial Peripheral Interface (SPI)
Can we just tie SS low?
Configurable Elements:
  Clock frequency
  Clock polarity
  Clock phase
On the MSP430:
  MSB first or LSB first
    you'll pretty much always want MSB first, which isn't the default
  8-bits or 7-bits per transmission
    7-bits is justified toward the LSB
  3-pin or 4-pin modes
Page 35 of LCD Driver
Control Register: Page 445 of the Family User Guide
SPI: Page 436 of the Family User Guide

## Slide 17: UCA/B Control Register 0
Control Register: Page 445 of the Family User Guide

## Slide 18: Phase = 0 and Polarity = 0
bis.b #UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 0, UCCKPL = 0
Input = 0xAA
Capture
Change

## Slide 19: Phase = 0 and Polarity = 1
bis.b #UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 0, UCCKPL = 1
Input = 0xAA
Capture
Change

## Slide 20: Phase = 1 and Polarity = 0
bis.b #UCCKPH|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 1, UCCKPL = 0
Input = 0xAA
Capture
Change

## Slide 21: Phase = 1 and Polarity = 1
bis.b #UCCKPH|UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 1, UCCKPL = 1
Input = 0xAA
Capture
Change

## Slide 22: Phase = 0 and Polarity = 0
bis.b #UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 0, UCCKPL = 0
Input = 0x5D
Capture
Change

## Slide 23: Phase = 0 and Polarity = 1
bis.b #UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 0, UCCKPL = 1
Input = 0x5D
Capture
Change

## Slide 24: Phase = 1 and Polarity = 0
bis.b #UCCKPH|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 1, UCCKPL = 0
Input = 0x5D
Capture
Change

## Slide 25: Phase = 1 and Polarity = 1
bis.b #UCCKPH|UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; UCCKPH = 1, UCCKPL = 1
Input = 0x5D
Capture
Change

## Slide 26: Universal Serial Communication Interface (USCI)
On the MSP430:
  Two Universal Serial Communication Interfaces (USCI), A and B
    Can do multiple protocols (one is SPI), defined by configuration registers
    UCA0 and UCB0
  datasheet - control registers (pp 435-448)
Page 436 or 452 of the Family User Guide

## Slide 27: Universal Serial Communication Interface (USCI)
Step 1
  Setting the UCSWRST bit in the CTL1 register [16.4.2] resets the subsystem into a known state until it is cleared. All the registers will hold their default values.
Step 2
  Set the appropriate bits in the control registers to configure our signal the way we want.
  Remember, you've got to set UCSYNC for the system to function!
    CTL0 [bit 7 phase; bit 6 polarity; bit 3 master/slave; bit 0 UCSYNC = 1 ] [16.4.1]
    CTL1 [bit 7&6 clock; bit 0 UCSWRST][16.4.2]
    UCBRx [clock speed] [16.4.3 & 16.4.4]
    STAT [16.4.5]
Step 3
  All the ports on our MSP430 are multiplexed! We need to set the PxSEL and PxSEL2
Step 4
  Clear the UCSWRST bit in the CTL1 register - releases the system to operate.
pp 437 for Block Diagram
i.e (SW reset)

## Slide 28: Example SPI Setup for Lab 3
1) bis.b #UCSWRST, &UCB0CTL1
2) mov #UCCKPH|UCMSB|UCMST|UCSYNC, &UCB0CTL0
bis #UCSSEL_2, &UCB0CTL1
bis #BIT0, &UCB0BR0
clr &UCB0BR1
3) bis #LCD_SCLK_PIN|LCD_MOSI_PIN|LCD_MISO_PIN, &P1SEL
bis #LCD_SCLK_PIN|LCD_MOSI_PIN|LCD_MISO_PIN, &P1SEL2
4) bic.b #UCSWRST, &UCB0CTL1

## Slide 29: Universal Serial Communication Interface (USCI)
Step 5
  Use the subsystem!
    To send a byte, just write to the TXBUF register. [16.4.6]
    To read a received byte, read from the RXBUF register. [16.4.7]
  How do you know “you’ve got mail” or last transmission is done?
    You've got to monitor the flags in the IFG2 register [16.4.9] to know when it's safe the send
  TXIFG
    Set when TXBUF is ready for a byte
    Cleared on write
    Just because the TXBUF is ready for another byte doesn't mean that the transmission is complete! It's double-buffered!
  RXIFG
    Set when RXBUF has received a complete character
    Cleared on read
    This is what you should monitor to determine a transmission has completed!

## Slide 30: Example (loopback)
bis.b #UCSWRST, &UCA0CTL1
bis.b #UCCKPL|UCMSB|UCMST|UCSYNC, &UCA0CTL0 ; don't forget UCSYNC!
bis.b #UCSSEL1, &UCA0CTL1 ; select a clock to use!
bis.b #UCLISTEN, &UCA0STAT ; enables internal loopback
bis.b #BIT4, &P1SEL ; make UCA0CLK available on P1.4
bis.b #BIT4, &P1SEL2
bis.b #BIT2, &P1SEL ; make UCA0SSIMO available on P1.2
bis.b #BIT2, &P1SEL2
bis.b #BIT1, &P1SEL ; make UCA0SSOMI available on P1.1
bis.b #BIT1, &P1SEL2
bic.b #UCSWRST, &UCA0CTL1 ; enable subsystem
send mov.b #0xBB, &UCA0TXBUF ; place a byte in the TX buffer
wait bit.b #UCA0RXIFG, &IFG2 ; wait for receive flag to be set (operation complete)
jz wait
mov.b &UCA0RXBUF, r4 ; read RX buffer to clear flag
jmp send ; send another byte

## Slide 31: Logic Analyzer
Sending 0xBB once (0x1011 1011) [MSB first!]
  Note how the clock default state is high and data is read on the second clock edge - consistent with our settings.

## Slide 32: I2C

## Slide 33: BACKUPS