## Slide 1
ECE382
Lesson 20
1

## Slide 2: Overview
Lesson Outline
  Functions
  Headers
  Libraries (modularity)
  Combining ASM and C

## Slide 3: C Language: Functions
Functions: like subroutines in assembly. Remember Modularity?
Example Function Call
void main(void)
{
uint8_t mySummation;
uint8_t maxN = 42;
mySummation = summation(23);
mySummation = summation(maxN);
}
How does the compiler know what “summation” is?

## Slide 4: C Language: Functions
Function Prototype
Promises the compiler that the function is implemented elsewhere in a C file
A header file provides the “interface” to the function
You are allowed to "call" the function from your code
The function prototype must be defined in a location physically before you call it (i.e. defined above main() or in a #include file).
If you offer a prototype but don't provide an implementation, you'll get a linker error.
<output_type> func_name(<input type 1> <variable name 1>, ...);
uint8_t summation (uint8_t n);
void main(void){
uint8_t mySummation;
uint8_t maxN = 42;
mySummation = summation(23);
mySummation = summation(maxN);
}
uint8_t summation(uint8_t n){
// recursion!
// A function calling itself
if (n <= 0)
return 0;
else
return n + summation(n-1);
}
Lets the compiler know, summation is defined later in the code

## Slide 5: C Language: Function Parameters
Pass by Value - Passing the actual value of the variable ( pass a copy )
Good choice for small-sized variables
Expensive to copy larger variables (e.g. structures, arrays, etc.)
Pass by Pointer - Pass pointer into variable (same as Pass by Reference) ( pass access to the original )
Constant size parameter no matter how large the object it is to point to
Allows you to directly modify the variable in the function without a return statement
Pass by Value Example: char x=5, y=10; z = some_function(x, y) … char some_function(char a, char b) { // does this change x and y? a += 5; b += 5; return a + b; } | Pass by Reference Example: char x=5; y=10; z = some_function(&x, &y) … char some_function(char* a, char* b){ // does this change x and y? *a += 5; *b += 5; return *a + *b; }
NOTE: we are getting a little ahead of ourselves with pointers

## Slide 6: Writing Clean Code
Meaningful Names
Use intention-revealing names ("self-documenting")
  int d, temp; // elapsed time in days, a temporary variable
  int elapsedTimeInDays, daysSinceModification;
Make meaningful distinctions
  void copyChars(char* a1, char* a2)
  void copyChars(char* source, char* destination)
Use pronounceable names
  DtaRcrd
  DataRecord
Use searchable names
  MAX
  MAX_STUDENTS
Functions: use verbs!
  forward()
  moveForward()
Don't be cute
  holyHandGrenade()
  deleteItem()
Pick one word per concept
  Bad: fetch(), retrieve(), get()
  Good (pick one): get()
Okay to use i, j, k for loop counters

## Slide 7: Clean Functions
Small - ideally less than 10 lines long
Do one thing
Use descriptive names
Parameters: rarely need more than two or three
Side effects - function should only do what you say it does
Do not use global variables
Only depend on local variables / parameters
Don't repeat yourself - write a function instead of copy / paste code multiple times
Only one entry / exit point
Indent correctly!
Use common standard C function names so other people know what is happening
  Bad: spiFlushBuffer() Good: spiWrite()
  Bad: i2cLoad() Good: i2cRead()
  Others: push, pop, open, close … as you program more, you will get it

## Slide 8: Clean Comments
Comment on "big picture" items
  Head of each file
  Definition of each function
  Beginning of each major block of code
As you move deeper in the hierarchy, the comments are more specific
Try writing functions / meaningful names
  if ((employeeFlags & HOURLY_FLAGS) && (employeeAge > 65)) ...
  if (isEligibleForFullBenefits(employee)) ...
TODO or FIXME comments
  // TODO: Make this into a function
  // TODO: Add another parameter to allow saving data
  // FIXME: clean up code so it is readable
Bad comments
  Restating your code (a = 1; // Setting a to 1)
  Commented-Out code
    Ok in development, but when you submit your final code for a grade … bad!
  Too much information … ok, students almost NEVER do this
  Don't comment bad code - rewrite it.
    If you find yourself commenting too much, it is probably bad code that needs to be re-written

## Slide 9: C Language: Preprocessor Commands
Preprocessor Commands: The preprocessor is executed before your code compiles
#include "file_name.h"
  Essentially a "copy and paste" of the file_name.h into your file
  "file_name.h", the preprocessor will search in your project working directory.
#include <file_name.h>
  Same as above, BUT, pulls from a standard or installed library
#define <SINGLE_WORD> <replacement_token>
  Essentially a global "search and replace" within your code
  Anytime the <SINGLE_WORD> token appears, it will be replaced by the <replacement token>
  Prefer to use: const int8_t <single_word> = <token>; // now the complier can check your code
#ifndef <SOME_CONSTANT> ... <some code> ... #endif
  Code is only included if <SOME_CONSTANT> is not defined
  Usually, your first line of code will be to #define <SOME_CONSTANT>
typedef unsigned short int16;
  Create your own type

## Slide 10: C Header files
A separate file that contains a related set of:
  Function prototypes
  typedef declarations
  #define constants
  etc.
File naming convention:
  All lowercase
  Use "_" to combine words
  ".h" is the file extension
Example: atd_helper.h
You must "wrap" the header in a #ifndef to prevent circular inclusions (also called guarding)
#ifndef __MYSTUFF_H__
#define __MYSTUFF_H__
// #define is ok here
// Your header file code (typedefs, function prototypes, #defines, etc.)
// Use good comment headers to define each function (see example)
// ...
#endif // __MYSTUFF_H__
mystuff.h (header)
-----------------------------
#include <stdlib.h>
#ifndef __mystuff_h__
#define __mystuff_h__
unsigned int summation (uint8_t n);
#endif
OK to use a #define here because this is an ifndef/define flow control

## Slide 11: C Implementation Files
A separate C file that implements the header file
Contains the function definitions
#include the header file as your first line
File naming convention:
  Same name as the header file!
  ".c" is the file extension
  Example: atd_helper.c
#include “mystuff.h"
// Function definitions
// ...
mystuff.c (implementation)
-----------------------------
#include “mystuff.h”
uint8_t summation(uint8_t n){
// recursion!
if (n <= 0)
return 0;
else
return n + summation(n-1);
}

## Slide 12: C Language: Libraries
main.c
-----------------------------
#include “mystuff.h”
void main(void){
uint8_t mySummation;
uint8_t maxN = 42;
mySummation = summation(23);
mySummation = summation(maxN);
}
mystuff.c (implementation)
-----------------------------
#include “mystuff.h”
uint8_t summation(uint8_t n){
// recursion!
if (n <= 0)
return 0;
else
return n + summation(n-1);
}
mystuff.h (header)
-----------------------------
#include <stdlib.h>
#ifndef __mystuff_h__
#define __mystuff_h__
unsigned int summation (uint8_t n);
#endif
Modular, reusable code any project can use.
These ensure the header is included in code only ONCE

## Slide 13: C Language: Libraries
main.c
-----------------------------
#include “mystuff.h”
void main(void){
uint8_t mySummation;
uint8_t maxN = 42;
mySummation = summation(23);
mySummation = summation(maxN);
}
mystuff.c (implementation)
-----------------------------
#include “mystuff.h”
uint8_t summation(uint8_t n){
// recursion!
if (n <= 0)
return 0;
else
return n + summation(n-1);
}
mystuff.h (header)
-----------------------------
#pragma once
#include <stdlib.h>
unsigned int summation (uint8_t n);
Modular, reusable code any project can use.
This also ensures the header is included in code only ONCE
This depends on the version of your compiler and SEEMS to be viewed as “poor form” by some programmers

## Slide 14: C Language: Libraries
Using libraries helps you:
  Write modular, reusable code that multiple projects can use
  Reduces errors in your code
    Once a library is written AND tested, it should NEVER introduce bugs into your code
    Writing test cases (unit tests) are common practice when developing code

## Slide 15: Combining ASM and C
Need to define variables or functions with keyword extern
  extern uint8_t horrible_global_variable;
  extern void my_function(int16_t value);
Why??
  Assembly code doesn’t have header files … remember?

## Slide 16: BACKUPS