## Slide 1
ECE382
Lesson 32?
1

## Slide 2: Overview
Lesson Outline
  Pulse Width Modulation (PWM)
  Capture and Compare

## Slide 3: PWM Setup Tasks
Set I/O direction for output
  MUX PWM
Set period
Set on time
Enable PWM mode on timer
Config / Start timer

## Slide 4: Timer Block Diagram
0
1
2
3
4
5
clks
cnts
Family User Guide pp 357
Blue Book pp 46
Capture / Compare

## Slide 5: Backup Slides
Family User Guide pp 372

## Slide 6: Timer Block Diagram
Family User Guide pp 357
CAP

## Slide 7: Input Capture
Capture mode is selected when the CAP bit in TACCTL is set to 1. It's used to record time events. It can be used for:
  Event detection
  Event counting
  Pulse-width measurement ***
  Frequency measurement
Each TACCRx has two possible capture pins - CCIxA and CCIxB. The one being monitored is selectable by software.
If a capture occurs: - The TAR value is copied into the TACCRx register - The interrupt flag CCIFG is set
Family User Guide pp 363

## Slide 8: Backup Slides
Family User Guide pp 372

## Slide 9: Timer Block Diagram
CCISx
Family User Guide pp 357
SCS
CMx
CCIFG

## Slide 10: Input Capture
The input signal level can be read at any time via the CCI bit. MSP430x2xx family devices may have different signals connected to CCIxA and CCIxB. See the device-specific data sheet for the connections of these signals.
Family User Guide pp 362

## Slide 11: Input Capture
The input signal level can be read at any time via the CCI bit. MSP430x2xx family devices may have different signals connected to CCIxA and CCIxB. See the device-specific data sheet for the connections of these signals.
Device Specific pp 16

## Slide 12: Backup Slides
Family User Guide pp 372

## Slide 13: Input Capture
Device Specific pp 43

## Slide 14: Output Compare
Compare mode is selected when the CAP bit in TACCTL is set to 0
Same Timer Modes: MCx
Count up to TACCRO. Now adding two new registers: TA0CCR1 and TA0CCR2
Mcx | Mode | Description
00 | Stop | The timer is halted. MC_0
01 | Up | The timer repeatedly counts from zero to the value of TACCR0. MC_1
10 | Continuous | The timer repeatedly counts from zero to 0FFFFh. MC_2
11 | Up/down | The timer repeatedly counts from zero up to the value of TACCR0 and back down to zero. MC_3

## Slide 15: Timer Block Diagram
Family User Guide pp 357
CCR0-2

## Slide 16: Output Compare
You will likely use mode 3 & 7 for PWM

## Slide 17: Ports?
Pin 3 TA0.0 P1.1
Pin 4 TA0.1 P1.2
Pin 8 TA1.0 P2.0
Pin 9 TA1.1 P2.1

## Slide 18: PWM Setup Tasks
Set I/O direction for output
  MUX PWM
Set period
Set on time
Enable PWM mode on timer
Config / Start timer
TAxCCRx
TAxCCTLx
PxSEL, PxSEL2
PxDIR
TAxCTL

## Slide 19: Example
#include <msp430.h>
int main(void)
{
WDTCTL = WDTPW|WDTHOLD; // stop the watchdog timer
P1DIR |= BIT2; // TA0CCR1 on P1.2
P1SEL |= BIT2; // TA0CCR1 on P1.2
TA0CTL &= ~MC1|MC0; // stop timer A0
TA0CTL |= TACLR; // clear timer A0
TA0CTL |= TASSEL1; // configure for SMCLK
TA0CCR0 = 100; // set signal period to 100 clock cycles (~100 microseconds)
TA0CCR1 = 25; // set duty cycle to 25/100 (25%)
TA0CCTL1 |= OUTMOD_7; // set TACCTL1 to Reset / Set mode
TA0CTL |= MC0; // count up
while (1) {
__delay_cycles(1000000);
TA0CCR1 = 50; // set duty cycle to 50/100 (50%)
__delay_cycles(1000000);
TA0CCR1 = 75; // set duty cycle to 75/100 (75%)
__delay_cycles(1000000);
TA0CCR1 = 100; // set duty cycle to 100/100 (100%)
__delay_cycles(1000000);
TA0CCR1 = 25; // set duty cycle to 25/100 (25%)
}
return 0;
}

## Slide 20: Example with Interrupt
#include <msp430.h>
void main(void)
{
WDTCTL = WDTPW|WDTHOLD;// stop the watchdog timer
P2DIR |= BIT1; // TA1CCR1 on P2.1
P2SEL |= BIT1; // TA1CCR1 on P2.1
P2OUT &= ~BIT1;
TA1CTL |= TASSEL_2|MC_1|ID_0; // configure for SMCLK
P1DIR |= BIT0; //use LED to indicate duty cycle has toggled
P1REN |= BIT3;
P1OUT |= BIT3;
TA1CCR0 = 1000; // set signal period to 1000 clock cycles (~1 millisecond)
TA1CCR1 = 250; // set duty cycle to 250/1000 (25%)
TA1CCTL0 |= CCIE; // enable CC interrupts
TA1CCTL1 |= OUTMOD_7|CCIE; // set TACCTL1 to Set / Reset mode//enable CC interrupts
TA1CCTL1 &= ~CCIFG; //clear capture compare interrupt flag
_enable_interrupt();
while (1) {
while (P1IN & BIT3); //every time the button is pushed, toggle the duty cycle
__delay_cycles(1000000);
TA1CCR1 = 1000; // set duty cycle to 1000/1000 (100%)
while (P1IN & BIT3);
__delay_cycles(1000000);
TA1CCR1 = 750; // set duty cycle to 750/1000 (75%)
while (P1IN & BIT3);
__delay_cycles(1000000);
TA1CCR1 = 500; // set duty cycle to 500/1000 (50%)
while (P1IN & BIT3);
__delay_cycles(1000000);
TA1CCR1 = 250; // set duty cycle to 250/1000 (25%)
while (P1IN & BIT3);
__delay_cycles(1000000);
TA1CCR1 = 100; // set duty cycle to 100/1000 (10%)
while (P1IN & BIT3);
__delay_cycles(1000000);
TA1CCR1 = 20; // set duty cycle to 20/1000 (2%)
}
}
#pragma vector = TIMER1_A0_VECTOR // This is from the MSP430G2553.h file
__interrupt void captureCompareInt (void) {
P1OUT |= BIT0; //Turn on LED
// Disable Timer A Interrupt
TA1CCTL1 &= ~CCIFG; //clear capture compare interrupt flag
// TACTL &= ~TAIFG;
}
#pragma vector = TIMER1_A1_VECTOR // This is from the MSP430G2553.h file
__interrupt void captureCompareInt2 (void) {
P1OUT &= ~BIT0; //Turn off LED
// Disable Timer A Interrupt
TA1CCTL1 &= ~CCIFG; //clear capture compare interrupt flag
// TACTL &= ~TAIFG;
}

## Slide 21: BACKUPS

## Slide 22: Using DC Motors
How do DC motors work? How do you make them go faster?

## Slide 23: Basic H Bridge

## Slide 24: Direction Control
H-bridge is design to turn on/off the FETs in a particular order such that current can flow through the motor in one or 2 ways. This has the effect of turning the motor shaft either CW or CCW

## Slide 25: Danger!
Since this is already setup on your system, this shouldn’t be a problem. However, if you build your own h-bridge, be careful!

## Slide 26: DC Motors & Generators

## Slide 27: How Does a DC Motor Work
Typical DC motor characteristics:
Stall torque – max torque produced when it stops moving
Voltage – operating voltage (higher V, lower current)
No load current – min free running current
Stall current – max current at stall
Horsepower: 2 hp = ~1492 W
1 hp = 745.7 W

## Slide 28: Motor Torque
Torque is a measure of how much a force acting on an object causes that object to rotate.

## Slide 29: Using DC Motors
How do DC motors work? How do you make them go faster?
  Provide analog DC voltage… The higher the voltage, the faster it spins
Two issues interfacing MSP430 with a DC motor?
  MSP430 only produces two voltages (Vcc and Gnd)
Solution? PWM- pulse width modulation (remember this?)
  MSP430 does not source enough current to power the motors (blow the chip)
Solution? Motor driver chip (SN754410)
MSP430 Timer system helps
Input Capture: Monitor a pin for a specified signal (rising edge, falling edge, either edge) and record when it occurs.  Ultrasonic sensor
Output Compare: Generate a specified signal with precise timing. (can make a PWM signal)  drive motors, servos
Do Not Exceed the 1A current rating (i.e. ~60% Duty Cycle)