## Slide 1: S06: Assembler / Linker
Required: PM: Ch 7, pgs 81-107 Assembler Directives
Recommended: MSP430 Assembly Tutorial MSP430 Disassembly.docx FUG: 3.4

## Slide 2: CS 224
Chapter | Lab | Homework
S00: Introduction |  | 
Unit 1: Digital Logic |  | 
S01: Data Types S02: Digital Logic | L01: Warm-up L02: FSM | HW01 HW02
Unit 2: ISA |  | 
S03: ISA S04: Microarchitecture S05: Stacks / Interrupts S06: Assembly | L03: Blinky L04: Micro-arch L05b: Traffic Light L06a: Morse Code | HW03 HW04 HW05 HW06
Unit 3: C |  | 
S07: C Language S08: Pointers S09: Structs S10: I/O | L07b: Morse II L08a: Life L09b: Snake | HW07 HW08 HW09 HW10

## Slide 3: Learning Outcomes…
After completing this section, you should be able to
Explain the difference between a low level and high level language.
Justify the study/use of assembly code.
Contrast assembler directives with assembler code.
Describe the assembly/linker process.
Contrast a library with a computer program.
Describe the different types of program sections and explain how they are used by the linker to create an executable.
Give examples of emulated and intrinsic instructions.
Use systematic decomposition to create an assembly program.

## Slide 4: Topics to Cover…
High Level vs. Assembly
Assembly Instructions
Emulated Instructions
Assembler
  Assembly Code
  Assembly Sections
  Assembly Process
  Assembly Directives
Linker
  Libraries
  Linking multiple files
How to Code in Assembly
Systematic Decomposition

## Slide 5: High Level vs. Assembly
High Level Languages
  More programmer friendly
  More ISA independent
  Each high-level statement translates to several instructions in the ISA of the computer
Assembly Languages
  Lower level, closer to ISA
  Very ISA-dependent
  Each instruction specifies a single ISA instruction
  Makes low level programming more user friendly
  More efficient code
High Level vs. Assembly

## Slide 6: Why Assembly Code?
Allows us to work at a slightly higher level than machine language.
Allows us to use symbolic names for opcodes
Allows us to use symbolic names for memory locations -
  SUM, PRODUCT
  Don’t need to know every address of every storage location.
Calculates addresses for us – really a big deal!
Helps to allocate memory locations.
Provides additional error checking
High Level vs. Assembly

## Slide 7: Assembly Instructions

## Slide 8: Double Operand
Mnemonic | Operation | Description
Arithmetic instructions |  | 
ADD(.B or .W) src,dst | src+dstdst | Add source to destination
ADDC(.B or .W) src,dst | src+dst+Cdst | Add source and carry to destination
DADD(.B or .W) src,dst | src+dst+Cdst (dec) | Decimal add source and carry to destination
SUB(.B or .W) src,dst | dst+.not.src+1dst | Subtract source from destination
SUBC(.B or .W) src,dst | dst+.not.src+Cdst | Subtract source and carry from destination
Double Operand Instructions
Logical and register control instructions |  | 
AND(.B or .W) src,dst | src.and.dstdst | AND source with destination
BIC(.B or .W) src,dst | .not.src.and.dstdst | Clear bits in destination
BIS(.B or .W) src,dst | src.or.dstdst | OR (set) bits in destination
BIT(.B or .W) src,dst | src.and.dst | Test bits in destination
XOR(.B or .W) src,dst | src.xor.dstdst | XOR source with destination
Data instructions |  | 
CMP(.B or .W) src,dst | dst-src | Compare source to destination
MOV(.B or .W) src,dst | srcdst | Move source to destination

## Slide 9: Single Operand
Double Operand Instructions
Mnemonic | Operation | Description
RRC(.B or .W) src | C  MSB  MSB−1 .... LSB+1  LSB  C | Rotate right thru carry
SWPB(.W) src | Bits 15 to 8 <−> bits 7 to 0 | Swap bytes
RRA(.B or .W) src | MSB  MSB, MSB  MSB−1, ... LSB+1  LSB, LSB  C | Rotate right arithmetic
SXT(.B) src | Bit 7 → Bit 8 ......... Bit 15 | Sign extend byte
PUSH(.B or .W) src | SP-2SP, src@SP | Push byte/word source on stack
CALL dst | dsttmp ,SP-2SP, PC@SP, tmpPC | Subroutine call to destination
RETI | TOSSR, SP+2SP TOSPC, SP+2SP | Return from interrupt

## Slide 10: Relative Jump Instructions
Double Operand Instructions
Mnemonic | Operation | Description
JNZ/JNE | Jump if Z == 0 | Jump if not equal (if !=)
JZ/JEQ | Jump if Z == 1 | Jump if equal (if ==)
JNC/JLO | Jump if C == 0 | Jump if carry (if unsigned <)
JC/JHS | Jump if C == 1 | Jump if no carry (if unsigned >=)
JN | Jump if N == 1 | Jump if negative (No JP)
JGE | Jump if N == V | Jump if zero or positive (if signed >=)
JL | Jump if N != V | Jump if less than (if signed <)
JMP | Jump | Jump unconditionally
PC-relative jumps, adding twice the sign-extended offset to the PC, for a jump range of -1024 to +1022.

## Slide 11: Emulated Instructions
In addition to the 27 instructions defined by the MSP 430 ISA, there are 24 additional emulated instructions
The emulated instructions make reading and writing code more easy, but do not have their own op-codes
Emulated instructions are replaced automatically by native MSP 430 instructions
There are no penalties for using emulated instructions.
Emulated Instructions

## Slide 12: Emulated Instructions
Mnemonic |  | Operation |  | Emulation |  | Description
Arithmetic instructions |  |  |  |  |  | 
ADC(.B or .W) dst | dst+Cdst |  | ADDC(.B or .W) #0,dst |  | Add carry to destination | 
DADC(.B or .W) dst | dst+Cdst (decimally) |  | DADD(.B or .W) #0,dst |  | Decimal add carry to destination | 
DEC(.B or .W) dst | dst-1dst |  | SUB(.B or .W) #1,dst |  | Decrement destination | 
DECD(.B or .W) dst | dst-2dst |  | SUB(.B or .W) #2,dst |  | Decrement destination twice | 
INC(.B or .W) dst | dst+1dst |  | ADD(.B or .W) #1,dst |  | Increment destination | 
INCD(.B or .W) dst | dst+2dst |  | ADD(.B or .W) #2,dst |  | Increment destination twice | 
SBC(.B or .W) dst | dst+0FFFFh+Cdst dst+0FFhdst |  | SUBC(.B or .W) #0,dst |  | Subtract source and borrow /.NOT. carry from dest. | 
Emulated Instructions

## Slide 13: Emulated Instructions
Mnemonic | Operation |  | Emulation |  | Description
Logical and register control instructions |  |  |  |  | 
INV(.B or .W) dst | .NOT.dstdst | XOR(.B or .W) #0(FF)FFh,dst |  | Invert bits in destination | 
RLA(.B or .W) dst | CMSBMSB-1 LSB+1LSB0 | ADD(.B or .W) dst,dst |  | Rotate left arithmetically | 
RLC(.B or .W) dst | CMSBMSB-1 LSB+1LSBC | ADDC(.B or .W) dst,dst |  | Rotate left through carry | 
Program flow control |  |  | 
BR dst | dstPC | MOV dst,PC | Branch to destination
DINT | 0GIE | BIC #8,SR | Disable (general) interrupts
EINT | 1GIE | BIS #8,SR | Enable (general) interrupts
NOP | None | MOV R3,R3 | No operation
RET | @SPPC SP+2SP | MOV @SP+,PC | Return from subroutine
Emulated Instructions

## Slide 14: Emulated Instructions
Mnemonic | Operation | Emulation |  | Description
Data instructions |  |  |  | 
CLR(.B or .W) dst | 0dst | MOV(.B or .W) #0,dst | Clear destination | 
CLRC | 0C | BIC #1,SR | Clear carry flag | 
CLRN | 0N | BIC #4,SR | Clear negative flag | 
CLRZ | 0Z | BIC #2,SR | Clear zero flag | 
POP(.B or .W) dst | @SPtemp SP+2SP tempdst | MOV(.B or .W) @SP+,dst | Pop byte/word from stack to destination | 
SETC | 1C | BIS #1,SR | Set carry flag | 
SETN | 1N | BIS #4,SR | Set negative flag | 
SETZ | 1Z | BIS #2,SR | Set zero flag | 
TST(.B or .W) dst | dst + 0FFFFh + 1 dst + 0FFh + 1 | CMP(.B or .W) #0,dst | Test destination | 
Emulated Instructions

## Slide 15: Quiz 6.1 - Pointers
Given the memory contents to the right, what are the values for registers r4 and r5 after each instruction to the left is executed?
0x8100 | 1 | 2
0x8102 | 3 | 4
0x8104 | 5 | 6
0x8106 | 7 | 8
0x8108 | 0x8100 | 
0x810a | 0x8101 | 
0x810c | 0x8102 | 
0x810e | 0x8103 | 
0x8110 | 0x8104 | 
0x8112 | 0x8105 | 
0x8114 | 0x8106 | 
0x8116 | 0x8107 | 
Instructions | r4 | r5
mov.w #tab1,r4 |  | 
mov.b @r4+,r5 |  | 
mov.w #3,r4 |  | 
mov.b tab1(r4),r5 |  | 
mov.w tab2(r4),r5 |  | 
add.w r4,r4 |  | 
mov.w tab2(r4),r5 |  | 
mov.b @r5,r5 |  | 
tab1: .byte 1,2
.byte 3,4
.byte 5,6
.byte 7,8
tab2: .word tab1+0
.word tab1+1
.word tab1+2
.word tab1+3
.word tab1+4
.word tab1+5
.word tab1+6
.word tab1+7
Address
Memory
Assembly

## Slide 16: Assembler

## Slide 17: Assembler
An assembler outputs an object file
An assembly program is a text file containing assembly instructions, directives, macros, and comments
An assembler translates a program into machine code
MSP430 Assembler
An object file is input to a linker program
Notes: 17

## Slide 18: Assembler Coding Format
Label
;*************************************************************************
; CS/ECEn 124 Lab 1 - blinky.asm: Software Toggle P1.0
;
; Description: Toggle P1.0 by xor'ing P1.0 inside of a software loop.
;*************************************************************************
DELAY .equ 0
.cdecls C,"msp430.h" ; MSP430
.text ; beginning of executable code
start: mov.w #0x0400,SP ; init stack pointer
mov.w #WDTPW|WDTHOLD,&WDTCTL ; stop WDT
bis.b #0x01,&P1DIR ; set P1.0 as output
mainloop: xor.b #0x01,&P1OUT ; toggle P1.0
mov.w #DELAY,r15 ; use R15 as delay counter
delayloop: sub.w #1,r15 ; delay over?
jnz delayloop ; n
jmp mainloop ; y, toggle led
.sect ".reset" ; MSP430 RESET Vector
.word start ; start address
.end
Labels start in column 1 and are 10 characters or fewer.
Instructions / DIRECTIVES start in column 12.
Operands start in column 21.
Comments start in column 45.
Use macros provided in the MSP430 header file.
The ".cdecls" directive inserts a header file into your program.
Assembler directives begin with a period (.)
The ".end" directive is the last line of your program.
Instructions are lower case and macros are UPPER CASE.
No line should exceed 80 characters.
Begin writing your assembly code after the ".text" directive.
MSP430 Assembler
Operation
Operands
Comments

## Slide 19: Symbols / Labels
Symbols
  Symbols are name/value pairs and stored in a symbol table.
    A symbol name is a string of up to 200 alphanumeric characters (A-Z, a-z, 0-9, $, and _), cannot contain embedded blanks, is case sensitive, and the first character cannot be a number.
    A symbol value is a label, constant, or substitution value.
  Symbols used as labels become symbolic addresses that are associated with locations in the program.
Labels
  Labels are symbols.
  Labels begins in column 1 and is optionally followed by a colon.
  The value of a label is the current value of the Location Counter (address within program).
  A label on a line by itself is a valid statement.
  Labels used locally within a file must be unique.
Assembly Code

## Slide 20: Mnemonics / Operands
Mnemonic Field
  The mnemonic field cannot start in column 1; if it does, it is interpreted as a label.
  The mnemonic field contains one of the following items:
    MSP430 instruction mnemonic (ie. ADD, MOV, JMP)
    Assembler directive (ie. .data, .list, .equ)
    Macro directive (ie. .macro, .var, .mexit)
    Macro invocation
Operand Field
  The operand field follows the mnemonic field and optionally contains one or more operands.
  An operand may consist of:
    Symbols
    Constants
    Expressions (combination of constants and symbols)
  Operands are separated with commas
Assembly Code
Notes: 20

## Slide 21: Constants / Expressions
Constants are maintained internally as a 32-bit, signed (2’s complement) or unsigned numbers.
  Constants are not sign extended.
  The pound sign precedes a constant in an instruction
    Decimal: decimal digits ranging from -2147483648 to 4294967295 (ie, 1000, -32768)
    Hexadecimal: up to 8 hexadecimal digits followed by ‘H’ (or ‘h’) or preceded by ‘0x’ (ie, 78h, 0x78)
    Binary: up to 32 binary digits followed by suffix B (or b) (ie. 0000b, 11110000B)
An expression is a constant, a symbol, or a series of constants and symbols separated by arithmetic operators that evaluates to a single 32-bit number.
    -2147483648 to 2147483647 for signed values
    0 to 4294967295 for unsigned values
Assembly Code
Notes: 21

## Slide 22: Expressions / Operators
The precedence order of expression evaluation is
  Evaluate parenthesized expressions
  Evaluate operators according to precedence groups
  When parentheses and precedence groups do not determine the order of expression evaluation, the expressions are evaluated from left to right
Assembly Code
Group Operator Description
1 +, -, ~, ! Unary plus, minus, 1’s complement, logical NOT
2 *, /, % Multiplication, Division, Modulo
3 +, - Addition, Subtraction
4 <<, >> Shift left, Shift right
5 <, <=, >, >= Less than, Less than or equal to, Greater than, Greater than
or Equal to
6 =[=], != Equal to, Not equal to
7 & Bitwise AND
8 ^ Bitwise exclusive OR (XOR)
9 | Bitwise OR
Notes: 22

## Slide 23: Assembler Directives
Assembly directives are used to:
  Create symbol table entries (.equ, .set, .cdecls).
  Select assembler sections (.sect, .bss, .text).
  Define values for memory locations (.byte, .word, .string).
  Specify the end of program (.end).
;*******************************************************************************
; CS/ECEn 124 Example Code
;*******************************************************************************
.cdecls C,"msp430x22x4.h" ; include C header
COUNT .equ 2000
;------------------------------------------------------------------------------
.bss cnt,2 ; ISR counter
;------------------------------------------------------------------------------
.text ; Program reset
start: mov.w #0x0400,SP ; Initialize stack pointer
mov.w #WDT_MDLY_0_5,&WDTCTL ; Set Watchdog interval to ~0.5ms
bis.w #LPM0+GIE,SR ; Enter LPM0 w/ interrupt
jmp $ ; Loop forever; interrupts do all
.sect ".reset" ; MSP430 RESET Vector
.word start ; Power Up ISR
.end
Directives
Assembly Code
Current Location Counter

## Slide 24: Assembly Style Guidelines
  Provide a program header, with author’s name, date, etc., and purpose of program.
  Start labels, opcode, operands, and comments in same column for each line. (Unless entire line is a comment.)
  Use comments to explain what each register does.
  Remember, the assembler is case sensitive.
  Use meaningful symbolic names.
    Mixed upper and lower case for readability.
    ASCIItoBinary, InputRoutine, SaveR1
  Provide comments between program sections.
  Each line must fit on the page -- no wraparound or truncations.
    Long statements split in aesthetically pleasing manner.
Assembly Code

## Slide 25: Quiz 6.2
What is an expression?
What is the difference between a symbol and a label?
Can the name “add” be used as a label?
What is the difference between a directive and a mnemonic?

## Slide 26: Assembler Sections

## Slide 27: Assembler Sections
A section is a block of code or data that occupies contiguous space in the memory map.
Each section has its own Location Counter.
The assembler assembles into the current section.
Assembler Sections
There are two types of sections:
  Initialized sections containing data or code (modal)
    .sect
    .text
  Uninitialized sections reserving space in the memory map for uninitialized data (temporary)
    .bss
    .usect
Object File |  | Target Memory
.bss var,2 |  | RAM
.usect "mySection" |  | 
.text |  | 
 |  | ROM (Flash)
.sect "reset" |  | 

## Slide 28: Location Counter
The Location Counter holds the relative memory position of an instruction within the current section.
  Each section has a location counter used to assign storage addresses to your program's statements.
  As the instructions of a source module are being assembled, the location counter keeps track of the current location in storage.
  A $ (dollar sign) can be used as an operand to an instruction to refer to the current value of the location counter.
The assembler assembles into the current section.
  An initialized section directive instructs the assembler to stop assembling in the current section and begin assembling in the indicated section.
  An uninitialized section directive does not end the current section, but simply escape from the current section temporarily. (Thus uninitialized directives .bss and .usect can appear anywhere in an initialized section without affecting its contents.)
Assembler Sections

## Slide 29: Quiz 6.3
 | .cdecls C,"msp430.h" ; include c header
 | .bss cnt,2 ; WDT second counter
 | .bss cat,4
 | .text ; program section
 | start: mov.w #0x0400,SP ; set stack pointer
 | mov.w #0x5a18,&WDTCTL ; set WD timer interval
 | mov.w #0x00fa,&cnt ; 1 sec WD counter
 | mov.b #0x01,&IE1 ; enable WDT interrupt
 | bis.b #0x01,&P1DIR ; P1.0 output
 | bis.w #0x0018,SR ; enable interrupts
 | .bss dog,2
 | wdt_isr: xor.b #0x01,&P1OUT ; toggle P1.0
 | reti ; return from interrupt
 | .sect ".int10" ; WDT vector section
 | .word wdt_isr ; Watchdog ISR
 | .sect ".reset" ; PUC vector section
 | .word start ; RESET ISR
 | .end
List the Location Counter values for the following:

## Slide 30: Assembly Process
The assembler translates 1-to-1 assembly language instructions (.asm) into the machine language of the ISA (.obj)
  1st Pass: store all labels/constants and their corresponding addresses/values in the symbol table
    Zero all Location Counters ($)
    For each non-empty line in the .text section:
      if line contains a label, add label and current LC to the symbol table
      if line contains an instruction, increment the LC accordingly
    Stop when .end directive is found.
  2nd Pass: convert instructions to machine language, using information from symbol table
    Find the .text assembly directive and zero all Location Counters ($)
    For each executable assembly language statement:
      generate the corresponding machine language instruction
      resolve labels referenced in instructions using the symbol table
      increment LC for each instruction as in pass 1
      output resulting machine code and program listing to output files
    Stop when .end directive is found.
Assembly Process

## Slide 31: Common Assembler Directives
Mnemonic and Syntax | Description
.bss symbol, size in bytes[, alignment] | Reserves size bytes in the .bss (uninitialized data) section
.sect "section name" | Assembles into a named (initialized) section
.text | Assembles into the .text (executable code) section
.byte value1[, ..., valuen] | Initializes one or more successive bytes in the current section
.string "string1"[, ..., "stringn"] | Initializes one or more text strings
.word value1[, ... , valuen] | Initializes one or more 16-bit integers
.align [size in bytes] | Aligns the LC on a boundary specified by size in bytes; must be a power of 2; defaults to word (2 byte)
.def symbol1[, ... , symboln] | Identifies one or more symbols that are defined in current module and that can be used in other modules
.include ["]filename["] | Includes source statements from another file
.ref symbol1[, ... , symboln] | Identifies one or more symbols used in the current module that are defined in another module
symbol .equ value | Equates value with symbol
symbol .set value | Equates value with symbol
.cdecls [options,] "filename" | Share C headers between C and assembly code
.end | Ends program
Assembler Directives
Fills (initializes) bytes
in CURRENT section
(Does NOT change section)
Creates Name/Value
symbol table entry
(Does NOT effect any
section Location Counter)
Changes to new section
(New Location Counter)
Reserves uninitialized
bytes in RAM section
(Does NOT change
current section)

## Slide 32: Linker
The Linker program "links" two files together according to their declared sections:
Linker

## Slide 33: Library Routines
Library
  A set of routines for a specific domain application.
  Example: math, graphics, GUI, etc.
  Use the .ref directive to reference symbols defined outside a program.
Library routine invocation
  Labels for the routines are defined as .def
  Each library routine contains its own symbol table.
  A linker resolves the external addresses before creating the executable image.
  Reports and unresolved symbols.
Libraries

## Slide 34: Linking Multiple Files
.ref myFunc
.ref sqrt
.text
…
call #myFunc
call #sqrt
…
.end
Source Module A
Module A
Object
Symbol Table
Assembler
.def myFunc
.text
myFunc:
…
ret
.end
Source Module B
Module B
Object
Symbol Table
Assembler
Module B
Object
Math
Library
Symbol Table
Math
Library
Module A
Object
Executable Image
Linker
Libraries

## Slide 35: Quiz 6.4
Create assembler and linker symbol table values for the following program: (Note: the linker loads the .text section at memory address 0xc000.)
DELAY .equ 0
.text
reset: mov.w #0x0400,SP
mov.w #0x5a80,&0x0120
bis.b #0x01,&0x0022
mloop: xor.b #0x01,&0x0021
mov.w #DELAY,r15
dloop: dec.w r15
jnz dloop
dlp2: dec.w r15
jnz dlp2
jmp mloop
.sect ".reset"
.word reset
.end
Symbol Name | Assembler Symbol Value | Resolved Linker Value

## Slide 36: How to Code Assembler

## Slide 37: How To Code Assembler…
Understand the problem (obviously)
Until you are comfortable in assembly, (and even afterwards), write out your solution in something familiar
  English
  Flowchart
  Pseudo-code
  Java, C, Ruby – the pseudo-code doesn’t really matter!
Then, translate to assembler
Coding Assembler

## Slide 38: Three Basic Constructs
Coding Assembler

## Slide 39: if-then-else
if-then-else
if (buzzerON == 1)
{
pulse_buzzer();
turn_on_LED();
}
else
{
turn_off_LED();
}
cmp.w #1,buzzerON ;
jne myElse ;
xor.b #0x20,&P4OUT ;
bis.b #0x02,&P1OUT ;
jmp myNext ;
myElse: ;
bic.b #0x02,&P1OUT ;
;
myNext: ;
Coding Assembler

## Slide 40: switch / case
switch / case
switch (myByte)
{
case DOT:
do_dot();
break;
case DASH:
do_dash();
break;
default:
}
cmp.w #DOT,myByte ;
jne sw_01 ;
call #do_dot ;
jmp sw_end ;
sw_01:
cmp.w #DASH,myByte ;
jne default ;
call #do_dash ;
jmp sw_end ;
;
default: ;
sw_end: ;
Coding Assembler

## Slide 41: for-loop
for-loop
int i;
for(i=0; i<10; i++)
{
do_dot();
delay();
do_dash();
delay();
}
.bss i,2 ;
mov.w #0,i ;
for_ck: cmp.w #10,i ;
jge for_done ;
call #do_dot ;
call #delay ;
call #do_dash ;
call #delay ;
add.w #1,i ;
jmp for_ck ;
for_done: ;
Coding Assembler

## Slide 42: while
while loop…
#define TRUE 1
int blink = TRUE;
while (blink)
{
LED_ON();
delay();
LED_OFF();
delay();
}
TRUE .equ 1
.bss blink,2 ;
mov.w #TRUE,blink ;
while_loop: ;
cmp.w #0,blink ;
jeq while_done ;
call #LED_ON ;
call #delay ;
call #LED_OFF ;
call #delay ;
jmp while_loop ;
while_done: ;
Coding Assembler

## Slide 43: Quiz 6.5
Code the following C program in assembler:
int i;
void func1(void) { ++i; return; }
void func2(void) { i += 2; return; }
void main(void)
{
for (i = 1; i < 10; i++)
{
if (i < 5)
{
func1();
}
else
{
func2();
}
}
}

## Slide 44: Systematic Decomposition
Finiteness
  Must terminate.
Definiteness
  Each step is precisely stated.
Effective Computability
  Each step can be carried out.
IDEA
Step by Step Procedure
Systematic Decomposition

## Slide 45: Stepwise Refinement
Also known as systematic decomposition.
Start with problem statement:
  “Write an assembler program to play the game of Simon using the LEDs and push button switches.”
Decompose task into a few simpler subtasks.
Decompose each subtask into smaller subtasks, and these into even smaller subtasks, etc.... until you get to the machine instruction level.
Incrementally develop program and test, test, test…
Systematic Decomposition

## Slide 46: Problem Statement
Because problem statements are written in English, they are sometimes ambiguous and/or incomplete.
  How is the game played? How many LEDs start the game? Which switches and which LEDs? How long is an LED on or off? What happens when an error is made? What happens when a sequence is successfully reproduced? How is a new sequence started? …
How do you resolve these issues?
  Ask the person who wants the problem solved, or
  Make a decision and document it.
Systematic Decomposition

## Slide 47: Simon Example
Systematic Decomposition
“Play the game of Simon using the LEDs and push button switches.”
Problem
Setup new game.
Output random sequence of tones and LEDs.
Reset sequence.
Get and compare player’s response.
Output results and restart game w/new sequence.
Init Simon board.
Algorithm
start:
call #init_board
newGame:
call #new_game
call #saveRandSeed
mov.b #0xff,&success
mov.w #TRYS-1,&trys
tryLoop:
tst.b &success
jeq newGame
inc.w &trys
test:
mov.w #0,r15
testLoop:
cmp.w r15,&trys
jge player
call #getRand
and.w #0x0003,r12
call #doLEDsTone
inc.w r15
jmp testLoop:
player:
call #restoreRandSeed
...
Incremental Development
while (1)
{ new_game:
{ saveRandSeed;
success = TRUE;
trys = TRYS-1;
}
while(success)
{ doSequence:
{ restoreRandSeed;
trys++;
for (i=0; i<trys; i++)
{ getRand;
doLEDsTone;
}
}
doPlayer:
{ restoreRandSeed;
for (i=0; i<trys; i++)
{ getSwitch;
doLEDsTone;
if (getRand  switch)
{ success = FALSE;
break;
}
}
}
doResults:
{ if (success) outSuccess;
else outRaspberry;
}
}
}
Pseudo-code

## Slide 49: Energy Consumption

## Slide 50: U.S. Energy Consumption
The United States is the 2nd largest energy consumer in terms of total use in 20101 in the world.
Not getting better – everyone must do their part.
How could I lower home energy consumption?
  Turn off lights
  Turn down thermostat
  Unplug appliances not in use
  Use slower motor speeds
  Heat/cool at a slower rate
  Improve insulation
  Purchase energy efficient appliances
  Eliminate unnecessary living space
How could I make computers more energy efficient?
1. Barr, Robert. "China surpasses US as top energy consumer". Associated Press. Retrieved 16 June 2012.
Energy Consumption
Notes: 1. Barr, Robert. "China surpasses US as top energy consumer". Associated Press. http://www.msnbc.msn.com/id/43327793/ns/business-oil_and_energy/t/china-surpasses-us-top-energy-consumer/#.T9y6aBSYNok. Retrieved 16 June 2012.

## Slide 51: Computer Energy Consumption
Computers occupy a small but growing percentage of annual U.S. electricity consumption.
  Estimates vary for 3% to 13% of entire U.S. supply.
  Hidden costs – every 100 watts consumed by computers requires 50 watts of cooling.
  Computers are ubiquitous – found in every energy sector.
Battery capacity doubles every 10 years while processing power doubles every 2 years.
Server farms, supercomputers, web hosting, scientific simulations, 3D rendering, search engines,…
  Google uses enough energy to continuously power 200,000 homes (260 million watts – ¼ output of a nuclear power plant).
  One Google search is equal to turning on a 60W light bulb for 17 seconds.
Energy Consumption
  http://techland.time.com/2011/09/09/6-things-youd-never-guess-about-googles-energy-use/
Notes:   http://techland.time.com/2011/09/09/6-things-youd-never-guess-about-googles-energy-use/
  Read more: http://techland.time.com/2011/09/09/6-things-youd-never-guess-about-googles-energy-use/#ixzz2MDRvGfYe

## Slide 52: Clocks

## Slide 53: Processor Clock Speeds
Often, the most important factor for reducing power consumption is slowing the clock down.
  Faster clock = Higher performance, more power required
  Slower clock = Lower performance, less power required
Processor Clocks
; Set ACLK to 12kHz
mov.w #LFXT1S_2,&BCSCTL3
; Set DCO to 8 MHz:
mov.b #CALBC1_8MHZ,&BCSCTL1
mov.b #CALDCO_8MHZ,&DCOCTL
Chart: Clock Speeds ()
| 0.25 | 0.18 | 0.13 | 0.09 | 0.065
Leakage | 5 | 10 | 30 | 60 | 142
Active Power | 35 | 45 | 60 | 80 | 100
10% loss of power
60% loss of power

## Slide 54: Example 6.1 – Clock Speed
.cdecls C,"msp430.h"
SMCLK .equ 1200000 ; 1.2 Mhz clock
WDT_CPS .equ SMCLK/8000 ; WDT clocks / second count
MHz8 .set 1 ; 8 MHz flag
; Code Section ------------------------------------------------------------
.text
start: mov.w #0x0400,SP ; init stack pointer
mov.w #WDT_MDLY_8,&WDTCTL ; stop WDT
.if MHz8 ; set DCO to 8 MHz
mov.b #CALBC1_8MHZ,&BCSCTL1 ; set range
mov.b #CALDCO_8MHZ,&DCOCTL ; set DCO step + modulation
.endif
bis.b #0x01,&P1DIR ; set P1.0 as output
mainloop: xor.b #0x01,&P1OUT ; toggle P1.0
mov.w #8,r14 ; use R14 as outer loop counter
delaylp1: mov.w #0,r15 ; use R15 as delay counter
delaylp2: sub.w #1,r15 ; delay over?
jne delaylp2 ; n
sub.w #1,r14 ; y, outer loop done?
jne delaylp1 ; n
jmp mainloop ; y, toggle led
; Interrupt Vectors -------------------------------------------------------
.sect ".reset" ; MSP430 RESET Vector
.word start ; start address
.end
Interrupts
Conditionally assemble setting new DCO constants (for 8 MHz)
Nested delay loop to blink LED

## Slide 56: Low-Power Mode

## Slide 57: MSP430 Clock Modes
Another method to reduce power consumption is to turn off some (or all) of the system clocks.
A device is said to be sleeping when in low-power mode; waking refers to returning to active mode.
Low Power Modes
“Only Mostly Dead”
(7 Years vs 1 Day)
Average
300x Savings
(1 Year vs 1 Day)

## Slide 58
Reserved | V | SCG1 | SCG0 | OSC OFF | CPU OFF | GIE | N | Z | C
Active Mode LPM0 LPM3 LPM4 |  | 0 0 1 1 | 0 0 1 1 | 0 0 0 1 | 0 1 1 1 | ~ 250 µA ~ 35 µA ~ 0.8 µA ~ 0.1 µA |  |  | 
; enable interrupts / enter low-power mode 0
bis.w #LPM0|GIE,SR ; LPM0 w/interrupts
MSP430 Clock Settings (r2)
Low Power Modes
SMCLK and ACLK Active
Sleep Modes
Only ACLK Active
No Clocks!
Can be combined

## Slide 59: Example 6.2 – Low Power
.cdecls C,"msp430.h"
SMCLK .equ 1200000 ; 1.2 Mhz clock
WDT_CPS .equ SMCLK/8000 ; WDT clocks / second count
STACK .equ 0x0400 ; top of stack
; Data Section ------------------------------------------------------------
.bss WDTSecCnt,2 ; WDT second counter
; Code Section ------------------------------------------------------------
.text
start: mov.w #STACK,SP ; initialize stack pointer
mov.w #WDT_MDLY_8,&WDTCTL ; set WD timer interval
mov.w #WDT_CPS,&WDTSecCnt ; initialize 1 sec WD counter
bis.b #WDTIE,&IE1 ; enable WDT interrupt
bis.b #0x01,&P1DIR ; P1.0 output
loop: bis.w #LPM0|GIE,SR ; sleep/enable interrupts
xor.b #0x01,&P1OUT ; toggle P1.0
jmp loop ; loop indefinitely
; Watchdog ISR ------------------------------------------------------------
WDT_ISR: sub.w #1,&WDTSecCnt ; decrement counter, 0?
jne WDT_02 ; n
mov.w #WDT_CPS,&WDTSecCnt ; y, re-initialize counter
bic.b #LPM0,0(SP) ; wakeup processor
WDT_02: reti ; return from interrupt
; Interrupt Vectors -------------------------------------------------------
.sect ".int10" ; Watchdog Vector
.word WDT_ISR ; Watchdog ISR
.sect ".reset" ; PUC Vector
.word start ; RESET ISR
.end
Low-Power Mode
Enable interrupts / Goto Sleep
(Low-power Mode 0)
4. Blink LED when awakened
5. Reset counter every second
6. Set Active Mode in saved SR
7. Wakeup processor on RETI
300µA
1µA
active
Activity Profile
sleep
average
Configure Watchdog as a timer
Enable device to interrupt

## Slide 60: Lower Power Savings
Finally, powering your system with lower voltages means lower power consumption as well.
Low Power Modes
P=CV2F
where
P=power consumption
C=load capacitance
V=operating voltage
F=frequency.

## Slide 61: Principles of Low-Power Apps
Maximize the time in low-power modes.
Sleep as long as possible and use interrupts to wakeup.
Use the slowest clock while still meeting processing needs.
Switch on peripherals only when needed (ie, switch off peripherals when not needed).
Use low-power integrated computer peripherals.
  Timers: Timer_A and Timer_B for PWM
  A/D convertors, flash, LCD’s
Use faster software algorithms / programming techniques
  Calculated branches instead of flag polling.
  Fast table look-ups instead of iterative calculations.
  Use in-line code instead of frequent subroutine / function calls.
  More single-cycle CPU register usage.
Low Power Modes

## Slide 62: Switches

## Slide 63: Switches
Switches
  Port 1, bits 0-3
  Use internal pull-ups
  Use interrupts
  H to L transition
Require debouncing
Switch Debounce
bic.b #0x0f,&P1DIR ; set P1.0-3 as inputs
bis.b #0x0f,&P1OUT ; use pull-ups
bis.b #0x0f,&P1REN ; enable pull-ups
bis.b #0x0f,&P1IES ; high to low transition
bis.b #0x0f,&P1IE ; enable interrupts

## Slide 64: Switch Debounce
Switch Debounce
Switch "debounced" after signal remains low for specified time
2.4
3.3
0.5
0.0
Logic "Low"
Logic "High"
Switch Pressed
Switch Released
Undefined

## Slide 65: Example 6.3 Switch Debounce
.cdecls C,"msp430.h"
.bss WDT_dcnt,2 ; WDT second counter
.bss switches,2 ; switches
.text
RESET: mov.w #0x0600,SP ; init stack pointer
mov.w #WDT_MDLY_8,&WDTCTL ; WDT SMCLK, 8 ms (@1 Mhz)
bis.b #WDTIE,&IE1 ; enable WDT interrupt
clr.w WDT_dcnt ; clear debounce counter
bis.b #0x0f,&P4DIR ; set P4.0-3 as outputs
bic.b #0x0f,&P1DIR ; set P1.0-3 as inputs
bis.b #0x0f,&P1OUT ; pull-up
bis.b #0x0f,&P1REN ; enable pull-ups
bis.b #0x0f,&P1IES ; high to low transition
bis.b #0x0f,&P1IE ; enable interrupts
mainloop: bis.w #LPM0|GIE,SR ; enable interrupts/goto sleep
xor.b switches,&P4OUT ; output (toggle) P4.0-3
jmp mainloop
; Port 1 ISR --------------------------------------------------------------
DEBOUNCE .equ 5 ; debounce count (~40 ms)
P1_ISR: bic.b #0x0f,&P1IFG ; put its hand down
mov.w #DEBOUNCE,WDT_dcnt ; reset debounce counter
reti
; Watchdog ISR ------------------------------------------------------------
WDT_ISR: cmp.w #0,WDT_dcnt ; debouncing?
jeq WDT_02 ; n
sub.w #1,WDT_dcnt ; y, decrement counter, 0?
jne WDT_02 ; n
mov.b &P1IN,switches ; y, read switches
xor.b #0x0f,switches ; positive assertion
and.b #0x0f,switches ; mask low 4 bits (switches)
bic.b #LPM0,0(SP) ; wake up
WDT_02: reti ; return from interrupt
.sect ".int02"
.word P1_ISR ; Port 1 ISR
.sect ".int10
.word WDT_ISR ; Watchdog ISR
.sect ".reset"
.word RESET ; RESET ISR
.end
Watchdog ISR
Decrement WDT_cnt (if non-zero), read switch and wakeup main routine.
Switch Debounce
Port 1 interrupt vector
Port 1 ISR
Reset debounce counter
Configure Switches:
High to Low
Pull-ups
Enable interrupts

## Slide 66: LED’s

## Slide 67: LEDs
A light-emitting diode (LED) is a semiconductor light source
When a diode is forward biased (switched on), electrons are able to recombine with holes within the device, releasing energy in the form of photons
Device: LED

## Slide 68: LEDs
LaunchPad Development Tool (MSP430G2553)
  P1.0 Red LED
  P1.6 Green LED
RBX430 Development board (MSP430F2274)
  P3.4 Green LED (LED5)
  P4.0-3 Green, Orange, Yellow, Red LEDs (LED1-4)
  P4.6 Red LED (LED6)
Example
  bis.b #0x0f,&P4DIR ; P4.0-3 output
  bic.b #0x0f,&P4OUT ; turn off all LEDs
  bis.b #0x03,&P4OUT ; turn on #3 & #4
  xor.b #0x0f,&P4OUT ; toggle 1-2, 3-4 LEDs
Device: LED

## Slide 69: Quiz 6.6
What does the following assembly code do?
.cdecls c,"msp430.h"
.text
start: mov.w #0x0400,SP
mov.w #0x5a80,&WDTCTL
bis.b #0x0f,&P4DIR
bic.b #0x0f,&P4OUT
mov.w #0,r15
mloop: mov.b #0x08,r4
dloop: sub.w #1,r15
jne dloop
xor.b r4,&P4OUT
rrc.b r4
jnc dloop
jmp mloop
.sect ".reset"
.word start
.end