## Slide 1
ECE382
Lesson 30
1

## Slide 2: Overview
Lesson Outline
  Pulse Width Modulation (PWM)
  Capture and Compare

## Slide 3: Lesson Outcomes
Advantages/disadvantages of digital signals
Understand the following parameters and impacts in ADC systems:
  Sampling rate, voltage range, bits, and resolution
Understand the 3 steps of ADC process
Understand the 3 common ADC errors
Understand how to use the ADC on the MSP430

## Slide 4: BLUF
3 steps in the Analog to Digital Conversion (ADC) Process:
  Sample (snapshot in time)
  Quantize (assign voltage level)
  Encode (convert to bits)
Sampling (time) and Resolution (voltage) are independent

## Slide 5: More BLUF
3 errors in the Analog to Digital Conversion (ADC) Process:
  Aliasing (due to inadequate sampling rate)
  Clipping (voltage exceeds input range of ADC)
  Quantization error (inherent – can only be minimized)

## Slide 6: Digital vs Analog
What’s the difference?
What are the advantages?
Disadvantages?

## Slide 7: Analog vs Digital
Analog
Information represented by a continuously variable physical quantity
No discontinuities in time or amplitude
Digital
Information represented by discrete valued variables
Time axis is sampled
Amplitude axis is quantized

## Slide 8: Digital Signals
Advantages
Noise resistant
Easy to store and recover data
Easy to encrypt and process data
Disadvantages
Lost data (important?)
Sampling errors may exist – aliasing
Quantization errors always exist

## Slide 9: ADC
How does Analog to Digital Conversion Happen?
Sampling: Snapshots at discrete times (Nyquist rate)(x-axis)
Quantization: Round to discrete voltage levels (resolution)(y-axis)
Encoding: convert decimal levels to binary (convert to bits)
D
Analog
Digital
Sampling
Resolution
Encode in 5 bits: 10011
What does the computer assume between samples?

## Slide 10: Key Definitions
Sampling:
  Taking measurements of a continuous time signal at discrete time instances
  Time axis
Quantization
  Assigning sampled measurements values from a discrete set of allowable values
  Amplitude axis
Encoding
  Convert a quantized measurement to a binary string

## Slide 11
How does Analog to Digital Conversion Happen?
Sampling: Snapshots at discrete times
Quantization: Round to discrete voltage levels
Encoding: convert decimal levels to binary

## Slide 12: Sampling
What is your class score right now?
  At Prog?
  At Final?
An example sampling rate could be every 5 lessons

## Slide 13: Quantize into discrete grade levels

## Slide 14: Encoding Grade Levels into decimal

## Slide 15
ADC – The device
3 Steps of the
ADC Process?

## Slide 16
Analog Signal

## Slide 17
1) Sample at uniform intervals
Capture Voltages at
Sampled “snapshots”
Ts
2Ts
3Ts
Ts = 1/fs
Potential Error:
Changes between samples
0

## Slide 18
2) Quantize into discrete voltage levels
0
1
2
3
4
5
6
7
Introduces
Quantization
Error

## Slide 19
0
1
2
3
4
5
6
7
110
111
111
110
101
011
001
000
001
010
011
3) Encode Levels as Binary

## Slide 20: Reconstruction from bits

## Slide 21
DAC Output = Digital!
0V
5V

## Slide 22: Reform smooth signal

## Slide 23: Compare

## Slide 24
ADC – The device

## Slide 25: Quantization Definitions
Vmax: Largest input that can be correctly converted
Vmin: Smallest input that can be correctly converted
b: Number of binary bits that will be used to encode data
Quantization levels: 2b
Resolution: Smallest signal change that can be measured by A/D conversion
Important Note: Quantization (y-axis) and sampling (x-axis) are independent processes

## Slide 27: Sampling frequency trade-offs
Sample too slow
  Aliasing
Sample too fast???
  Hardware limitations
    max sampling rate of Real-time signal
    Available memory
    More processor time
    More storage space

## Slide 28: Nyquist (Sampling)
Nyquist frequency:
fs >= 2fhigh
Where fhigh is the highest frequency being sampled
fs=5N
fs=N
fs=2/3N
fs=.54N
fs=1/2N
fs=1/3N
fs=1/5N
Look closely, the wheel appears to be moving in reverse … the camera isn’t capturing fast enough to record the motion correctly!

## Slide 29: Aliasing Examples
https://www.youtube.com/watch?v=CaiIZI1oe40
https://www.youtube.com/watch?v=smDpCsVVgPA

## Slide 30: Aliasing
Sampling exactly in step with blade rotation
Car wheels going backward on TV
Must sample “fast enough” to avoid this

## Slide 31
Nyquist Sampling Rate fN = 2 * fhigh
To avoid aliasing
fsample > 2 * fhigh
http://www.kostic.niu.edu/aliasing-movie.gif

## Slide 32
Quantize into discrete voltage levels
0
1
2
3
4
5
6
7
Introduces
Quantization
Error
VMIN
VMAX

## Slide 33: Key Points
Resolution is determined by the Analog to Digital Converter (ADC) not the input signal
Smaller resolution is generally better
Resolution units are volts/level
Quantization throws away data and therefore induces error
  Max quantization error is equal to resolution
Quantization “Clips” any values outside Vmin & Vmax
  How can we avoid clipping? Transducer interface

## Slide 34: Resolution Tradeoff Example

## Slide 35: Smaller Resolution = More Details

## Slide 36
Given: vin(t) = 4 + 4 cos (360◦ 2k t) V, or better
Find: Appropriate ADC Parameters and resultant QEMAX
Notes: Time between samples: 100 usec
1st sample: 500 mV
2nd sample: -154.5 mV
Resolution = 250 mV/level
EL1 = 6
EL2 = 3.382
QL1 = 6  Binary output = 110
QL2 = 3  Binary output = 011

## Slide 37
Given: vin(t) = 50 cos (360◦ 3k t) mV What are the issues here? How would you fix it?
Notes: Time between samples: 100 usec
1st sample: 500 mV
2nd sample: -154.5 mV
Resolution = 250 mV/level
EL1 = 6
EL2 = 3.382
QL1 = 6  Binary output = 110
QL2 = 3  Binary output = 011

## Slide 38
Given: vin(t) = 50 cos (360◦ 3k t) mV What are the issues here? How would you fix it?
Notes: Time between samples: 100 usec
1st sample: 500 mV
2nd sample: -154.5 mV
Resolution = 250 mV/level
EL1 = 6
EL2 = 3.382
QL1 = 6  Binary output = 110
QL2 = 3  Binary output = 011

## Slide 39: Analog to Digi Errors??
Notes: Name 3 types of errors (aliasing, clipping, and Q.E.)

## Slide 40: Analog to Digi Errors??
3 errors in the Analog to Digital Conversion (ADC) Process:
  Aliasing (due to inadequate sampling rate)
  Clipping (voltage exceeds input range of ADC)
  Quantization error (inherent – can only be minimized)

## Slide 41: Signal Conditioning
How do you prevent aliasing when using ADC?
  Anti-Aliasing filter!
How can we minimize Q.E.? Prevent Clipping?
  Fit the signal to the window
True or False?
  Quantization error can be eliminated

## Slide 42: Anti-Aliasing filter to the rescue!
Given: vin(t) = 50 cos (360◦ 3k t) mV How to prevent aliasing???
Notes: Time between samples: 100 usec
1st sample: 500 mV
2nd sample: -154.5 mV
Resolution = 250 mV/level
EL1 = 6
EL2 = 3.382
QL1 = 6  Binary output = 110
QL2 = 3  Binary output = 011

## Slide 43: Lesson 36 TI Example code
// TI example code
#include <msp430g2553.h>
void main(void)
{
WDTCTL = WDTPW + WDTHOLD; // Stop WDT
ADC10CTL0 = ADC10SHT_3 + ADC10ON + ADC10IE; // ADC10ON, interrupt enabled
ADC10CTL1 = INCH_4; // input A4
ADC10AE0 |= BIT4; // P1.4 ADC Analog enable
ADC10CTL1 |= ADC10SSEL1|ADC10SSEL0; // Select SMCLK
P1DIR |= 0x01; // Set P1.0 to output direction
while (1)
{
ADC10CTL0 |= ENC + ADC10SC; // Sampling and conversion start
__bis_SR_register(CPUOFF + GIE); // LPM0, ADC10_ISR will force exit
if (ADC10MEM < 0x1FF)
P1OUT &= ~0x01; // Clear P1.0 LED off
else
P1OUT |= 0x01; // Set P1.0 LED on
}
}
// ADC10 interrupt service routine
#pragma vector=ADC10_VECTOR
__interrupt void ADC10_ISR(void)
{
__bic_SR_register_on_exit(CPUOFF); // Clear CPUOFF bit from 0(SR)
}
Setup
Sample, Quantize, and Encode
Read Encoded Value

## Slide 44: ADC10CTL0 Register
ADC10CTL0 = ADC10SHT_3 + ADC10ON + ADC10IE; // ADC10ON, interrupt enabled
ADC10CTL1 = INCH_4; // input A4
ADC10AE0 |= BIT4; // P1.4 ADC Analog enable
ADC10CTL1 |= ADC10SSEL1|ADC10SSEL0; // Select SMCLK
P1DIR |= 0x01; // Set P1.0 to output direction

## Slide 45: ADC10CTL0 Register Cont.

## Slide 46: ADC10CTL1 Register
ADC10CTL0 = ADC10SHT_3 + ADC10ON + ADC10IE; // ADC10ON, interrupt enabled
ADC10CTL1 = INCH_4; // input A4
ADC10AE0 |= BIT4; // P1.4 ADC Analog enable
ADC10CTL1 |= ADC10SSEL1|ADC10SSEL0; // Select SMCLK
P1DIR |= 0x01; // Set P1.0 to output direction

## Slide 47: ADC10CTL1 Register Cont.
Note:
Port 1: analog muxed
Port 2: timer muxed

## Slide 48: ADC10AE0 Register
ADC10CTL0 = ADC10SHT_3 + ADC10ON + ADC10IE; // ADC10ON, interrupt enabled
ADC10CTL1 = INCH_4; // input A4
ADC10AE0 |= BIT4; // P1.4 ADC Analog enable
ADC10CTL1 |= ADC10SSEL1|ADC10SSEL0; // Select SMCLK
P1DIR |= 0x01; // Set P1.0 to output direction

## Slide 49: ADC10CTL1 Register
ADC10CTL0 = ADC10SHT_3 + ADC10ON + ADC10IE; // ADC10ON, interrupt enabled
ADC10CTL1 = INCH_4; // input A4
ADC10AE0 |= BIT4; // P1.4 ADC Analog enable
ADC10CTL1 |= ADC10SSEL1|ADC10SSEL0; // Select SMCLK
P1DIR |= 0x01; // Set P1.0 to output direction

## Slide 50: While Loop (Sample, Quantize, & Encode)
while (1)
{
ADC10CTL0 |= ENC + ADC10SC; // Sampling and conversion start
__bis_SR_register(CPUOFF + GIE); // LPM0, ADC10_ISR will force exit
if (ADC10MEM < 0x1FF)
P1OUT &= ~0x01; // Clear P1.0 LED off
else
P1OUT |= 0x01; // Set P1.0 LED on
}
}
// ADC10 interrupt service routine
#pragma vector=ADC10_VECTOR
__interrupt void ADC10_ISR(void)
{
__bic_SR_register_on_exit(CPUOFF); // Clear CPUOFF bit from 0(SR)
}

## Slide 51: ADC10 Block Diagram

## Slide 52: Successive-approximation-register(SAR)
https://www.maximintegrated.com/en/app-notes/index.mvp/id/1080
As the name implies, the SAR ADC basically implements a binary search algorithm. Therefore, while the internal circuitry may be running at several megahertz (MHz), the ADC sample rate is a fraction of that number due to the successive-approximation algorithm.

## Slide 53: While Loop (Disable CPU for Low Power)
while (1)
{
ADC10CTL0 |= ENC + ADC10SC; // Sampling and conversion start
__bis_SR_register(CPUOFF + GIE); // LPM0, ADC10_ISR will force exit
if (ADC10MEM < 0x1FF)
P1OUT &= ~0x01; // Clear P1.0 LED off
else
P1OUT |= 0x01; // Set P1.0 LED on
}
}
// ADC10 interrupt service routine
#pragma vector=ADC10_VECTOR
__interrupt void ADC10_ISR(void)
{
__bic_SR_register_on_exit(CPUOFF); // Clear CPUOFF bit from 0(SR)
}
How many bits?
What is the max value?
10b
0x3FF

## Slide 54: While Loop (Read Encoded Input Memory)
while (1)
{
ADC10CTL0 |= ENC + ADC10SC; // Sampling and conversion start
__bis_SR_register(CPUOFF + GIE); // LPM0, ADC10_ISR will force exit
if (ADC10MEM < 0x1FF)
P1OUT &= ~0x01; // Clear P1.0 LED off
else
P1OUT |= 0x01; // Set P1.0 LED on
}
}
// ADC10 interrupt service routine
#pragma vector=ADC10_VECTOR
__interrupt void ADC10_ISR(void)
{
__bic_SR_register_on_exit(CPUOFF); // Clear CPUOFF bit from 0(SR)
}

## Slide 55: LM34 Temperature Sensor

## Slide 56: ADC Temperature Schematic

## Slide 57: Changes to ADC10CTL0 Register for LM34
ADC10CTL0 |= SREF_1 | ADC10SHT_3 | ADC10ON | REFON | ADC10IE; // ADC10ON, interrupt enabled

## Slide 58: ADC10CTL1 Register
ADC10CTL1 |= INCH_4 | ADC10DIV_7; // input ch A4, Div by 8

## Slide 59: ADC
1.5V=
0V=

## Slide 60: DAC

## Slide 61: BACKUPS