## Slide 1
ECE382
Lesson 2
1

## Slide 2: Outline
Lesson Outline
  uC Comparison
  Intro to the MSP430
  MSP430 Architecture
Why?
  Most likely you will use an embedded system or uC in another class or capstone … you need to know “when to use what”
    These are all tools in a toolbox, pick the right one
    There NEVER is one right answer!
  All of these have similar (same?) capabilities, so learning it on an MSP430 will help you on another uC

## Slide 3: Micro-Controllers (uC) and Embedded Systems
There are many popular systems out there, with AVR (think Arduino) being very popular
Both the MSP430 and Atmega328, you can easily build a system using just the chip and a couple parts
All systems below support I2C, SPI, and UART serial comm
  Only the Raspberry Pi has Ethernet, Bluetooth and Wifi 2.4/5 GHz
    But it also requires an OS, the uC’s don’t
Arduino | Raspberry Pi | TI Launchpad
Atemga328 | ARMv8 quad core | MSP430G2553
2 KB RAM 32 KB Flash | 1 GB RAM | 512 B RAM 16 KB Flash
23 GPIO 6 ADC, 10b | 40 I/O pins | 20 GPIO pins 8 ADC, 10b
Chip: $1.64 | Board: $35 | Chip: $1.68

## Slide 4: Learn on Simple Systems
Minimum HW to get the MSP430 running
Minimum HW to get the Atmega328 (Arduino) running
Although the Raspberry Pi is cool, it is insanely complicated compared to a uC plus it add the complexity of an OS

## Slide 5: Intro to the MSP430
The MSP430 is a low-cost, low-power consumption embedded applications
  RISC architecture with just 27 instructions.
  Our version: Msp430g2553
  Why use it?
    Very simple architecture
    Low cost, low power
    Excellent IDE … something Arduino doesn’t have
Realistically, you will use either the Pi or an Arduino in other courses/capstone

## Slide 6: TI Launchpad

## Slide 7: Instruction Set Architecture (ISA)
ISA consists of
  set of operations (instructions)
  registers
  data units (byte/word/etc)
  addressing modes
  memory organization / memory map

## Slide 8: MSP430’s ISA
RISC architecture
  fewer instructions (27)
  emulates higher-level instructions (about 27)
    for instance, NOP  ___________
  16-bit datapath
Mov r3, r3

## Slide 9: MSP430’s ISA
16-bit datapath
  word size is 16 bits
  word is the natural unit of info for the processor
    16 bit addresses
    16 bit registers
    all instructions are 16 bits long
    this consistency isn't necessarily true of all processors, but it's convenient - allows us to load addresses into registers, perform ops on them, etc.
What is a register?

## Slide 10: MSP430’s ISA
Registers - 16 bits wide
  Fast memory that holds values in-use by the CPU
  Four special purpose registers
    r0 - Program Counter - holds address of instruction currently being executed
    r1 - Stack Pointer - address of top of stack
    r2 - Status Register - holds flags related to various conditions
    r3 - Constant Generator - 0, but can assume other values for different addressing modes
  12 general purpose registers
    r4 to r15: can be used to hold anything you want

## Slide 11: MSP430’s ISA
Set of Operations
  27 Instructions in 3 families
    Single-operand
      for instance, SWPB r12
    Conditional jump
      for instance, JMP jump_label
    Two-operand
      for instance, MOV r12, r10
    Extension words
      Additionally, depending on how you use these instructions, you might add more words to your commands
      You will see this when we turn assembly into machine code

## Slide 12: MSP430’s ISA
Data Units
  byte-addressable memory
  instructions for byte and word actions
    MOV.B r12, r10
    MOV.W r12, r10 (if not specified, default: word)
    MOV r12, r10 (this is a word operation)
  remember, word size is 16 bits
    words must lie on even addresses
      The HW prevents you from access bytes … we’ll see that later

## Slide 13: MSP430’s ISA
Msp430g2553 Memory Map
512b of RAM - 0x200-0x400 16kb of ROM - 0xc000-0xffdf
0x1100-0xbfff is empty!
There is no memory backing it up!
If you attempt to write to this area of memory, you'll trigger what's essentially a segmentation fault because that memory doesn't exist. It will cause the chip to do a Power-up Clear (PUC), resetting the state of your processor. This is a tough error to debug.
How many addr bits?

## Slide 14: MSP430’s ISA
How many addr bits?
 |  | MSP430G2553
Memory Main: interrupt vector Main: code memory | Size Flash Flash | 16kB 0xFFFF to 0xFFC0 0xFFFF to 0xC000
Information memory | Size Flash | 256 Byte 010FFh to 01000h
RAM | Size | 512 Byte 0x03FF to 0x0200
Peripherals | 16-bit 8-bit 8-bit SFR | 01FFh to 0100h 0FFh to 010h 0Fh to 00h
Excerpt from Table 8: Memory Organization from MSP430G2x53 Device Specific User Guide (pp13) |  | 

## Slide 15: MSP430Architecture Uses Little Endian
Values stored in little-endian byte order
Least significant byte is stored first
5000
5001
5002
5003
Memory Address
Note, the address provides location to a BYTE and NOT a BIT
MSB
LSB
Notice the difference between how humans write things on paper, but the machine stores it in memory!
LSB
MSB

## Slide 16: Assembly and Machine Languages
Instructions:
  words in a computers language
Instruction Set:
  the dictionary of the language
Assembly Language:
  human-readable format of computer instructions
Machine Language:
  computer-readable instructions - binary (1's and 0's)

## Slide 17: Assembly and Machine Languages
Assembler
Your Assembly Program
Linker
Relocatable Object Code
Executable Code
This is what the IDE does, for us it is Code Composer Studio (CCS)
Now, on a computer with an OS, this would be a potential App the user could run … on a uC, there is no choice and this is the only code that runs
Instructions:
  words in a computers language
Instruction Set:
  the dictionary of the language
Assembly Language:
  human-readable format of computer instructions
Machine Language:
  computer-readable instructions
  binary (1's and 0's)

## Slide 18: Example MSP430 program
; This program sets all pins on Port 1 to output and high.
; Since LEDs 1 and 2 are connected to P1.0 and P1.6
; respectively, they will light up.
.include 'header.S'
.text
main:
mov.w #WDTPW, r15 ; turn off watchdog timer
xor.w #WDTHOLD, r15
mov.w r15, &WDTCTL
bis.b #0xFF, &P1DIR ; set port1 direction to output
bis.b #0xFF, &P1OUT ; turn on leds at port1
loop:
jmp loop ; loop forever
Instructions similar to the ones you used in ECE281

## Slide 19: Disassembled Code
Disassembly of section .text:
0000c000 <__ctors_end>:
c000: 3f 40 00 5a mov #23040, r15 ;#0x5a00
c004: 3f e0 80 00 xor #128, r15 ;#0x0080
c008: 82 4f 20 01 mov r15, &0x0120
c00c: f2 d3 22 00 bis.b #-1, &0x0022 ;r3 As==11
c010: f2 d3 21 00 bis.b #-1, &0x0021 ;r3 As==11
0000c014 <loop>:
c014: ff 3f jmp $+0 ;abs 0xc014
The point here, is, the linker changes the addresses of the relocatable code for your SPECIFIC uC (G2553). A different model could have different addresses

## Slide 20: Backups