## Slide 1
ECE382
Lesson 20
1

## Slide 2: Overview
Lesson Outline
  Intro to C
  Program flow control

## Slide 3: C Language: Comments
// Single line comment
/* block comment that can span
multiple lines */
int i = 0; // a declaration
/*************************************
** The previous variable was
** declared just as an example.
*************************************/

## Slide 4: C Language: Variables
•Note: These sizes are dependent on the compiler and target architecture - these are for the MSP430.
•Note: Do not use the float / double types on the MSP430 - since it doesn't have floating point hardware support, implementing software support will use almost all of your memory.
Type | Size | Description
char | 1 byte | number or ASCII character
int | 2 bytes | larger number
float | 2 bytes | single-precision floating point number
double | 4 bytes | double-precision floating point number
bool | 1 byte | True or false, need to include stdbool.h
Variable Types

## Slide 5: C Language: Variables
•Note: Once again, sizes are dependent on compiler / target architecture - these are for the MSP
Variable Modifiers
Modifier | Description
short | remains a 2-byte integer
long | increases int size to 4 bytes
signed | two's complement numbers (default)
unsigned | allows unsigned arithmetic
static | directly allocates memory to remember a value between function calls. Variable is allocated to "permanent" memory, not the stack.
extern | actual storage and initial value of variable is defined elsewhere
const | assigns a constant (read-only) value to a variable

## Slide 6: #include <msp430.h>
c:\ti\ccsv6\ccs_base\msp430\include\msp430g2553.h
c:\ti\ccsv6\ccs_base\msp430\include\msp430.h
From assembly template:

## Slide 7: #include <stdint.h>
In: C:\ti\ccsv6\tools\compiler\msp430_15.12.3.LTS\include
Take a look, this defines a bunch of data types to help you:
Long Declaration | Clear Shorthand
signed char | int8_t
unsigned char | uint8_t
int | int16_t
unsigned int | uint16_t
long | int32_t
unsigned long | uint32_t
Why is this useful? Portability … an int isn’t always 16 bits on every architecture. It is useful to use these, makes your code more readable (and portable)
These data types will cleanly compile on x86, MSP430, ARM (32b/64b), etc

## Slide 8: Others
#include <stdbool.h> defines booleans
  true = 1
  false = 0
  bool is a valid data type
#include <math.h> defines things like:
  #define M_PI 3.14159265358979323846 /* pi */
  #define M_PI_2 1.57079632679489661923 /* pi/2 */
  sqrtf() square root float
  sqrt() square root double (default)
  cosf() cosine float
  cos() cosine double (default)
  etc

## Slide 9: So now you can write this
#include <msp430.h>
#include <stdint.h>
#include <stdbool.h>
/*
* main.c
*/
void main(void) {
WDTCTL = WDTPW | WDTHOLD; // Stop watchdog timer
uint8_t bob = 0;
bool run = true;
while(run){
bob += 1;
}
while(true){;} // CPU trap
}

## Slide 10: Volatile
static int foo;
void bar(void) {
foo = 0;
while (foo != 255)
;
}
void bar_optimized(void) {
foo = 0;
while (true)
;
}
static volatile int foo;
void bar (void) {
foo = 0;
while (foo != 255)
;
}
If you program this, where foo is tied to a pin and polled for change
A good compiler will optimize to this. Nothing changes foo, or so the compiler thinks.
In order to tell the compiler, “hey, don’t change foo!”, declare it volatile.
Volatile is an important key word in embedded applications talking to memory mapped IO

## Slide 11: C Language: Constants
Preferred Constant Declaration
The #define statement is a pre-processor directive.
pre-processor will “find-replace” each instant
similar to a .equ statement in assembly.
// #define MY_CONST some_value
#define SCREEN_WIDTH 640
#define SCREEN_HEIGHT 480
int numPixels = 0;
numPixels = SCREEN_WIDTH * SCREEN_HEIGHT;
•Note: There is no ';' or '=' in #define statements
•Note: Variables must be declared at the top of a block, and they are not initialized by default. A block is denoted by braces {}
•Note: A value can be binary (0b), octal (0), or hex (0x) by using prefixes
Generally poor form, unless you are writing compilers or SW tools

## Slide 12: Constants vs Macros (#define)
const
Tells the compiler the variable (or pointer) can not be modified
Properly scoped / identifier clash issues handled nicely
Depending on how it is used may not consume RAM
The compiler can check you are using it correctly (i.e. data type) and throw a warning or error if you are not
#define
It acts like a global copy/paste and can produce very difficult bugs to find
  Is this a problem? uint8_t == int16_t
"global" scope / more prone to conflicting usages, which can produce hard-to-resolve compilation issues and unexpected run-time results rather than sane error messages
Compiler assumes it is untyped and some compilers will allow comparisons between defines and unsigned ints (which you may not want)

## Slide 13: C Language: Operators
Assignment, Arithmetic Operators
char myVar, a, b; // variable declaration, gcc sets their value to 0
myVar = a; // assignment - note, all vars have undefined values at this point
myVar = a + b; // addition
myVar = a - b; // subtraction
myVar = a * b; // multiplication
myVar = a / b; // division
myVar = a % b; // modulus (remainder)
myVar++; // increment
myVar--; // decrement
myVar += a; // myVar = myVar + a
myVar -= a; // myVar = myVar - a

## Slide 14: C Language: Operators
Relational Operators
if ((a < 10) && (a > 5)) {
// literally: if a is greater than 5 and less than 10, do whatever is in here
// practically: if a is between 5 and 10, do whatever is in here
}
•Note: In C, "false" is 0, while any non-zero value is considered true.
Operator | Description
< | less than
<= | less than or equal to
> | greater than
>= | greater than or equal to
== | equal to
!= | not equal to
&& | logical AND
¦ ¦ | logical OR

## Slide 15: C Language: Operators
Bit-wise Operators
uint8_t a = 5;
uint8_t b = 5;
a &= ~BIT2;
B |= BIT2;
// Example with SPI
UCA0CTL1 &= ~UCSWRST; // enable the subsystem (AND UCA0CTL1 with NOT UCSWRST)
UCA0CTL1 |= UCSWRST; // disable the subsystem (OR UCA0CTL1 with UCSWRST)
Operator | Description
& | AND
¦ | OR
^ | XOR
~ | One's Complement
>> | Bit-shift right
<< | Bit-shift left
BIT2: 00000100
~BIT2: 11111011
a & b: 00000101
11111011
0 0 0 0 0 1

## Slide 16: BIS and BIC in C
BIC in C
BIT2: 00000100
~BIT2: 11111011
a & ~BIT2: 00000101
11111011
00000001
uint8_t a = 5;
uint8_t b = 5;
a &= ~BIT2; // clear bit 2
b |= BIT1; // set bit 1
BIS in C
b | BIT1: 00000101
00000010
00000111
Instead of number, these could be ports or registers that we are setting/clearing bits on

## Slide 17: If Statement
  if (logical expression){
  statements;
  }
  else if (logical expression){
  statements;
  }
  ...
  else{
  statements;
  }
Example:
  if (temp < MIN_TEMP) {
  flag = TOO_LOW;
  }
  else if (temp > MAX_TEMP){
  flag = TOO_HIGH;
  }
  else{
  flag = JUST_RIGHT;
  }

## Slide 18: Switch Statement
  switch (value){
  case constant-expression1:
  statements;
  break;
  case constant-expression2:
  statements;
  break;
  default:
  // gets executed if no other case hits
  statements;
  break;
  }
Example:
  switch (GAME_STATE){
  case MENU:
  displayMenu();
  break;
  case PLAYING:
  updateState();
  break;
  case LOST:
  displayLost();
  break;
  }

## Slide 19: For Loop
  for (initial; continue; increment){
  statements;
  }
initial – initializes variable to the starting value
continue – continues looping while condition is true
increment - usually used to increment / decrement a variable
Example:
  int sum = 0; // good form to ALWAYS initialize your variables
  for (int i = 1; i <= 20; i++){
  sum += i;
  }

## Slide 20: While / Do While Loop
  while (condition) {
  statements;
  }
  do while is guaranteed to be executed once, while isn't.
  do
  {
  statements;
  } while (condition);
Example:
  int i = 5;
  while (i < 10){i++;}
  do {
  i++;
  } while (i < 10);
  // final value of i is 11
Will execute at least once!
Is this valid? … yes! You could write your entire program on one line … but please don’t!!

## Slide 21: Basic C Program Structure
  // #include statements
  // #define statements
  // global variables <- NOOOOOO!
  void main(void)
  {
  // Variable declarations
  // Useful code
  while (1) {;} // trap the CPU
  }
Example:
  #include <stdio.h>
  #include <stdint.h>
  const unint8_t NUM_LOOPS = 23;
  void main(void)
  {
  unsigned char i;
  unsigned int summation = 0;
  for (i = 1; i <= NUM_LOOPS; i++)
  {
  summation += i;
  }
  while (1) {;} // trap the CPU
  }

## Slide 22: main.c Documentation
  /*--------------------------------------------------------------------
  Name:<Your Name>
  Date:<The date you stated working on the file>
  Course: <The course's name>
  File:<This file's name>
  HW: <HW# and name>
  Purp:A brief description of what this program does and
  the general solution strategy.
  Doc: <list the names of the people who you helped>
  <list the names of the people who assisted you>
  Academic Integrity Statement: I certify that, while others may have
  assisted me in brain storming, debugging and validating this program,
  the program itself is my own work. I understand that submitting code
  which is the work of other individuals is a violation of the honor
  code. I also understand that if I knowingly give my original work to
  another individual is also a violation of the honor code.
  -------------------------------------------------------------------------*/
Your code is LATE (25% per day) if you do not have this at the top of main.c

## Slide 23: BACKUPS