## Slide 1
ECE382
Lesson 9+10
1

## Slide 2: Overview
Lesson Outline
  The Stack
  Subroutines (like functions)
  Application (ABI)
Why?
  Modular code: we want to break things up into small, testable pieces of code that we can reuse … subroutines help us do this
  ABI helps ensure binary compatibility of modular code
  Subroutines use the stack to do their job
    But understanding how the stack works also allows you to do “stack manipulation” and maybe write a virus or patch broken code

## Slide 3: Stack
What is a Stack?
  Last In First Out (LIFO) queue
  Push and Pop are our two operations for dealing with the stack
  The last item you pushed onto the stack is the first item you'll pop off of it.
Why use a Stack?
  Temporary Storage
  Subroutine calls/returns use the Stack
Stack Pointer
  Holds the address of the top of the stack
    Stack Pointer (SP), also known as r1

## Slide 4: Stack
Stack Instructions
Where is the Stack located in memory?
Assembly Instruction | Description
PUSH(.B) | Push operand on stack. Push byte decrements SP by 2.
Emulated Instruction | Assembly Instruction
POP dst | MOV @SP+, dst

## Slide 5: Stack
Where is the Stack located in memory?
In RAM
- need to read and write to it
RAM is from 0x200 to 0x400
Where in RAM should you initialize the
Stack Pointer to point to?

## Slide 6: Stack
Where in RAM should you initialize the
Stack Point too?
0x400
0x200 would be bad!

## Slide 7: Stack
mov.w #0x0400, r1 ;initialize stack pointer
push.w #0xdfec ;push the value 0xdfec onto the stack.
;This decrements the SP by two to 0x03fe and
; stores EC at 0x03fe and DF at 0x03ff
pop.w r10 ;pop the value we just pushed off of the stack and
; into r10
; this decrements the SP by two, back to 0x0400.
push #0xbeef
push.b #0xcc
push #0xdfec
pop r5
pop.b r6
pop r7
push #0xfade
push.b #0xaa
push #0xdeaf
pop.b r5
pop r6
pop.b r7
Address | Value
0x3FA | 
0x3FB | 
0x3FC | 
0x3FD | 
0x3FE | 
0x3FF | 
0x400 | 

## Slide 8: The example code

## Slide 9: Initial State
SP 0x0400
R5 0x0000
R6 0x0000
R7 0x0000
R10 0x0000
Next instruction to run
SP location highlighted
Stack

## Slide 10: push.w #0xdfec
SP 0x03FE
R5 0x0000
R6 0x0000
R7 0x0000
R10 0x0000
PUSH
SP – 2  SP
src  @SP

## Slide 11: pop.w r10
SP 0x0400
R5 0x0000
R6 0x0000
R7 0x0000
R10 0xDFEC
POP
@SP  dest
SP + 2  SP

## Slide 12: push #0xbeef
SP 0x03FE
R5 0x0000
R6 0x0000
R7 0x0000
R10 0xDFEC

## Slide 13: push.b #0xcc
SP 0x03FC
R5 0x0000
R6 0x0000
R7 0x0000
R10 0xDFEC
This byte left AS IS

## Slide 14: push #0xdfec
SP 0x03FA
R5 0x0000
R6 0x0000
R7 0x0000
R10 0xDFEC

## Slide 15: pop R5
SP 0x03FC
R5 0xDFEC
R6 0x0000
R7 0x0000
R10 0xDFEC

## Slide 16: pop.b R6
SP 0x03FE
R5 0xDFEC
R6 0x00CC
R7 0x0000
R10 0xDFEC

## Slide 17: pop R7
SP 0x0400
R5 0xDFEC
R6 0x00CC
R7 0xBEEF
R10 0xDFEC

## Slide 18: push #0xfade
SP 0x03FE
R5 0xDFEC
R6 0x00CC
R7 0xBEEF
R10 0xDFEC

## Slide 19: push.b #0xaa
SP 0x03FC
R5 0xDFEC
R6 0x00CC
R7 0xBEEF
R10 0xDFEC
This byte left AS IS

## Slide 20: push #0xdeaf
SP 0x03FA
R5 0xDFEC
R6 0x00CC
R7 0xBEEF
R10 0xDFEC

## Slide 21: pop.b R5
SP 0x03FC
R5 0x00AF
R6 0x00CC
R7 0xBEEF
R10 0xDFEC
Byte Op cleared UPPER nibble

## Slide 22: pop R6
SP 0x03FE
R5 0x00AF
R6 0xAAAA
R7 0xBEEF
R10 0xDFEC
Mystery byte here
This byte was never changed

## Slide 23: pop.b R7
SP 0x0400
R5 0x00AF
R6 0xAAAA
R7 0x00DE
R10 0xDFEC
Byte Op cleared UPPER nibble

## Slide 24: Stack
How can I use the Stack to swap the values in two registers (like r10, r11)?
Can we push too many variables on the stack?
Is the stack limited?

## Slide 25: Subroutines
Why Subroutines?
  Supports Modularity; easier to read code; Supports re-use
  Call #SQ_ROOT
  …
  Call #SQ_ROOT
  …
  …
  SQ_ROOT: …
  …
  …
  RET
What happens in you didn’t initialize the Stack Pointer?
What If Stack Pointer pointed to ROM?
Assembly Instruction | Description
CALL | Fetch operand, push PC, then assign operand value to PC.
Emulated Instruction | Assembly Instruction
RET | MOV @SP+, PC
0xC010
0xC020

## Slide 26: Example Subroutine
main:
mov.w #2, r10
mov.w #4, r11
call #addition
nop
nop
nop
nop
addition:
add.w r10, r11
ret

## Slide 27: Arguments
Arguments are the parameters (or data) passed to and from a subroutine
  ;---------------------------------------------------
  ; Function: Adds two numbers
  ; Inputs: Op1 (r10), Op2 (r11)
  ; Outputs: result (r11)
  ; Registers destroyed: r11
  ;---------------------------------------------------
  addition:
  add.w r10, r11
  ret
How could I avoid destroying registers used in a subroutine?

## Slide 28: Arguments
Use a stack to avoid destroying registers
  mySubroutine:
  push.w r5
  push.w r6
  push.w r7
  ;... Do subroutine work here ....
  pop.w r7
  pop.w r6
  pop.w r5
  ret
What is Pass-by-Value and Pass-by-Reference?

## Slide 29: Arguments
Pass-by-Value
  pass the actual values of the arguments to a subroutine
Pass-by-Reference
  Pass the address of the argument to a subroutine
Which did we do in the Addition subroutine?
Which method can modify the original source data, and which can only modify a copy of the source data?
Which is best if you are passing an array of 1000 values?

## Slide 30: Example Subroutine with pass-by-reference
;---------------------------------------------------
; Function: Adds two numbers, returns the result
; Inputs: address of Op1 (r10), address of Op2 (r11)
; Outputs: result (r11)
; Registers destroyed: r11
;---------------------------------------------------
addition:
push.w r12
mov.w @r11, r12
add.w @r10, r12
mov.w r12, r11
pop r12

## Slide 31: Key Subroutine Rules
Always return from a subroutine!
  should only return from one place in your subroutine.
Subroutines only receive information via registers!
  reusable for many different programs
  should not rely on specific label names for arguments (what about ports?)
  Can we use the Stack to pass arguments?
Subroutines should be reusable!

## Slide 32: Very Simple Explanation
Hardware
OS (not present in a uC)
Libraries
Application SW
ISA
ABI
API
Your code
Ensure subroutines/functions have the same interface to make writing programs easier and introduce less bugs
Deals with source code
Ensure subroutines/functions after compiling, operate the same on similar HW (say all x86) the same
Deals with a binary program

## Slide 33: Application Binary Interface (ABI)
Convention of specifying which registers are used for arguments passed in to a subroutine and which are used to pass back results.
For subroutines in the MSP430 use r12, r13, r14, and r15 to pass arguments to your subroutine.
Use the stack if you have more than four arguments
If you follow the ABI and then link to a 3rd party library (meaning someone else developed it and you have probably never seen the source code), it should work correctly!!

## Slide 34
Find asm library function example

## Slide 35: BACKUPS