## Slide 1: Lab 7b: Morse Code II
http://www.youtube.com/watch?v=fZKVdxeWsyw

## Slide 2: Lab 7b: Morse Code II
"Use your Morse Code main assembly lab code to write a C program that outputs alphanumeric Morse code messages using an LED and a transducer (magnetic speaker). Use the watchdog as an interval timer whose interrupt service routine (ISR) pulse width modulates (PWM) the transducer device creating a tone. Use a C string to store the message. Use Switch #1 to toggle the tones on and off."

## Slide 3: Morse Code II Lab
Use your Morse Code main assembly lab code to write a C program that outputs alphanumeric Morse code messages using an LED and a transducer (magnetic speaker).
Use the watchdog as an interval timer whose interrupt service routine (ISR) pulse width modulates (PWM) the transducer device creating a tone.
Use a C string to store the message.
Store all C and assembly equates in a C header file. Include the header file in both your C and assembly programs.
Assess Dot and Dash codes from an external assembly file.
Use Switch #1 to turn the tones on and off.

## Slide 4: Learning Objectives
By completing the Morse Code Lab, a student will have:
  Translated assembly language code to C.
  Used a C header file for all assembly/C constants.
  Interfaced C code with external functions including assembly and other C modules.
  Demonstrated "callee-save" protocol when calling subroutines.
  Linked symbolic values together from different program files.

## Slide 5: C / Assembler Protocol
f(w,x,y,z)
Arguments are evaluated right to left:
  if 8 or 16-bit data types, w, x, y, and z are passed to the function in registers r12, r13, r14, r15 respectively.
  If 32-bit data types, z is pushed onto the stack, followed by y, followed by w and x in registers pairs r13:r12 and r15:r14 respectively.
  The result is returned in R12 (or R13:R12 for a 32 bit type) or in a special area pointed to by R12 if it is a struct or union type.
Argument | < 32-bit Type | 32-bit Type | struct/union
4th (z) | R15 | On the stack | On the stack
3rd (y) | R14 | On the stack | On the stack
2nd (x) | R13 | R15:R14 | On the stack
1st (w) | R12 | R13:R12 | On the stack
Return Value | R12 | R13:R12 | Special Area

## Slide 6: C / Assembler Protocol
C
Assembly
extern int asm_mult(int, int);
void main(void)
{
int result;
result = asm_mult(10, 20);
return;
}
int C_multiply(int x, int y)
{
return x * y;
}
.def asm_mult
.ref C_multiply
.text
; asm_mult ********************
; IN: r12 = arg1
; r13 = arg2
; OUT: r12 = arg1 * arg2
;
asm_mult:
call #C_multiply
ret
.end
extern must be used to declare C function prototype

## Slide 7: C / Assembler Protocol
extern int asm_mult(int, int);
void main(void)
{
int result;
result = asm_mult(10, 20);
return;
}
int C_multiply(int x, int y)
{
return x * y;
}
C
Assembly
.def asm_mult
.ref C_multiply
.text
; asm_mult ********************
; IN: r12 = arg1
; r13 = arg2
; OUT: r12 = arg1 * arg2
;
asm_mult:
call #C_multiply
ret
.end
All C functions are externally defined
(unless declared static)

## Slide 8: volatile
volatile proceeding a variable name instructs the compiler to
  prohibit caching the variable’s contents when optimizing code.
  always re-read the variable’s value when accessing the variable.
  not use computer registers to store a variable’s content.
volatile int switches,dcnt
void main(void)
{
if (switches & 0x01) {...}
}
#pragma vector=PORT1_VECTOR
__interrupt void Port_1_ISR(void)
{ P1IFG &= ~0x0f; // P1.0-3 IFG cleared
dcnt = DEBOUNCE_CNT; // enable debounce
}
#pragma vector = WDT_VECTOR
__interrupt void WDT_ISR(void)
{ if (dcnt && (--dcnt == 0)) switches = (P1IN ^ 0x0f) & 0x0f;
}
Inform the compiler that integers switches and dcnt are not to be optimized.
Pressing a switch sets dcnt
Sample P1IN when dcnt equals 0

## Slide 9: Part 1 – Setup
Create an empty CCS Morse2 C project.
Rename main.c to morse2.c, add your Morse Code Lab assembly files (morse.asm, morse_codes.asm), and a C header file (morse2.h) to your Morse2 project.
Modify your morse2.c to call main_asm in morse.asm file.
  Replace the main function in morse2.c file with the following code:
extern int main_asm(void);
int main(void)
{
WDTCTL = WDTPW | WDTHOLD;
main_asm();
return 0;
}

## Slide 10: Part 1 – Setup
  Add (temporarily) the following assembly code to your morse.asm file:
  Find and delete (or comment) the following assembly code from your morse.asm file:
Compile and execute. Verify your Morse Code II lab works.
.def main_asm
; power-up reset --------------------------------------
RESET: mov.w #STACK,SP ; initialize stack pointer
call #main_asm ; call main function
jmp $ ; you should never get here!
.sect ".reset"
.word RESET ; RESET ISR

## Slide 11: Part 2 – The Lab
Replace the contents of your C main function with cut assembly code from your morse.asm file.
  Replace:
  with the cut main_asm assembly code from your morse.asm file:
  Comment all lines of assembly code (using contrl-/).
main_asm();
; start main function vvvvvvvvvvvvvvvvvvvvvvvvvvvvvvv
.def main_asm
main_asm: mov.w #WDT_CTL,&WDTCTL ; set WDT interval
mov.b #WDTIE,&IE1 ; enable WDT int
...
jmp loop ; repeat
; end main function ^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^

## Slide 12: Part 2 – The Lab (continued)
Move all #define's and assembly .equ's to morse2.h. Include morse2.h in both morse2.c and morse.asm files.
  Translate all assembly .equ's to C #define's and include in morse2.h.
    Do not put any variable or function definitions (code) in your header file!
    Be careful to parenthesize all constant calculations. (ie, Use "#define ELEMENT (XXX * 10) / 100" instead of "#define ELEMENT XXX * 10 / 100", which evaluates to zero.)
  Include morse2.h in your C files:
  Include morse2.h in your assembly files:
#include "msp430.h" // .cdecls C,"msp430.h"
#include "morse2.h"
#include <stdlib.h>
#include <ctype.h>
.cdecls C,"msp430.h"
.cdecls C,"morse2.h"

## Slide 13: Part 2 – The Lab (continued)
Add C code to your main function that implements the commented assembly code.
  Where possible, place the C code on the same line as the assembly code.
  Remember, MSP430 registers are just variables.
  Multiple assembly lines may be represented by one C statement.
  All assembly functions called from C must follow C register usage and be callee-safe.
extern char* letters[]; // ; start main function vvvvvvvvvvvvvvvv
    // .def main_asm
int main(void) // main_asm:
{
WDTCTL = WDT_CTL; // mov.w #WDT_CTL,&WDTCTL ; WDT config
WDTSecCnt = WDT_IPS; // mov.w #WDT_IPS,WDTSecCnt ; 1s counter
IE1 = WDTIE; // mov.b #WDTIE,&IE1 ; WDT ints
P3DIR = 0x10; // bis.b #0x10,&P3DIR
while (1) // loop:
{ char c;
char* cptr;
char* mptr = message; // mov.w #message,r4 ; message
while (c = *mptr++) // loop2:
{ // mov.b @r4+,r5 ; get char
// cmp.b #0,r5 ; done?
// jeq loop10 ; y

## Slide 14: Part 2 – The Lab (continued)
Use .ref and extern to cross reference variables.
  To reference assembly variables from C, use extern and .def:
  Assembly C
  To reference C variables from assembly code, use .ref:
  C Assembly
.def beep_cnt
.bss beep_cnt,2
extern int beep_cnt;
beep_cnt = 100;
int beep_cnt;
beep_cnt = 100;
.ref beep_cnt;
mov.w #100,beep_cnt

## Slide 15: Part 2 – The Lab (continued)
Repeat the process of cutting, pasting, and translating an assembly ISR into your morse2.c file.
Call at least one assembly function using correct C calling convention. Modify function (if necessary) such that it is callee-safe.
extern volatile int dcnt; // .def dcnt
// .bss dcnt,2 ; debounce counter
#pragma vector=PORT1_VECTOR
__interrupt void Port_1_ISR(void)
{ // P1_ISR:
P1IFG &= ~0x0f; // bic.b #0x0f,&P1IFG ; acknowledge
dcnt = DB_CNT; // mov.w #DB_CNT,&dcnt ; reset counter
return; // reti
}

## Slide 16: How Assembler Relates to C

## Slide 17: if-then-else
if-then-else
if (buzzerON == 1)
{
pulse_buzzer();
turn_on_LED();
}
else
{
turn_off_LED();
}
cmp.w #1,buzzerON ;
jne myElse ;
xor.b #0x20,&P4OUT ;
bis.b #0x02,&P1OUT ;
jmp myNext ;
myElse: ;
bic.b #0x02,&P1OUT ;
;
myNext: ;

## Slide 18: switch / case
switch / case
switch (myByte)
{
case DOT:
do_dot();
break;
case DASH:
do_dash();
break;
default:
}
cmp.w #DOT,myByte ;
jne sw_01 ;
call #do_dot ;
jmp sw_end ;
sw_01:
cmp.w #DASH,myByte ;
jne default ;
call #do_dash ;
jmp sw_end ;
;
default: ;
sw_end: ;

## Slide 19: for-loop
for-loop
int i;
for(i=0; i<10; i++)
{
do_dot();
delay();
do_dash();
delay();
}
.bss i,2 ;
mov.w #0,i ;
for_ck: cmp.w #10,i ;
jge for_done ;
call #do_dot ;
call #delay ;
call #do_dash ;
call #delay ;
add.w #1,i ;
jmp for_ck ;
for_done: ;

## Slide 20: while
while loop…
#define TRUE 1
int blink = TRUE;
while (blink)
{
LED_ON();
delay();
LED_OFF();
delay();
}
TRUE .equ 1
.bss blink,2 ;
mov.w #TRUE,blink ;
while_loop: ;
cmp.w #0,blink ;
jeq while_done ;
call #LED_ON ;
call #delay ;
call #LED_OFF ;
call #delay ;
jmp while_loop ;
while_done: ;

## Slide 21: Morse Code II Requirements
1 point | Your Morse II Lab includes C and assembly code, and contains header comments stating your name and a declaration that the completed assignment is your own work.
2 points | Your Morse Code "main" function and at least one ISR are written in C. At least one assembly function is called from C using correct C calling convention and is callee-safe.
1 point | Assembly arrays numbers and letters in morse_codes.asm are correctly referenced in your C program as character pointer arrays.
2 points | A C header file containing all C #define's and assembly equates(.equ's changed to #define's) is included in all .c and .asm files. NO VARIABLE OR FUNCTION DEFINITIONS ARE FOUND IN THE HEADER FILE (ie, only declarations, pre-processor commands, and function prototypes).
2 points | Your commented assembly code appears to the right of the C statements. (Small blocks of assembly code are acceptable. See example above.)
2 points | Your C Morse Code II machine meets all the same requirements as the assembly Morse Code lab.
Morse Code

## Slide 22: Morse Code II Requirements
Morse Code
+1 point | Passed off with a TA at least one day early. (No timestamps please!)
+2 points | The current character, message, and speed are displayed in real-time on the LCD.
+1 point† | The MSP430 enters low power mode 0 while the watchdog ISR outputs DOTs, DASHes, and space elements.
+2 points† | Using interrupts, pressing Switch #2 (SW2) decreases the output speed of your Morse Code Machine by 1 word per minute. Pressing Switch #3 (SW3) increases the speed of your machine by 1 word per minute. The output speed is displayed in the LEDs (D1-D4). Do the calculations in the switch and watchdog ISRs.
-1 points | For each school day late. (Timestamps may be used to verify completion time.)
 | †Only awarded if not used for bonus credit in the Morse Lab.
Bonus Points:

## Slide 24: Morse Code
The word PARIS is the standard to determine Morse Code speed.
  Each dit (dot) is one element,
  Each dah (dash) is three elements,
  Intra-character spacing is one element,
  Inter-character spacing is three elements,
  and inter-word spacing is seven elements.
PARIS is exactly 50 elements
  If you send PARIS 5 times in a minute (5 WPM) you have sent 250 elements.
  250 elements into 60 seconds per minute = 240 milliseconds per element.
  13 words-per-minute is one element every 92.31 milliseconds.
           
Morse Code

## Slide 25: Part 1 – Setup
Create an empty CCS Morse2 C project.
Rename main.c to morse2.c, add Morse Code Lab assembly files, and a C header file to your Morse2 project.
Modify your morse2.c to call main_asm in morse.asm file.
  Replace the main function in morse2.c file with the following code:
  Add (temporarily) the following assembly code to your morse.asm file:
  Delete the following assembly code from your morse.asm file:
Compile and execute. Verify your Morse Code II lab works.
extern int main_asm(void);
int main(void) {
WDTCTL = WDTPW | WDTHOLD;
main_asm();
return 0;
}
.def main_asm
.sect ".reset“
.word RESET ; RESET ISR