## Slide 1: S01 - Data Types
Required: PM: Ch 3, pgs 27-35
PM: Ch 5.1-6, pgs 47-56
Code: Chs 1-9, 20 Recommended: Wiki: Signed Numbers Two's Complement Wiki: Two's_complement Wiki: Fixed Point Floating Point

## Slide 2: CS 224
Chapter | Lab | Homework
S00: Introduction |  | 
Unit 1: Digital Logic |  | 
S01: Data Types S02: Digital Logic | L01: Warm-up L02: FSM | HW01 HW02
Unit 2: ISA |  | 
S03: ISA S04: Microarchitecture S05: Stacks / Interrupts S06: Assembly | L03: Blinky L04: Microarch L05b: Traffic Light L06a: Morse Code | HW03 HW04 HW05 HW06
Unit 3: C |  | 
S07: C Language S08: Pointers S09: Structs S10: I/O | L07b: Morse II L08a: Life L09b: Snake | HW07 HW08 HW09 HW10

## Slide 3: Data Types Learning Outcomes…
Students will be able to:
Represent an integral decimal number as an unsigned or signed 1’s and 2’s complement integer, signed magnitude number, and ASCII character.
Represent a fractional decimal number in fixed point and floating point formats.
Convert a binary number to decimal format.
Convert a decimal number to binary format.
Articulate the use of computer word size, endianess, sign extension, and number overflow in developing computer programs.

## Slide 4: Need to Know…
Binary Digital System
Hexadecimal Numbers
Integral Data Types
    Unsigned
    Sign magnitude
    1’s & 2’s complement
    Overflow
    Word Size
    Sign-extension
    Decimal to binary conversion
Fractional Data Types
    Fixed Point
    Floating Point
ASCII Characters
Casting, Endianess

## Slide 5: What are Decimal Numbers?
“Decimal” means that we have ten digits to use in our representation of numbers
  Symbols 0 through 9
  Positional notation
  Most widely used by modern civilizations
What is 3,546?
  3 thousands + 5 hundreds + 4 tens + 6 ones.
  3,54610 = 3103 + 5102 + 4101 + 6100
How about negative numbers?
  Need additional symbol(s)
Digital Binary System

## Slide 6: What are Binary Numbers?
“Binary” means that we have two digits to use in our representation of numbers
  Symbols 0 and 1
  Positional notation
  More adaptable for computers
What is the decimal value of binary 1011?
  1 eights + 0 fours + 1 twos + 1 ones
  10112 = 123 + 022 + 121 + 120
How about negative numbers?
  We don’t want to add additional symbols
  So…
Digital Binary System

## Slide 7: Binary Digital System
What is a Binary Digital System?
  Binary (base 2) means there are two states, 0 and 1.
  Digital means there are a finite number of symbols.
  Basic unit of information is the binary digit, or bit.
How are bits represented?
  Voltages
  Residual magnetism
  Light
  Polarization
What about more than two states?
  A collection of 2 bits has 4 possible states: 00, 01, 10, 11
  A collection of 3 bits has 8 possible states: 000, 001, 010, 011, 100, 101, 110, 111
  A collection of n bits has 2n possible states.
Digital Binary System

## Slide 8: Electronic Representation of a Bit
Computers rely only on approximate physical values.
  A logical ‘1’ is a relatively high voltage (2.4V - 5V).
  A logical ‘0’ is a relatively low voltage (0V – 0.5V).
Analog processing relies on exact physical values which are affected by temperature, age, etc.
  Analog values are never quite the same.
  Each time you play a vinyl album, it will sound a bit different.
Digital Binary System
Bits rely on approximate physical values which are not affected by age or temperature.
  Music that never degrades.
  Pictures that never get dusty or scratched.

## Slide 9: Binary Nomenclature
Byte (B) | 100 |  | 20 | 1 byte
Kilobyte (kB) | 103 | Kibibyte | 210 | 1024 bytes
Megabyte (MB) | 106 | Mebibyte | 220 | 1,048,576 bytes
Gigabyte (GB) | 109 | Gibibyte | 230 | 1,073,741,824 bytes
Terabyte (TB) | 1012 | Tebibyte | 240 | 1,099,511,627,776 bytes
Petabyte (PB) | 1015 | Pebibyte | 250 | 1,125,899,906,842,624 bytes
Exabyte (EB) | 1018 | Exbibyte | 260 | 1,152,921,504,606,846,976 bytes
Zettabyte (ZB) | 1021 | Zebibyte | 270 | 1,180,591,620,717,411,303,424 bytes
Yotabyte (YB) | 1024 | Yobibyte | 280 | 1,208,925,819,614,629,174,706,176 bytes
Digital Binary System
SI Name (Symbol) | Value | Binary | Value | 
By using groups of bits, we can achieve high precision.
    8 bits => each bit pattern represents 1/256.
    16 bits => each bit pattern represents 1/65,536
    32 bits => each bit pattern represents 1/4,294,967,296
    64 bits => each bit pattern represents 1/18,446,744,073,709,550,000
IEC International Standard names and symbols for binary prefixes:

## Slide 10: Hexadecimal Notation
Binary is hard to read (very verbose)
Hexadecimal is a common alternative
  16 digits are 0123456789ABCDEF
0100 0111 1000 1111 = 0x478F
1101 1110 1010 1101 = 0xDEAD
1011 1110 1110 1111 = 0xBEEF
1010 0101 1010 0101 = 0xA5A5
Binary Hex
0000 0 0001 1 0010 2 0011 3 0100 4 0101 5 0110 6 0111 7 1000 8 1001 9 1010 A 1011 B 1100 C 1101 D 1110 E 1111 F
0x is a common
prefix for writing
numbers which means
hexadecimal
Separate binary code into groups of 4 bits (starting from the right)
Translate each group into a single hex digit
Hexadecimal

## Slide 11: Data Types
What kinds of data do computers use?
  Numbers – signed, unsigned, integers, floating point, complex, rational, irrational, …
  Text – characters, strings, …
  Images – pixels, colors, shapes, …
  Sound – pitch, amplitude, …
  Logical – true / false, open / closed, on / off, …
  Instructions – programs, …
  …
Data Types
What is a Data type?
  How is the data is represented
  What operations are valid for the data

## Slide 12: Some Important Data Types
Unsigned integers
  Only non-negative numbers
  0, 1, 2, 3, 4, …
Signed integers
  Negative, zero, positive numbers
  …, -3, -2, -1, 0, 1, 2, 3, …
Fixed point numbers
  Bounded negative, zero, positive numbers w/fraction
  -2.5, 0.0, 100.125, …
Floating point numbers
  Unbounded negative, zero, positive numbers w/fraction
  PI = 3.14159 x 100
Characters
  8-bit, unsigned integers
  ‘0’, ‘1’, ‘2’, … , ‘a’, ‘b’, ‘c’, … , ‘A’, ‘B’, ‘C’, … , ‘@’, ‘#’,
Data Types

## Slide 13: Integral Data Types

## Slide 14: Unsigned Integers
329
102
101
100
101
22
21
20
3x100 + 2x10 + 9x1 = 329
1x4 + 0x2 + 1x1 = 5
most
significant
least
significant
What do these unsigned binary numbers represent?
0000
0110
1111
1010
0001
1000
0111
1100
1011
1001
Computers use weighted positional notation
Unsigned
0
6
15
10
1
8
7
12
11
9

## Slide 15: Unsigned Binary Arithmetic
Base 2 addition – just like base 10!
  add from right to left, propagating carry
10010 10010 1111
+ 1001 + 1011 + 1
10111
+ 111
carry
Subtraction, multiplication, division,…
1
1
0
1
1
1
0
1
1
1
0
0
0
0
1
0
1
1
1
1
Unsigned

## Slide 16: Quiz 1.1
Number2 | Number10
00010101 | 
11111111 | 
01111111 | 
Convert the following unsigned binary numbers to their decimal equivalent:

## Slide 17: Data Types Matter!
On June 4, 1996 an unmanned Ariane 5 rocket launched by the European Space Agency exploded just forty seconds after lift-off. The rocket was on its first voyage, after a decade of development costing $7 billion. The destroyed rocket and its cargo were valued at $500 million.
Source: http://www.ima.umn.edu/~arnold/455.f96/disasters.html
On February 25, 1991, during the Gulf War, an American Patriot Missile battery in Dharan, Saudi Arabia, failed to intercept an incoming Iraqi Scud missile. The Scud struck an American Army barracks and killed 28 soldiers.

## Slide 18: Data Types Matter!
On July 23, 1983, at 41,000 feet somewhere over the Canadian countryside, Air Canada 143 suddenly was without fuel, despite its computers indicating there was plenty of fuel remaining in multiple tanks. With its fuel gone, so were its electrical and hydraulic systems and 767 jumbo jet had just become roughly the equivalent of a flying brick.
Fuel loading was miscalculated due to a misunderstanding of the recently adopted metric system which replaced the imperial system.
Source: http://en.wikipedia.org/wiki/Gimli_Glider

## Slide 19: Signed Integers
Integers of n bits have 2n distinct values
  Signed integer assign about half to positive integers (1 through 2n-1) and about half to negative (- 2n-1 through -1)
  that leaves two values: one for 0, and one extra
  MSB indicates sign: 0=positive, 1=negative
  Examples: Sign-magnitude, 1’s complement, and 2’s complement
Positive signed integers are treated just like unsigned – zero in most significant bit (MSB)
  00101 = 5
Negative signed integers have a one in the MSB
  sign-magnitude – 10101 = -5
  one’s complement – 11010 = -5
  two’s complement – 11011 = -5
Signed

## Slide 20: Sign-Magnitude Integers
Representations
  01111binary  15decimal
  11111  -15
  00000  0
  10000  -0
Range
  -(2(n-1)-1) to 2(n-1)-1
Problems
  Two representations of zero (+0 and –0)
  Arithmetic circuits are complex and cumbersome
  Negation/absolute value operations are easy, but addition/subtraction operations are difficult.
To negate a number,
toggle the sign bit.
Left-bit encodes sign:
0 = + (or 0)
1 = - (or 0)
Signed
Notes: Sign-Magnitude
Consists of an n bit unsigned magnitude and a sign bit. The definition of the sign bit is:
0: the integer is positive or zero; 1: the integer is negative or zero.
The integer represented in (n+1) bit sign-magnitude is
The range of values for an (n+1) bit sign-magnitude integer is to .
The format of an 8-bit sign-magnitude number is:
Some examples of 8-bit sign-magnitude numbers are shown below:
The range of an 8-bit sign-magnitude integer is -127 to +127.
There are different sign-magnitude representations for +0 and -0.
Sign reversal and absolute value operations are easy using sign-magnitude representation.
Adding the negative of a number is not the same as subtraction in sign-magnitude. Different operations must be defined for addition and subtraction with sign-magnitude numbers.

## Slide 21: 1’s Complement Integers
Representations
  00110binary  6decimal
  11001  -6
  00000  0
  11111  -0
Range
  -(2(n-1)-1) to 2(n-1)-1
Problems
  Two representations of zero (+0 and –0)
  Arithmetic circuits use binary addition with end-around carry (ie. resulting carry out of the most significant bit of the sum is added to the least significant bit of the sum.)
To negate a number,
invert number bit-by-bit.
Left-bit encodes sign:
0 = + (or 0)
1 = - (or 0)
Signed
Notes: One's Complement
In one's complement representation subtraction is performed by addition of a negative integer. This eliminates the need for a separate subtraction processor. As in sign-magnitude, the leftmost bit indicates the sign of an integer in complement representation. The representation for positive integers is the same as unsigned with the leftmost bit = 0.
Negative integers are formed by reversing all bits to form the bitwise complement of a positive integer. If I is the (n+1) bit binary sequence:
then -I in one's complement is given by:
where for all i.
Let I be a negative one's complement integer. The value of I is obtained by forming its one's complement:
since . Thus,
Negative one's complement integers are formed by subtracting a bias of from the positive integers. Taking into account the sign bit , the value for a positive or negative (n+1) bit one's complement integer is:
The range of values for an (n+1) bit one's complement integer is to .
Since the complement of 0 is , there are different representations for +0 and -0 in one's complement.
Examples of 8-bit one's complement numbers:
The range of 8-bit one's complement integers is -127 to +127.
Addition of signed numbers in one's complement is performed using binary addition with end-around carry. If there is a carry out of the most significant bit of the sum, this bit must be added to the least significant bit of the sum.
To add decimal 17 to decimal -8 in 8-bit one's complement:

## Slide 22: 2’s Complement Integers
Representation
  00110binary  6decimal
  11010  -6
  00000  0
  11111  -1
Range
  –2(n-1) to 2(n-1)-1
Simplifies logic circuit construction
  Addition is performed using simple binary addition
  Bottom line: simpler/faster hardware units!
To negate a number,
1’s complement + 1.
Left-bit encodes sign:
0 = + (or 0)
1 = -
Signed
Notes: Two's Complement
Two's complement representation has a single zero representation and eliminates the end-around carry operation required in one's complement addition. Positive two's complement integers have the same representation as unsigned numbers.
The additive inverse in two's complement is formed by taking the one's complement of a number and then adding 1 to the least significant bit.
Comparing this procedure to one's complement, it is easy to see that the value of an (n+1) bit two's complement integer is:
The range of values for an (n+1) bit two's complement integer is to .
Since the additive inverse of 0 is 0 in two's complement, the zero value has a unique representation.
To find the 8 bit two's complement representation of -8:
Examples of 8-bit two's complement numbers:
The range of 8-bit two's complement integers is -128 to +127.
Addition of signed numbers in two's complement is performed using simple binary addition.
To add decimal 17 to decimal -8 in 8-bit two's complement:
A carry out of the most significant bit is ignored in two's complement addition.

## Slide 23: 2’s Complement Integer
If number is positive or zero,
  normal binary representation
If number is negative,
  start with positive number
  flip every bit (i.e., take the one’s complement)
  then add one
00101 (5) 01001 (9)
11010 (1’s comp) (1’s comp)
+ 1 + 1
11011 (-5) (-9)
10110
10111
Signed

## Slide 24: 2’s Complement
Positional number representation with a twist
  the most significant (left-most) digit has a negative weight
  n-bits represent numbers in the range -2n-1 … 2n-1 - 1
What are these 2’s complement numbers?
0110 = 22 + 21 = 6
1110 = -23 + 22 + 21 = -2
0000
0110
1111
1010
0001
1000
0111
1100
1011
1001
Signed
0
6
-1
-6
1
-8
7
-4
-5
-7

## Slide 25: Quiz 1.2
Number10
What is the decimal number represented by the following binary digits?
101112
(unsigned)
(sign magnitude)
(1's complement)
(2's complement)

## Slide 26: 2’s Complement Shortcut
To take the two’s complement of a number:
  copy bits from right to left until (and including) the first “1”
  flip remaining bits to the left
011010000 011010000
100101111 (1’s comp)
+ 1
100110000 100110000
(copy)
(flip)
Signed

## Slide 27: 2’s Complement Binary Addition
Rules of Binary Addition:
  0 + 0 = 0
  0 + 1 = 1
  1 + 0 = 1
  1 + 1 = 0, with carry
Two's complement addition follows the same rules as binary addition.
Two's complement subtraction is the binary addition of the minuend to the 2's complement of the subtrahend (adding a negative number is the same as subtracting a positive one).
5 + (-3) = 2 0000 0101 = +5
+ 1111 1101 = -3
--------- --
0000 0010 = +2
Signed
0000
1000
0100
1100
0010
1010
0110
1110
0001
1111
1101
1011
1001
0111
0101
0011
0
-8
4
-4
1
2
3
5
6
7
-7
-6
-5
-3
-2
-1
+
-

## Slide 28: 2’s Complement Overflow
Overflow = the result doesn’t fit in the capacity of the representation
ALU’s are designed to detect overflow
It’s really quite simple
  if the carry in to the most significant position (MSB) is different from the carry out from the most significant position (MSB), then overflow occurred.
Generally, overflow is only reported as a CPU status bit
NOTE: CARRY OUT IS NOT OVERFLOW!
Overflow
00100110
+ 11101101
38
-19
19
100010011
00100110
+ 01101101
38
109
-109
010010011
carry
carry

## Slide 29: 2’s Complement Overflow
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1011
1100
1101
1010
1110
1111
0
1
2
3
4
5
6
7
8
9
A
D
C
B
E
F
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
-8
3
4
5
6
7
2
-7
-6
-5
-4
-3
-2
-1
Overflow

## Slide 30: Quiz 1.3
Fill in the 3 boxes using the appropriate data type arithmetic:
What data type uses the same arithmetic logic as an unsigned integer?
Which data type has the simplest arithmetic logic?
00100110
+ 11101101
Signed-Magnitude
1’s Complement
2’s Complement
00100110
+ 11101101
00100110
+ 11101101

## Slide 31: Review: Numbers…
7
6
5
4
3
2
1
0
-1
-2
-3
-4
111
110
101
100
011
010
001
000
011
010
001
000, 100
101
110
111
011
010
001
000, 111
110
101
100
011
010
001
000
111
110
101
100
Un-signed
Signed Magnitude
1’s Complement
2’s Complement
Range:
0 to 7
-3 to 3
-3 to 3
-4 to 3
Review
10110 = 101
101unsigned = 5
101signed magnitude = -1
1011’s complement = -2
1012’s complement = -3

## Slide 32: 2’s Complement Sign-Extension
You can make a number wider by simply replicating its leftmost bit as desired.
0110 =
000000000000000110 =
1111 =
11111111111111111 =
1 =
6
6
-1
-1
-1
What is the decimal value of the following 2’s complement numbers?
Sign-Extension
All the same!
(Sign-extended values)

## Slide 33: Decimal to Binary Conversion
Continually divide the number by 2 and prepend the remainders until zero.
1  25 + 0  24 + 1  23 + 0  22 + 1  21 + 1  20
32 + 0 + 8 + 0 + 2 + 1
= 43
43
2
2
2
2
2
2
5 R 0
0
2 R 1
1
21 R 1
1
10 R 1
1
1 R 0
0
0 R 1
1
Conversions
Do a 2’s complement to negate number:
-(0101011) = 1010101
Prepend a zero.
0

## Slide 34: Quiz 1.4
Number10 | Binary (2’s complement)
5 | 
123 | 
-35 | 
Convert the following decimal numbers to their 8-bit, 2’s complement binary number equivalent:

## Slide 35: Pre-class Quiz…
What’s wrong with this C computer program?
What might be wrong with this picture?
int main()
{
unsigned char i, sum = 0;
for (i = 0; i < 1000; i++)
{
sum = sum + i;
}
}

## Slide 36: Fractional Data Types

## Slide 37: Fixed Point Numbers
Bounded negative, zero, positive numbers w/fraction
  Fractions are created by dividing a binary number into an integral and fractional part
  The program is responsible for knowing the position of the “decimal point”
  Signed or un-signed
  Requires less processing resources than floating-point
Fixed Point
Decimal Point
Fractional Part
Whole or integral Part
0
0
0
0
0
1
1
0
0
0
0
0
0
0
0
0
2-6
2-5
2-4
2-3
2-2
2-1
20
21
22
23
24
25
26
27
28
-29
= 1.5

## Slide 38: Fixed Point Numbers
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
With a fixed-point fractional part, we can have 5/2 = 2.5
The more bits you use in your fractional part, the more accuracy you will have.
Uses 2’s complement for negative numbers.
Accuracy is 2 -(# fraction bits).
For example, if we have 6 bits in our fractional part (like the above example), our accuracy is 2-6 = 0.015625. In other words, every bit is equal to 0.015625
Fixed Point
Intregal part
Fractional part

## Slide 39: Fixed Point Arithmetic
Adding 2.5 + 2.5
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
Fixed point addition:
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
0
0
0
0
0
1
0
1
0
0
0
0
0
0
0
0
+
= 5
Fixed Point
Without fixed point math the result would have been 4 due to the truncation of the integer division.
Faster, easier than any other fractional data type.

## Slide 40: Floating Point Numbers
Numbers such as , e, cannot be expressed by a fixed number of significant figures.
Computers use a base-2 representation, they cannot precisely represent certain exact base-10 numbers.
Fractional quantities are typically represented in computer using “floating point” form, e.g.,
Floating Point
Number = -1s  1.fraction  2(exponent – 127)
Mantissa
0.5 <= m < 1
Base

## Slide 41: Floating Point Numbers
Unbounded negative, zero, positive numbers w/fraction
  Binary scientific notation
  IEEE 754 Standard - 32 / 64 bit floating point
  Exponent is biased by 127 (2e-1 – 1)
  Implied leading 1 in mantissa (fraction or significand)
  Zero represented by all 0’s
  Denormalized, infinity, NaN
Floating Point
s
exponent
fraction
1
8
23
N = -1s  1.fraction  2(exponent – 127)

## Slide 42: Normalizing Floating Point
Scientific Notation
  0.00123  103 = 1.23
  0.01230  102 = 1.23
  0.12300  101 = 1.23
Base 2 equivalences
  0.0112  2(129-127) = .375  22 = 1.5
  0.1102  2(128-127) = .75  21 = 1.5
  1.1002  2(127-127) = 1.5  20 = 1.5
Floating point normalization
  Fraction is shifted left (decrementing exponent) until greater than 1 – then the 1 is dropped.
  Allows for one more binary bit of precision.
Floating Point
s
exponent
fraction
1
8
23
N = -1s  1.fraction  2(exponent – 127)
1 is assumed
and not stored
in number.

## Slide 43: Floating Point Numbers
Exponent is 129 – 127 = 2
Fraction is 1.10101 = 20 + 2-1 + 2-3 + 2-5
= 1 + 1/2 + 1/8 + 1/32 = 1.65625
Negative
The final number is -1.65625 x 22 = -6.625
What does this represent?
The final number is 1.5 x 21 = 3.0
0 10000000 10000000000000000000000
Floating Point
1 10000001 10101000000000000000000
And this one?
Exponent is 128 – 127 = 1
Fraction is 1.1 = 20 + 2-1 = 1 + 1/2 = 1.5
Positive

## Slide 44: Quiz 1.5 – FP to Decimal
What is the decimal equivalent of the following signed, 16-bit (8 bit fraction), fixed point number?
Fractional Part
Integral Part
0
0
0
0
1
1
0
1
1
1
1
0
1
0
0
0
2-8
2-7
2-6
2-5
2-4
2-3
2-2
2-1
20
21
22
23
24
25
26
-27
=
What is the decimal equivalent of the following 32-bit floating point number?
1 10000011 11000000000000000000000 =
s
exponent
fraction
1
8
23
N = -1s  1.fraction  2(exponent – 127)

## Slide 45: Decimal to Floating Point
To convert a decimal number to binary IEEE 754 floating point:
  Convert the absolute value of the decimal number to a binary integer plus a binary fraction.
  Normalize the number in binary scientific notation to obtain fraction and exponent.
  Bias exponent by 127, set s=0 for a positive number and s=1 for a negative number, and combine.
Floating Point
s
exponent
fraction
1
8
23
N = -1s  1.fraction  2(exponent – 127)
Example: convert 22.625 to FP
  1. Convert decimal 22 to binary:
    2210 = 101102
  2. Convert decimal 0.625 to binary:
    0.62510 = 0.1012
  3. Combine integer and fraction:
    10110.1012  20
  4. Normalize:
    10110.1012  20
    1011.01012  21
    101.101012  22
    10.1101012  23
    1.01101012  24
  5. Bias exponent, drop the leading bit, and combine sign, exponent, and fraction:
    0 10000011 01101010000000000000000

## Slide 46: Quiz 1.6 – Decimal to FP
Fractional Part
Integral Part
2-10
2-9
2-8
2-7
2-6
2-5
2-4
2-3
2-2
2-1
20
21
22
23
24
-25
1. Convert the following decimal number to a 2’s complement, 16-bit (Q6.10) fixed point number.
-25.8125 =
 | 2(exponent – 127) |  |  |  |  |  |  |  | (1).Fraction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
What is the IEEE 754 binary floating point equivalent of the following decimal number?
-37.375 =
HINT: 0.8125 = 1/2 + 1/4 + 1/16)
HINT: 0.375 = 1/4 + 1/8)

## Slide 47: FP Behavior
Programmer must be aware of accuracy limitations!
  =? 1 + (1030 + –1030)
  =? 1 + 0
   1
  =? (1.0 ÷ 640.0) + (6.0 ÷ 640.0)
  =? .001563 + .009375
   .010938
  (1 + 1030) + –1030
  1030 – 1030
  0
  (1.0 + 6.0) ÷ 640.0
  7.0 ÷ 640.0
  .010937
Operations not associative!
×,÷ not distributive across +,-

## Slide 48: Chopping vs. Rounding
Base 10 pi=3.14159265358…
Chopped pi=3.141592 et=0.00000065
Rounded pi=3.141593 et=0.00000035
Some machines use chopping, because rounding adds to the computational overhead. Since number of significant figures is large enough, resulting chopping error is usually negligible.

## Slide 49: Other Data Types

## Slide 50: ASCII Codes
The American Standard Code for Information Interchange (ASCII) is a character-encoding scheme based on the ordering of the English alphabet.
  Represent text in computers
  7-bit, unsigned integers
  1st 32 codes unprintable
  Developed from teletype
ASCII Characters

## Slide 51: Unicode Codes
Unicode is a computing industry standard for the consistent encoding, representation and handling of text expressed in most of the world's writing systems.
Latest version of Unicode contains a repertoire of more than 110,000 characters covering 100 scripts.
  0000-001F Control Characters
  0020-00FF Latin (ASCII + extended)
  0250-02AF IPA Extentions
  0300-036F Diacritical Marks
  0400-052F Cyrillic (Russian, Ukrainian, Bulgarian)
  0530-058F Armenian
  0590-05FF Hebrew (Hebrew, Yiddish)
  0600-077F Arabic (Arabic, Persian, Kurd, Syrian)
  0780-07BF Thaana (Maldivian)
  07C0-07FF Nko
  0800-083F Samaritan
  0840-085f Mandaic
Unicode Characters
Mandraic
Devanagari (sanskrit, hindi)
Bengali
Gujarati (abugida)
Oriya
Telugu
Malayalam
Thai
Lao
Tibetab
Georgian
Hangul Jamo
…

## Slide 52: Additional Data Types
Proposed C fixed-point
  ISO/IEC 9899:1999
  #include <stdfix.h>
  _Fract, _Accum
  TI: UQ8.8
bool (added to C in 1999)
enums
Complex
BCD
EBCDIC
Data Types

## Slide 53: MSP430 C Variable Data Types
Type | Size | Representation | Minimum | Maximum
char, signed char | 8 bits | ASCII | -128 | 127
unsigned char | bool 8 bits | ASCII | 0 | 255
short, signed short | 16 bits | 2's complement | -32768 | 32767
unsigned short | 16 bits | Binary | 0 | 65535
int, signed int | 16 bits | 2's complement | -32768 | 32767
unsigned int | 16 bits | Binary | 0 | 65535
long, signed long | 32 bits | 2's complement | -2,147,483,648 | 2,147,483,647
unsigned long | 32 bits | Binary | 0 | 4,294,967,295
enum | 16 bits | 2's complement | -32768 | 32767
float | 32 bits | IEEE 32-bit | 1.175495e-38 | 3.4028235e+38
double | 32 bits | IEEE 32-bit | 1.175495e-38 | 3.4028235e+38
long double | 32 bits | IEEE 32-bit | 1.175495e-38 | 3.4028235e+38
pointers, references | 16 bits | Binary | 0 | 0xFFFF
function pointers | 16 bits | Binary | 0 | 0xFFFF
C

## Slide 54: Data Storage
Little and Big Endian
  Storage order for larger data types
  Little endian – least significant bits stored first (lower address)
Address | 0x0200 | 0x0201 | 0x0202 | 0x0203 | …
Little endian: | 0x34 | 0x12 | 0x78 | 0x56 | …
Big endian: | 0x12 | 0x34 | 0x56 | 0x78 | …
0x1234, 0x5678
Word size is the natural unit of data used by a particular computer design and usually refers to:
  Size of registers
  Amount of data transferred to/from memory in single operation
  Largest possible address
  Number of bits processed in a single operation
  Base word size (Intel 32/64 bit, MPS430 is 16-bits)
When accessing/storing a 16-bit
word, the least significant byte
is first (lower) in memory.
0x34 0x12
0x12 0x34

## Slide 55: Data Alignment / Padding
Data structure alignment is the way data is arranged and accessed in computer memory.
  Data alignment and data structure padding. When a modern computer reads from or writes to a memory address, it will do this in word sized chunks (e.g. 4 byte chunks on a 32-bit system) or larger. Data alignment means putting the data at a memory offset equal to some multiple of the word size, which increases the system's performance due to the way the CPU handles memory.
  To align the data, it may be necessary to insert some meaningless bytes between the end of the last data structure and the start of the next, which is data structure padding.

## Slide 56: Type Casting
In binary operations (e.g., +, -, /, etc.) with operands of mixed data types, the resultant data type will take the higher order data type of the two operands1
Data type conversion
  Casting – explicitly convert a variable (expression) from one data type to another data type.
  Promotion or data coercion – implicitly change a “smaller” data type into a “larger” data type.
long double
double
float
unsigned long long
long long
unsigned long
long
unsigned int
int
unsigned short
short
unsigned char
char
Higher
Lower

## Slide 57: Choosing a Data Type
Loop counter
Gender
# of CD’s
Sound amplitude
Pi
GPA
GPS Coordinates
Bank account
Message
Population
Real numbers (physical)
unsigned int
Boolean, char, int
unsigned int
int (2’s complement)
float
Fixed point
float
int, Fixed point
ASCI Text
int
float

## Slide 58: Summary / Review

## Slide 59: Review: Representation
Everything is stored in memory as one’s and zero’s
  integers, floating point numbers, characters
  program code
Data Type = Representation + Operations
You can’t tell what is what just by looking at the binary representation
  memory could have multiple meanings
  it is possible to execute your Word document
Review

## Slide 60: Review: Integral Numbers…
7
6
5
4
3
2
1
0
-1
-2
-3
-4
111
110
101
100
011
010
001
000
011
010
001
000, 100
101
110
111
011
010
001
000, 111
110
101
100
011
010
001
000
111
110
101
100
Un-signed
Signed Magnitude
1’s Complement
2’s Complement
Range:
0 to 7
-3 to 3
-3 to 3
-4 to 3
Review

## Slide 61: Review: Fractional Numbers…
Review
s
exponent
fraction
1
8
23
N = -1s  1.fraction  2(exponent – 127)
Fractional Part
Whole or integral Part
0
0
0
0
1
1
0
1
1
1
1
0
1
0
0
0
2-8
2-7
2-6
2-5
2-4
2-3
2-2
2-1
20
21
22
23
24
25
26
-27
Fixed Point
  Bounded, whole/fraction
  Positional 2’s complement
  Integral binary operations
Floating Point
  Unbounded, Sign-magnitude
  IEEE 754 standard
  Normalized, implied 1
  Exponent biased by 127
  Special infinity, zero, NaN
  Range: 1.18  10-38 to 3.4  1038

## Slide 62: float's vs int's
Review

## Slide 63: Quiz 1.7
00000110 (signed magnitude)
+ 10001101 (signed magnitude)
(signed magnitude)
(1’s complement)
+ 00000010 (1’s complement)
(1’s complement)
(2’s complement)
+ 00100101 (2’s complement)
(2’s complement)
(decimal10)