## Slide 1: S03: Instruction Set Architecture
Required: PM: Ch 7.1-3, pgs 81-95 MSP430 Disassembly.html Code: Chs 18-19, pgs 238-285
Recommended: Introduction to TI MSP430 Launchpad Tutorial MSP430 User's Guide (3.0-3)

## Slide 2: CS 224
Chapter | Lab | Homework
S00: Introduction |  | 
Unit 1: Digital Logic |  | 
S01: Data Types S02: Digital Logic | L01: Warm-up L02: FSM | HW01 HW02
Unit 2: ISA |  | 
S03: ISA S04: Microarchitecture S05: Stacks / Interrupts S06: Assembly | L03: Blinky L04: Microarch L05b: Traffic Light L06a: Morse Code | HW03 HW04 HW05 HW06
Unit 3: C |  | 
S07: C Language S08: Pointers S09: Structs S10: I/O | L07b: Morse II L08a: Life L09b: Snake | HW07 HW08 HW09 HW10

## Slide 3: Learning Outcomes…
After discussing Instruction Set Architecture and studying the reading assignments, you should be able to:
Explain what is a computer architecture.
Describe the differences between a Harvard and von Neumann machine.
Describe the differences between a RISC and CISC machine.
Explain the addressing modes of the MSP430.
Discuss computer instruction cycles.
Disassemble MSP430 instructions.

## Slide 4: Topics to Cover…
ISA
Von Neumann vs. Harvard
RISC vs.CISC
Computer Instructions
MSP430 ISA
  MSP430 Registers
  MSP430 ALU
Assembler Primer
MSP430 Instructions
  Double Operand
  Single Operand
  Jump
Addressing Modes
Instruction Length
Clock Cycles
Instruction Disassembly

## Slide 5: Instruction Set Architecture
The computer ISA defines all the programmer-visible components and operations of the computer
  Memory organization
    address space -- how may locations can be addressed?
    addressibility -- how many bits per location?
  Register set
    how many? what size? how are they used?
  Instruction set
    opcodes
    data types
    addressing modes
ISA provides all information needed for someone that wants to write a program in machine language (or translate from a high-level language to machine language).
ISA

## Slide 6: Harvard Architecture
Von Neumann vs. Harvard
DATA
MEMORY
INSTRUCTION
MEMORY
CLOCK
IN
OUT
Control
Status
Instruction
Control & Address
Data
ALU
CONTROL
The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data.
Examples:
8051
Atmel AVR
ARM

## Slide 7: The Von Neumann Computer
OUTPUT
* monitor
* printer
* LEDs
* D/A
* disk
INPUT
* keyboard
* mouse
* scanner
* A/D
* serial
* disk
PROCESSING UNIT
Program Counter
Instruction Register
MEMORY
ALU
Registers
Control
Datapath
Von Neumann proposed this model in 1946
The Von Neumann model: Program instructions and Data are both stored as sequences of bits in computer memory
Address Bus
Data Bus
Clock
Control
Logic
Von Neumann vs. Harvard
Examples:
Cray
PC’s
MSP430
Notes: John von Neumann ( /vɒn ˈnɔɪmən/; December 28, 1903 – February 8, 1957) was a Hungarian-American mathematician and polymath who made major contributions to a vast number of fields,[1] including mathematics (set theory, functional analysis, ergodic theory, geometry, numerical analysis, and many other mathematical fields), physics (quantum mechanics, hydrodynamics, and fluid dynamics), economics (game theory), computer science (linear programming), and statistics. He is generally regarded as one of the greatest mathematicians in modern history.[2]
As a 6 year old, he could divide two 8-digit numbers in his head.[14] By the age of 8, he was familiar with differential and integral calculus.[

## Slide 8: MSP430 Architecture
Von Neumann
Instructions
and Data
Input / Output
Processing
Unit (CPU)

## Slide 9: RISC / CISC Architecture
Single-clock
Reduced instructions
No microcode
Data explicitly accessed
Easier to validate
Larger code sizes (~30%)
Low cycles/second
More transistors on memory registers
Pipelining friendly
Emphasis on software
Multi-clock
Complex instructions
Complicated microcode
Memory to memory operations
Difficult to validate
Smaller code sizes
High cycles/second
More transistors for complex instructions
Compiler friendly
Emphasis on hardware
CISC
RISC
RISC vs. CISC

## Slide 10: RISC/CISC Instruction Set
MSP430
(RISC)
IA-32 (CISC)
Logical
Arithmetic
Jump
Special
27 Instructions
RISC vs. CISC

## Slide 11: Quiz 3.1
  Compiler friendly
  Larger code sizes (~30%)
  Complicated microcode
  Fewer instructions
  Easier to validate
  Emphasis on hardware
  Emphasis on software
  Memory to memory operations
  Pipelining friendly
What best differentiates RISC and CISC architectures?
RISC
CISC

## Slide 12: Computer Instructions

## Slide 13: Computer Instructions
Computer program consists of a sequence of instructions
  instruction = verb + operand(s)
  stored in memory as 1’s and 0’s
  called machine code.
Instructions are fetched from memory
  The program counter (PC) holds the memory address of the next instruction (or operand).
  The instruction is stored internal to the CPU in the instruction register (IR).
Programs execute sequentially through memory
  Execution order is altered by changing the Program Counter.
  A computer clock controls the speed and phases of instruction execution.
Computer Instructions

## Slide 14: Machine vs Assembly Code
Computer Instructions
Disassembler
0100000100111111
0000011000000000
0100000010110010
0100001100001110
0101001101011110
1111000001111110
0001001000110000
1000001110010001
0010001111111101
0100000000110001
0101101000011110
0000000100100000
0000000000001111
0000000000001110
0000000000000000
Machine Code
mov.w #0x0600,r1
mov.w #0x5a1e,&0x0120
mov.w #0,r14
add.b #1,r14
and.b #0x0f,r14
push #0x000e
sub.w #1,0(r1)
jne $-4
mov.w @r1+,r15
Assembly Code
Assembler

## Slide 15: Anatomy of Machine Instruction
“Add the value in Register 4 to the value in Register 5”
Computer Instructions
2. 1st object – Source Operand
3. 2nd object – Destination Operand
1. Verb – Opcode (0, 1, or 2 operands)
0101010000000101
add r4,r5
How many
instructions are
possible with a
4-bit op-code?
How many
source/destination
registers can
selected with a
4-bit field?

## Slide 16: Instruction Addressing Modes
Machine language instructions operate (verb) on operands (objects).
Addressing modes define how the computer identifies the operand (or operands) of each instruction.
Operands are found in
  registers,
  instructions, or
  memory.
Memory operands are accessed
  directly,
  indirectly (pointer), or
  indexed.
Computer Instructions

## Slide 17: Today’s Microcontrollers…
Intel 4004 | TinyDuino
Z80 | DigiSpark
6502 | Arduino Yun
Microchip PIC | BLEduino
Parallax BASIC STAMP | Geogram One
Arduino | Raspberry PI
Tessel | BeagleBone
LaunchPad MSP430 | PCDuino
Picaxe-28X2 Shields | AMD Gizmo Board
Netduino | Lilypad
Parallax Propeller | Papilio One FPGA

## Slide 18: LaunchPad vs Arduino
TI MSP430
  Von Neumann
  16-bit RISC/CISC
  27 Instructions
  16 16-bit orthogonal Registers
  16-bit ALU
  Up to 24 MHz
  1.2 - 3.3 volt
  Active Mode:
  Power-down:
Atmega8/168
  Harvard architecture
  8-bit RISC
  131 Instructions
  32 8-bit address/data Registers
  8-bit ALU
  1 - 20 MHz (20 MIPS)
  5 volt
  Active Mode: 0.2 mA
  Power-down Mode: 0.1 μA

## Slide 19: MSP430 ISA

## Slide 20: MSP430 ISA
RISC/CISC machine
  27 orthogonal instructions
    8 jump instructions
    7 single operand instructions
    12 double operand instructions
  4 basic addressing modes.
  8/16-bit instruction addressing formats.
Memory architecture
  16 16-bit registers
  16-bit Arithmetic Logic Unit (ALU).
  16-bit address bus (64K address space)
  16-bit data bus (8-bit addressability)
  8/16-bit peripherals
MSP430 ISA

## Slide 21: MSP430 Bus Architecture
Memory Data Bus (bi-directional)
  Addressability = # of bits stored in each memory location (8-bits).
  Memory Select (MSEL) connects an addressed memory location to the data bus.
  Memory Write Enable (MWE) is asserted when writing to memory.
  CPU addresses data values either as bytes (8 bits) or words (16 bits). Words are always addressed at an even address (least significant byte), followed by the next odd address (significant byte) which is little endian.
Memory Address Bus (uni-directional)
  Address Space = number of possible
  memory locations (memory size)
  Memory Address Register (MAR) stores
  the memory address for the address bus
  Addresses peripherals as well as memory.
MSP430 ISA

## Slide 22: MSP430 Memory Architecture
Input / Output
  Used to get information in and out of the computer.
  External devices attached to a computer are called peripherals.
  Lower 512 bytes (0x0000 - 0x01FF) of address space
Memory
  64k byte addressable, address space
  (0x0000 - 0xFFFF)
  Flash / ROM – Used for both code/data
    Interrupt vectors - Upper 16 words
  RAM (0x200 - 0x9FF) – Volatile storage
  Peripherals
    16-bit peripherals (0x0100 - 0x01FF)
    8-bit peripherals (0x0010 - 0x00FF)
    Special Function Registers – Lower 16 bytes
Flash (ROM)
RAM
I/O
0x0000
0xFFFF
MSP430 ISA

## Slide 23: MSP430 ALU Architecture
Sixteen 16-bit registers
  Program Counter (R0), Stack Pointer (R1), Status Register (R2)
  Constant Generator (R3), General Purpose Registers (R4-R15)
  Very fast memory - close to the ALU (register file).
ALU (Arithmetic and Logic Unit)
performs the arithmetic and logical
operations
  Arithmetic operations: add, subtract
  Logical operations: and, xor, bit
  Sets condition codes
  The word length of a computer is the
  number of bits processed by the ALU.
MSP430 ISA

## Slide 24: MSP430 ALU
16 bit Arithmetic Logic Unit (ALU).
  Performs instruction arithmetic and logical operations.
  Instruction execution may affect the state of the following status bits:
    Zero (Z)
    Carry (C)
    Overflow (V)
    Negative (N)
  The MCLK (Master) clock signal drives the CPU and ALU logic.
MSP430 ALU

## Slide 25: MSP430 Registers
MSP430 Registers
Register | Name | Function
R0 (PC) | Program Counter | Address of next instruction to be fetched. LSB is always zero. Incremented by 2, 4, or 6
R1 (SP) | Stack Pointer | Return address of calls and interrupts Programs local data “Grows down” thru RAM LSB is always zero.
R2 (SR/CG1) | Status Register | Carry, negative, zero, overflow status bits Interrupt enable Power mode Constant generator for 4, 8 (CG1)
R3 (CG2) | Constant Generator | Constant generator for -1, 0, 1, 2
R4-R15 | General Purpose | 

## Slide 26: MSP430 Control Architecture
Clock
  System and peripheral clocks
Control Unit
  The control unit directs the execution of
  the program
  The Program Counter (R0) or PC points to the next instruction to be executed
  The Instruction Register or IR contains
  the current executing instruction
  The Status Register (R2) or SR contains
  information about the last instruction
  executed as well as system parameters
  The control unit prevents bus conflicts and timing/propagation problems
  The control unit is a Finite State Machine driven by a clock
MSP430 ISA

## Slide 27: MSP430 Ports
Computer communicates with external world thru 8 bit memory locations called Ports.
  Each Port bit is independently programmable for Input or Output.
  Edge-selectable input interrupt capability (P1/P2 only) and programmable pull-up/pull-down resistors available.
Port Registers
  PxIN – read from port
  PxOUT – write to port
  PxDir – set port direction (input or output)
MSP430 Ports

## Slide 28: Quiz 3.2
1. What is an ISA?
2. What is a memory address space?
3. What is memory addressability?
4. What is a computer port?
5. List some distinctive properties of the MSP430 ISA.

## Slide 29: Assembly Primer

## Slide 30: MSP430 Assembler
A typical assembly language line has four parts:
  label—starts in the column 1 and may be followed by a colon (:) for clarity.
  operation—either an instruction, which is translated into binary machine code for the processor itself, or a directive, which controls the assembler.
  operands—data needed for this operation (not always required).
  comment—text following a semicolon (;).
start: | mov.w | #0x0280,sp | ; setup stack pointer
Label: | Operation | Operands | Comment
Assembler Primer

## Slide 31: MSP430 Assembler
Labels are case sensitive, but instructions and directives are not - pick a style and stick with it.
Use comments freely in assembly language – otherwise your program is unreadable and very difficult to debug.
The default base (radix) of numbers in assembly language is decimal. The C-style notation 0xA5 for hexadecimal numbers is now widely accepted by assemblers. Other common notations include $A5, h'A5' and 0A5h. Binary numbers can similarly be written as 10100101b.
Use symbolic names for constants and expressions. The ".equ" and ".set" assembler directives provide macro text replacement for this purpose. (Make upper case.)
Assembler Primer

## Slide 32: Assembler Coding Style
Assembler Primer
;*************************************************************************
; CS/ECEn 124 Lab 1 - blinky.asm: Software Toggle P1.0
;
; Description: Toggle P1.0 by xor'ing P1.0 inside of a software loop.
;*************************************************************************
DELAY .equ 0
.cdecls C,"msp430.h" ; MSP430
.text ; beginning of executable code
reset: mov.w #0x0280,SP ; init stack pointer
mov.w #WDTPW+WDTHOLD,&WDTCTL ; stop WDT
bis.b #0x01,&P1DIR ; set P1.0 as output
mainloop: xor.b #0x01,&P1OUT ; toggle P1.0
mov.w #DELAY,r15 ; use R15 as delay counter
delayloop: sub.w #1,r15 ; delay over?
jnz delayloop ; n
jmp mainloop ; y, toggle led
.sect ".reset" ; MSP430 RESET Vector
.word reset ; start address
.end
Labels start in column 1 and are 10 characters or fewer.
Instructions / DIRECTIVES start in column 12.
Operands start in column 21.
Comments start in column 45.
Use macros provided in the MSP430 header file.
The ".cdecls" directive inserts a header file into your program.
Assembler directives begin with a period (.)
The ".end" directive is the last line of your program.
Instructions are lower case and macros are UPPER CASE.
No line should exceed 80 characters.
Begin writing your assembly code after the ".text" directive.

## Slide 33: MSP430 Instructions

## Slide 34: MSP430 Instructions
The first 4-bits (nybble) of an instruction is called the opcode and specifies not only the instruction but also the instruction format.
The MSP430 ISA uses three formats to encode instructions for processing by the CPU core: double operand, single operand, and jumps.
Single and double operand instructions process word (16-bits) or byte (8-bit) data operations. (Default is word)
Complete orthogonal instruction set – Although the MSP430 architecture implements only 27 instructions, every instruction is usable with every addressing mode throughout the entire memory map.
High register count, page free, stack processing, memory to memory operations, constant generator.
Instruction Formats

## Slide 35: MSP430 Instructions
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Instruction Register
Memory |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
mov.w r5,r4
rrc.w r5
jc main
mov.w #0x0600,r1
Opcode | Instruction | Format
0000 | Undefined | Single Operand
0001 | RCC, SWPB, RRA, SXT, PUSH, CALL, RETI | 
0010 | JNE, JEQ, JNC, JC | Jumps
0011 | JN, JGE, JL, JMP | 
0100 | MOV | Double Operand
0101 | ADD | 
0110 | ADDC | 
0111 | SUBC | 
1000 | SUB | 
1001 | CMP | 
1010 | DADD | 
1011 | BIT | 
1100 | BIC | 
1101 | BIS | 
1110 | XOR | 
1111 | AND | 
1111
1110
1101
1100
1011
1010
1001
1000
0111
0110
0101
0100
0011
0010
0001
0000
4 to 16 Decoder
Opcode
Program Counter
MSP430 Instructions
R0
1 cycle needed to
fetch instruction

## Slide 36: MPS430 Instruction Formats
Format I: Instructions with two operands:
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
MSP430 Instructions
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode (4 + 5 bits) |  |  |  |  |  |  |  |  | b/w | As |  | D/S-reg |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode (4 + 2 bits) |  |  |  |  |  | 10-bit, 2’s complement PC offset |  |  |  |  |  |  |  |  | 
Format II: Instruction with one operand:
Format III: Jump instructions:

## Slide 37: Format I: Double Operand
Double operand instructions:
Mnemonic | Operation | Description
Arithmetic instructions |  | 
ADD(.B or .W) src,dst | src+dstdst | Add source to destination
ADDC(.B or .W) src,dst | src+dst+Cdst | Add source and carry to destination
DADD(.B or .W) src,dst | src+dst+Cdst (dec) | Decimal add source and carry to destination
SUB(.B or .W) src,dst | dst+.not.src+1dst | Subtract source from destination
SUBC(.B or .W) src,dst | dst+.not.src+Cdst | Subtract source and not carry from destination
Logical and register control instructions |  | 
AND(.B or .W) src,dst | src.and.dstdst | AND source with destination
BIC(.B or .W) src,dst | .not.src.and.dstdst | Clear bits in destination
BIS(.B or .W) src,dst | src.or.dstdst | Set bits in destination
BIT(.B or .W) src,dst | src.and.dst | Test bits in destination
XOR(.B or .W) src,dst | src.xor.dstdst | XOR source with destination
Data instructions |  | 
CMP(.B or .W) src,dst | dst-src | Compare source to destination
MOV(.B or .W) src,dst | srcdst | Move source to destination
Double Operand Instructions

## Slide 38: Example: Double Operand
Copy the contents of a register to another register
  Assembly: mov.w r5,r4
  Instruction code: 0x4504
One word instruction
The instruction instructs the CPU to copy the 16-bit 2’s complement number in register r5 to register r4
Opcode mov | S-reg r5 | Ad Register | b/w 16-bits | As Register | D-reg r4
0 1 0 0 | 0 1 0 1 | 0 | 0 | 0 0 | 0 1 0 0
Double Operand Instructions

## Slide 39: Format II: Single Operand
Single operand instructions:
Mnemonic | Operation | Description | 
Logical and register control instructions |  |  | 
RRA(.B or .W) dst | MSBMSB… LSBC | Roll destination right | 
RRC(.B or .W) dst | CMSB…LSBC | Roll destination right through carry | 
SWPB( or .W) dst | Swap bytes | Swap bytes in destination | 
SXT dst | bit 7bit 8…bit 15 | Sign extend destination | 
PUSH(.B or .W) src | SP-2SP, src@SP | Push source on stack | 
Program flow control instructions |  |  | 
CALL(.B or .W) dst | SP-2SP, PC+2@SP dstPC |  | Subroutine call to destination
RETI | @SP+SR, @SP+SP |  | Return from interrupt
Single Operand Instructions

## Slide 40: Example: Single Operand
Logically shift the contents of register r5 to the right through the status register carry
  Assembly: rrc.w r5
  Instruction code: 0x1005
One word instruction
The CPU shifts the 16-bit register r5 one bit to the right (divide by 2) – the carry bit prior to the instruction becomes the MSB of the result while the LSB shifted out replaces the carry bit in the status register
Opcode rrc | b/w 16-bits | As Register | D/S-reg r5
0 0 0 1 0 0 0 0 0 | 0 | 0 0 | 0 1 0 1
Single Operand Instructions

## Slide 41: Jump Instruction Format
Jump instructions are used to direct program flow to another part of the program (by changing the PC).
The condition on which a jump occurs depends on the Condition field consisting of 3 bits:
  000: jump if not equal
  001: jump if equal
  010: jump if carry flag equal to zero
  011: jump if carry flag equal to one
  100: jump if negative (N = 1)
  101: jump if greater than or equal (N = V)
  110: jump if lower (N  V)
  111: unconditional jump
Jump Instructions
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode + Condition |  |  |  |  |  | 10-bit, 2’s complement PC offset |  |  |  |  |  |  |  |  | 

## Slide 42: Jump Instruction Format
Jump instructions are executed based on the current PC and the status register
Conditional jumps are controlled by the status bits
Status bits are not changed by a jump instruction
The jump off-set is represented by the 10-bit, 2’s complement value:
Thus, the range of the jump is -511 to +512 words, (-1023 to 1024 bytes ) from the current instruction
Note: Use a BR instruction to jump to any address
Jump Instructions

## Slide 43: Example: Jump Format
Continue execution at the label main if the carry bit is set
  Assembly: jc main
  Instruction code: 0x2fe4
One word instruction
The CPU will add to the incremented PC (R0) the value -28 x 2 if the carry is set
Opcode JC | Condition Carry Set | 10-Bit, 2’s complement PC offset -28
0 0 1 | 0 1 1 | 1 1 1 1 1 0 0 1 0 0
Jump Instructions

## Slide 44: Quiz 3.3
How are the sixteen MSP430 registers the same?
How do they differ?
What does 8-bit addressibility mean?
Why does the MSP430 have a 16-bit data bus?
What does the “addc.w r11,r12” instruction do?

## Slide 45: MSP430 Addressing Modes

## Slide 46: Addressing Modes
MSP430 has 4 basic ways to get an operand.
Address mode: Register + Mode (As or Ad)
Addressing Modes
Register
Memory
  Register
  Register Indirect
  Indirect Auto-increment
 +1,2
+
  Indexed Register
Index

## Slide 47: Addressing Modes (C, C++)
Addressing Mode | Assembly | C, C++
Register | mov.w r4,r5 | int dog, cat; cat = dog;
Indexed Register | mov.b table(r4),r5 | char table[100]; cat = table[dog];
Indirect Register | mov.b @r6,r5 | char* cow = table; cat = *cow;
Indirect Auto-increment | mov.b @r6+,r5 | cat = *cow++;
Immediate | mov.w #100,r5 | cat = 100;
Absolute | mov.w &100,r5 | cat = *100;
Symbolic | mov.w dog,r5 | cat = dog;

## Slide 48: Source Addressing Modes
The MSP430 has four basic addressing modes for the source address (As):
  00 = Rs - Register (+0 cycles)
  01 = index(Rs) - Indexed Register (+2 cycles)
  10 = @Rs - Register Indirect (+1 cycle)
  11 = @Rs+ - Indirect Auto-increment (+1 cycle)
When used in combination with registers R0-R3, three additional source addressing modes are available:
  label - PC Relative, index(PC) (+2 cycles)
  &label – Absolute, index(SR) (+2 cycles)
  #n – Immediate, @PC+ (+1 cycle)
Constant generator with R2 and R3:
  #-1, 0, 1, 2, 4, 8 (+1 cycle)
  30% code savings
Addressing Modes

## Slide 49: Destination Addressing Modes
There are only two basic addressing modes for the destination address (Ad):
  0 = Rd - Register (+0 cycles)
  1 = index(Rd) - Indexed Register (+2 cycles)
When used in combination with registers R0/R2, two additional destination addressing modes are available:
  label - PC Relative, index(PC) (+2 cycles)
  &label – Absolute, index(SR) (+2 cycles)
Storing result in memory adds an additional clock cycle.
Addressing Modes

## Slide 50: Instruction Operand Access
1 ;****************************************************
2 .cdecls C,"msp430.h" ; MSP430
3 000 .text
4
5 8000 540A reset: add.w r4,r10 ; r10 = r4 + r10
6 8002 541A add.w 6(r4),r10 ; r10 = M(r4+6) + r10
8004 0006
7 8006 542A add.w @r4,r10 ; r10 = M(r4) + r10
8 8008 543A add.w @r4+,r10 ; r10 = M(r4++) + r10
9 800a 501A add.w cnt,r10 ; r10 = M(cnt) + r10
800c 0012
10 800e 521A add.w &cnt,r10 ; r10 = M(cnt) + r10
8010 801E
11 8012 503A add.w #100,r10 ; r10 = 100 + r10
8014 0064
12 8016 531A add.w #1,r10 ; r10 = 1 + r10
13 8018 5090 add.w cnt,var ; var = M(cnt) + M(var)
801a 0004
801c 0004
14
15 801e 0000 cnt: .word 0
16 8020 0000 var: .word 0
Addressing Modes
Register
Indexed Register
Indirect Register
Indirect Auto-inc
Symbolic or PC relative
Absolute
Immediate
Constant

## Slide 51: 00 = Register Mode
Memory
0x0000
0xFFFF
Addressing Modes
Registers
CPU
ADDER
add.w r4,r10 ;r10 = r4 + r10
PC
PC
R10
R4
IR
Data Bus (1 cycle)
0x540a
0x540a
PC
ALU
Address Bus
+2
opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 Cycle Instruction

## Slide 52: 01 = Indexed Mode
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
CPU
ADDER
add.w 6(r4),r10 ;r10 = M(r4+6) + r10
0x0006
PC
PC
PC
R10
R4
IR
Data Bus (1 cycle)
0x541a
0x541a
PC
ALU
Address Bus
+2
+2
opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
3 Cycle Instruction

## Slide 53: 10 = Indirect Register Mode
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
CPU
ADDER
add.w @r4,r10 ;r10 = M(r4) + r10
PC
PC
R10
R4
IR
Data Bus (1 cycle)
0x542a
Address Bus
0x542a
PC
ALU
+2
opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
2 Cycle Instruction

## Slide 54
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Data Bus (+1 cycle)
CPU
ADDER
11 = Indirect Auto-increment Mode
add.w @r4+,r10 ;r10 = M(r4+) + r10
PC
PC
R10
R4
IR
Data Bus (1 cycle)
0x543a
Address Bus
PC
0x543a
Address Bus
0002
ALU
+2
opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 0
2 Cycle Instruction

## Slide 55: Addressing Mode Variations
Indexed Register
  xxxx(PC) = Symbolic (PC Relative)
  xxxx(SR) = Absolute (SR = R2 = 0)
Constants
  @SR = 4
  @SR+ = 8
  R3 = 0
  xxxx(R3 ) = 1
  @R3 = 2
  @R3+ = -1

## Slide 56
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
CPU
ADDER
01 w/R0 = Symbolic Mode (PC Relative)
cnt
add.w cnt,r10 ;r10 = M(cnt) + r10
0x000c
PC
PC
PC
PC
R10
IR
Data Bus (1 cycle)
0x501a
0x501a
PC
ALU
Address Bus
+2
+2
opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
3 Cycle Instruction

## Slide 57
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
CPU
ADDER
cnt
01 w/R2 = Absolute Mode
0000
add.w &cnt,r10 ;r10 = M(cnt) + r10
0xc018
PC
PC
PC
R10
IR
Data Bus (1 cycle)
0x521a
0x521a
PC
ALU
Address Bus
+2
+2
opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
3 Cycle Instruction

## Slide 58
Memory
0x0000
0xFFFF
Addressing Modes
Registers
CPU
ADDER
11 w/R0 = Immediate Mode
add.w #100,r10 ;r10 = 100 + r10
PC
PC
PC
R10
Data Bus (+1 cycle)
IR
Data Bus (1 cycle)
0x503a
PC
0x503a
0x0064
ALU
Address Bus
+2
+2
opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
2 Cycle Instruction

## Slide 59
Memory
0x0000
0xFFFF
Addressing Modes
Registers
CPU
ADDER
Constant Generator
add.w #1,r10 ;r10 = #1 + r10
PC
PC
R10
0000
0001
0002
0004
0008
ffff
IR
Data Bus (1 cycle)
0x531a
Address Bus
PC
0x531a
ALU
+2
opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0
1 Cycle Instruction

## Slide 60
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
CPU
ADDER
Three Word Instruction
cnt
add.w cnt,var ;var = M(cnt) + M(var)
0x000c
PC
PC
PC
var
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
PC
Data Bus (+1 cycle)
0x0218
IR
Data Bus (1 cycle)
0x5090
0x5090
PC
PC
ALU
Address Bus
+2
+2
+2
opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
6 Cycle Instruction

## Slide 61: Instruction Length and Cycles

## Slide 62: Instruction Length
1 word (2 bytes) for instruction:
  Format I:
  Format II:
  Format III:
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  | S-reg |  |  |  | Ad | b/w | As |  | D-reg |  |  | 
Instruction Length
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  |  |  |  |  |  | b/w | As |  | D/S-reg |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  |  |  | 10-bit, 2’s complement PC offset |  |  |  |  |  |  |  |  | 
1 additional word (2 bytes) for each of the following addressing modes:
  Source index mode (As = 01)
    mov 10(r4),r5
    mov cnt,r5
    mov &P1IN,r5
  Source immediate mode (As = 11, S-reg = PC)
      (except constants -1, 0, 1, 2, 4, 8 which use S-reg = r2/r3)
    mov #100,r5
    mov r4,10(r5)
    mov r4,cnt
    mov r4,&P1OUT
  Destination index mode (Ad = 1)

## Slide 63: Instruction Clock Cycles
Generally, 1 cycle per memory access:
  1 cycle to fetch instruction word
  +1 cycle if source is @Rn, @Rn+, or #Imm
  +2 cycles if source uses indexed mode
    1st to fetch base address
    2nd to fetch source
    Includes absolute and symbolic modes
  +2 cycles if destination uses indexed mode
  +1 cycle if writing destination back to memory
Additionally
  +1 cycle if writing to PC (R0)
  Jump instructions are always 2 cycles
MSP430 Clock Cycles

## Slide 64: Quiz 3.4
What is the length (in words) and cycles for each of the following instructions?
Instruction | L | C |  | Instruction | L | C
add.w r5,r6 |  |  |  | mov.w EDE,TONI |  | 
add.w cnt(r5),r6 |  |  |  | mov.b &MEM,&TCDAT |  | 
add.w @r5,r6 |  |  |  | mov.w @r10,r11 |  | 
add.w @r5+,r6 |  |  |  | mov.b @r10+,tab(r6) |  | 
add.w cnt,r6 |  |  |  | mov.w #45,TONI |  | 
add.w &cnt,r6 |  |  |  | mov.w #2,&MEM |  | 
add.w #100,r6 |  |  |  | mov.b #1,r11 |  | 
mov.w r10,r11 |  |  |  | mov.w #45,r11 |  | 
mov.w @r5,6(r6) |  |  |  | mov.b #-1,-1(r15) |  | 
mov.w 0(r5),6(r6) |  |  |  | mov.w @r10+,r10 |  | 
1.
2.
3.
4.
5.
6.
7.
8.
9.
10.
11.
12.
13.
14.
15.
16.
17.
18.
19.
20.

## Slide 65: Processor Speed
MCLK – Master Clock
  Most instruction phases require a clock cycle
  No clock, no instruction execution
CPI – Cycles Per Instruction
  Average number of clock cycles per complete instruction.
MIPS – Millions of Instructions per Second (MIPS)
  Characterizes a processor’s performance
  MIPS = MCLK / CPI.
Clock speed ≠ faster computer
Instruction Clock Cycles
MCLK = 2 MHz, CPI = 5, MIPS = 0.4
MCLK = 1 MHz, CPI = 2, MIPS = 0.5

## Slide 66: Quiz 3.5
Given a 1.2 MHz processor, what value for DELAY would result in a 1/4 second delay?
DELAY .equ
mov.w #DELAY,r12 ; 2 cycles
delay1: mov.w #1000,r15 ; 2 cycles
delay2: sub.w #1,r15 ; 1 cycle
jne delay2 ; 2 cycles
sub.w #1,r12 ; 1 cycle
jne delay1 ; 2 cycles
?

## Slide 67: Disassembling Instructions

## Slide 68: How to Disassemble MSP430 Code
  R0
1. Begin with a “PC” pointing to the first word in program memory.
2. Retrieve instruction word and increment PC by 2.
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
  R0

## Slide 69: How to Disassemble MSP430 Code
0100 0000 0011 0001
0100 0000 0011 0001
0100 0000 0 0 11 0001
  R0
3. List the instruction mnemonic using the opcode (bits 12-15).
4. Append “.b” or “.w” using the b/w bit when appropriate (0=w, 1=b).
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
.w
mov

## Slide 70: How to Disassemble MSP430 Code
  R0
  R0
5. If double operand instruction, decode and list source operand. (If
necessary, fetch operand from memory and increment PC by 2.)
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0 0 11 0001
.w
mov
0x0400
#

## Slide 71: How to Disassemble MSP430 Code
  R0
6. If single or double operand instruction, decode and list destination
operand.
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0 0 11 0001
.w
mov
0x0400
#
,r1

## Slide 72: How to Disassemble MSP430 Code
0100 0000 1011 0010
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
  R0
…Retrieve instruction word, increment PC by 2, list mnemonic, and operand size.
0x0400
mov
.w
#
,r1
0100 0000 1 0 11 0010
mov
.w

## Slide 73: How to Disassemble MSP430 Code
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
  R0
0100 0000 1 0 11 0010
…Retrieve immediate source operand and increment PC by 2.
mov
.w
0x5a80
0x0400
mov
.w
#
,r1
#

## Slide 74: How to Disassemble MSP430 Code
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
  R0
0100 0000 1 0 11 0010
…Retrieve absolute destination operand and increment PC by 2.
mov
.w
0x120
0x5a80
#
0x0400
mov
.w
#
,r1
,&

## Slide 75: How to Disassemble MSP430 Code
0100 0010 0111 1111
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
  R0
0100 0000 1011 0010
…Retrieve instruction word, increment PC by 2, list mnemonic, and operand size.
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
0100 0010 0 1 11 1111
mov
.b

## Slide 76: How to Disassemble MSP430 Code
0100 0010 0 1 11 1111
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
…Use constant generator R2 for source operand.
#8
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
mov
.b

## Slide 77: How to Disassemble MSP430 Code
0100 0010 0 1 11 1111
mov
.b
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
…Use register mode for destination operand.
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
#8
,r15

## Slide 78: How to Disassemble MSP430 Code
0001 0010 1011 0000
000100101 0 11 0000
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
  R0
0100 0000 1011 0010
0100 0010 0111 1111
…Retrieve instruction word, increment PC by 2, list mnemonic, (but no operand size is used.)
call
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
mov
.b
#8
,r15
.w

## Slide 79: How to Disassemble MSP430 Code
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
000100101 0 11 0000
…Retrieve immediate destination operand from memory and increment PC by 2.
call
0xc012
  R0
  R0
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
mov
.b
#8
,r15
#
.w

## Slide 80: How to Disassemble MSP430 Code
.w
0011 1111 1111 1100
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
  R0
0100 0000 1011 0010
0100 0010 0111 1111
…Retrieve instruction word, increment PC by 2, and list mnemonic.
call
#
0xc012
mov
.b
#8
,r15
0001 0010 1011 0000
001111 1111111100
jmp

## Slide 81: How to Disassemble MSP430 Code
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
001111 1111111100
…Calculate destination address by sign extending the least significant 10 bits, multiplying by 2, and adding the current PC.
jmp
0xc00a
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
0001 0010 1011 0000
(-4  2) + 0xc012 = 0xc00a
.w

## Slide 82: How to Disassemble MSP430 Code
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
1000 0011 0001 1111
…Retrieve instruction word, increment PC by 2, list mnemonic, and operand size.
0011 1111 1111 1100
jmp
0xc00a
  R0
  R0
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
0001 0010 1011 0000
1000 0011 0 0 01 1111
sub
.w
.w

## Slide 83: How to Disassemble MSP430 Code
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
1000 0011 0001 1111
…Use constant generator R3 for immediate source operand.
0011 1111 1111 1100
jmp
0xc00a
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
0001 0010 1011 0000
1000 0011 0 0 01 1111
sub
.w
#1
.w

## Slide 84: How to Disassemble MSP430 Code
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
1000 0011 0001 1111
…Use register mode for destination operand.
0011 1111 1111 1100
jmp
0xc00a
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
0001 0010 1011 0000
1000 0011 0 0 01 1111
sub
.w
,r15
#1
  R0
.w

## Slide 85: How to Disassemble MSP430 Code
.w
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
  R0
0100 0000 1011 0010
0100 0010 0111 1111
1000 0011 0001 1111
0010 0011 1111 1110
…Retrieve instruction word, increment PC by 2, and list mnemonic.
jmp
0xc00a
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
0001 0010 1011 0000
0011 1111 1111 1100
sub
#1
,r15
.w
001000 1111111110
jne

## Slide 86: How to Disassemble MSP430 Code
001000 1111111110
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
1000 0011 0001 1111
…Calculate destination address by sign extending the least significant 10 bits, multiplying by 2, and adding the current PC.
jmp
0xc00a
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
0001 0010 1011 0000
0011 1111 1111 1100
sub
#1
,r15
.w
jne
0xc012
(-2  2) + 0xc016 = 0xc012
.w

## Slide 87: How to Disassemble MSP430 Code
0100 0001 0011 0000
0100 0001 0 0 11 0000
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
1000 0011 0001 1111
0010 0011 1111 1110
…Retrieve instruction word, increment PC by 2, and list mnemonic.
0001 0010 1011 0000
0011 1111 1111 1100
jmp
0xc00a
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
jne
sub
#1
,r15
.w
0xc012
mov
.w
  R0
  R0
.w

## Slide 88: How to Disassemble MSP430 Code
0100 0001 0011 0000
0100 0001 0 0 11 0000
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
1000 0011 0001 1111
0010 0011 1111 1110
…Use indirect register auto-increment mode for source operand.
0001 0010 1011 0000
0011 1111 1111 1100
jmp
0xc00a
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
jne
sub
#1
,r15
.w
0xc012
mov
.w
@r1+
.w

## Slide 89: How to Disassemble MSP430 Code
0100 0001 0011 0000
0100 0001 0 0 11 0000
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
1000 0011 0001 1111
0010 0011 1111 1110
…Use register mode for destination operand. (Pop the stack into the PC – “ret” instruction.)
0001 0010 1011 0000
0011 1111 1111 1100
jmp
0xc00a
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
jne
sub
#1
,r15
.w
0xc012
mov
.w
@r1+
,r0
.w

## Slide 90: How to Disassemble MSP430 Code
0100 0001 0011 0000
  R0
Instruction Disassembly
  0xc000: 4031
  0xc002: 0400
  0xc004: 40b2
  0xc006: 5a80
  0xc008: 0120
  0xc00a: 427f
  0xc00c: 12b0
  0xc00e: c012
  0xc010: 3ffc
  0xc012: 831f
  0xc014: 23fe
  0xc016: 4130
0100 0000 0011 0001
0100 0000 1011 0010
0100 0010 0111 1111
1000 0011 0001 1111
0010 0011 1111 1110
…Continue the disassembly process.
0001 0010 1011 0000
0011 1111 1111 1100
jmp
0xc00a
mov
.w
0x5a80
#
,&
0x120
0x0400
mov
.w
#
,r1
call
#
0xc012
mov
.b
#8
,r15
jne
sub
#1
,r15
.w
0xc012
mov
.w
@r1+
,r0
.w
(ret)

## Slide 91: How to Disassemble MSP430 Code
Begin with a “PC” pointing to the first word in program memory.
Retrieve instruction word and increment PC by 2.
Find and list the corresponding instruction mnemonic using the opcode (most significant 4-9 bits).
Append “.b” or “.w” using the b/w bit (0=word, 1=byte).
If double operand instruction, decode and list source operand (Table 5).
If single or double operand instruction, decode and list destination operand (Tables 3 and 5).
If jump instruction, sign extend the 10-bit PC offset, multiply by 2, and add to the current PC. List that address.
Review

## Slide 92: Quiz 3.6
Disassemble the following MSP430 instructions:
Address Data
0x8010: 4031
0x8012: 0600
0x8014: 40B2
0x8016: 5A1E
0x8018: 0120
0x801a: 430E
0x801c: 535E
0x801e: F07E
0x8020: 000F
0x8022: 1230
0x8024: 000E
0x8026: 8391
0x8028: 0000
0x802a: 23FD
0x802c: 413F
0x802e: 3FF6