## Slide 1: S04: MSP430 Microarchitecture
Required: PM: Ch 8.1-3, pgs 109-114 Code: Ch 17, pgs 206-237 Recommended: Wiki: Microarchitecture Wiki: Addressing_mode Wiki: Three-state logic
Lab: Microarch

## Slide 2: CS 224
Chapter | Project | Homework
S00: Introduction |  | 
Unit 1: Digital Logic |  | 
S01: Data Types S02: Digital Logic | L01: Warm-up L02: FSM | HW01 HW02
Unit 2: ISA |  | 
S03: ISA S04: Microarchitecture S05: Stacks / Interrupts S06: Assembly | L03: Blinky L04: Microarch L05b: Traffic Light L06a: Morse Code | HW03 HW04 HW05 HW06
Unit 3: C |  | 
S07: C Language S08: Pointers S09: Structs S10: I/O | L07b: Morse II L08a: Life L09b: Snake | HW07 HW08 HW09 HW10

## Slide 3: Learning Outcomes…
After discussing microarchitecture and studying the reading assignments, you should be able to:
Explain what is a computer microarchitecture.
Describe how memory-mapped I/O is implemented.
Program digital I/O using computer ports.
List the addressing modes of the MSP430.
Identify MSP430 microarchitecture components.
Explain how a microarchitecture executes computer instructions.
Identify multiplexor, decoder, driver, ALU, and register circuitry.
Explain program counter, stack pointer, and condition code registers.
Explain the difference between clock cycles and instruction steps.

## Slide 4: Topics to Cover…
Memory Mapped I/O
I/O Ports
Microarchitecture
Instruction Cycle
  Fetch
  Decode
  Evaluate operands
  Execute
  Store
Operand Addressing Modes
  Register
  Indirect
  Symbolic

## Slide 5: Terms…
Absolute Addressing – direct addressing of memory (immutable).
Address Space – number of addressable memory locations.
Addressability – size of smallest addressable memory location.
Arithmetic Logic Unit (ALU) – combinational logic that performs arithmetic and logical operations.
Bus – physical connection shared by multiple hardware components.
Finite State Machine – finite set of states than transition from a current to next state by some triggering condition.
Indexed Addressing – final address is offset added to base address.
Instruction Phases – steps used by a FSM to execute an instruction.
Memory Mapped I/O – memory locations used to input/output.
Microarchitecture – physical implementation of an ISA.
Read-Before-Write – access memory before changing with write.
Relative Addressing – address is relative to current memory position.

## Slide 6: Memory Mapped I/O

## Slide 7: Memory Mapped I/O
Memory Mapped I/O
Memory Address Bus (A[15:0])
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Bits A[15:9]
...
512 Peripherals
...
Device 0x01ff
Device 0x01fe
Device 0x0000
Bits A[8:0]
9 to 512 Decoder
High (1) if and only if bits 9-15 are low (0).
Memory CS
High (1) if any of bits 9-15 are high (1).
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0

## Slide 8: MSP430 P1/P2 Port Registers
P1DIR | 0x0022 | 0000 0000
P1OUT | 0x0021 | 0000 0000
P1IN | 0x0020 | 0000 0000
  bis.b #0x41,&P1DIR
  bis.b #0x01,&P1OUT
0100 0001
0000 0001
Memory Mapped I/O
  Ports connect CPU to external world
  Ports are 8 bit memory locations (R/W enabled)
  Each bit independently programmable for Input or Output (I/O)
  Edge-selectable input interrupt capability (P1/P2)
Memory Mapped I/O
O
I
I
I
I
I
I
O
  xor.b #0x41,&P1OUT
0100 0000
0x0000
0xFFFF
0x0200
0x0400
0xF800
MSPG2553
0x01FF
0x03FF
FLASH
Main Memory
RAM
Peripherals
Ports
SFR’s
Interrupt Vectors

## Slide 9: Digital Port Input/Output
Direction Register (PxDIR):
  Bit = 0: the individual port pin is set as an input (default)
  Bit = 1: the individual port pin is set as an output
Input Register (PxIN):
  Bit = 1: The input port pin is high
  Bit = 0: The input port pin is low
Output Register (PxOUT):
  Bit = 1: The output port pin is set high;
  Bit = 0: The output port pin is set low.
  Note: the PxOUT is a read-write register which means previously written values can be read, modified, and written back
Memory Mapped I/O

## Slide 10: Quiz 4.1
Four LEDs are attached to Port 4, bits 0 thru 3. Indicate which LEDs are ON/OFF after each instruction is executed.
  mov.b #0x0f,&P4DIR
  and.b #0xf0,&P4OUT
  bis.b #0x09,&P4OUT
  xor.b #0x0f,&P4OUT
  bic.b #0x06,&P4OUT
  add.b #0x03,&P4OUT
P4.7
P4.6
P4.5
P4.4
P4.3
P4.2
P4.1
P4.0

## Slide 11: Microarchitecture

## Slide 12: Microarchitecture Journey
Transistor
a
b
NOR
Complementary Logic
W
X
Y
Z
A
B
A
B
S
C
Combinational Logic
Register
Register
Register
Register
we
we
we
we
we
d
q
a1 a0
2-to-4
Decoder
4-to 1
Multiplexor
Storage Devices
Sequential Logic
q
q
d
we
Microarchitecture
Finite State Machine
ISA
Microarchitecture

## Slide 13: Microarchitecture
The Instruction Set Architecture (ISA) defines the processor instruction set, processor registers, address and data formats
  The processor as seen by an assembly language programmer.
The microarchitecture implements the ISA.
  Gates, registers, ALUs, clocks
  Data and control paths
Microarchitectures differentiate themselves by:
  Chip area/cost
  Power consumption
  Logic complexity
  Manufacturability
  Ease of debugging
  Testability
Microarchitecture

## Slide 14: Lab 4: MSP430 Microarchitecture
MSP430 Microarchitecture Simulator:
  Use the MSP430 Microarchitecture Simulator to create a machine that implements the Texas Instruments MSP430 ISA.
  Generate a Finite State Machine (FSM) for fetch, decode, evaluate source, evaluate destination, execute, and store cycles of MSP430 instructions.
  Execute a program that displays an incrementing counter in the simulator LEDs.
Learning Objectives:
  Learn how a microarchitecture executes computer instructions.
  Learn about multiplexor, decoder, driver, ALU, and register circuitry.
  Learn about program counter, stack pointer, and condition code registers.
  Understand better the difference between clock cycles and instruction steps.
MSP430 Microarchitecture

## Slide 15: MSP430 Machine Code
;***********************************************************
; MSP430 Micro-Architecture Simulator Code
;
; Description: Display an incrementing counter in LEDs.
;***********************************************************
.cdecls C,"msp430.h"
.text
8000: 4031 0600 RESET: mov.w #0x0600,r1 ; init stack pointer
8004: 40b2 5a80 0120 mov.w #0x5A80,&WDTCTL ; stop WDT
800a: d0f2 000f 0022 bis.b #0x0f,&P1DIR ; set P1.0-3 output
8010: 430e mov.w #0,r14
8012: 4ec2 0021 loop: mov.b r14,&P1OUT ; output P1.0-3
8016: 531e add.w #1,r14
8018: f03e 000f and.w #0x000f,r14 ; mask counter
801c: 401f 000e mov.w delay,r15 ; r15 = delay
8020: 120f push r15 ; push delay on stack
8022: 8391 0000 wait: sub.w #1,0(sp) ; decrement delay count
8026: 23fd jne wait ; delay over?
8028: 41ef mov.w @sp+,r15 ; y, restore r15
802a: 3ff3 jmp loop ; repeat
802c: 0002 delay: .word 2 ; delay count
.sect ".reset" ; RESET Vector
.word RESET ; NMI
.end
MSP430 Microarchitecture
Memory Address
Memory Data

## Slide 16: MSP430 Microarchitecture Simulator
MSP430 Microarchitecture

## Slide 17: MSP430 Microarchitecture

## Slide 18: MSP430 Microarchitecture
MSP430 Microarchitecture
MSP430 MPU
16 16-bit Registers
ALU
Control Logic
(Finite State Machine)
Memory
(Address Space)
Input/Output
Clocks

## Slide 19: Quiz 4.2
ALU
Clocks
Control
I/O
Memory
Peripherals
Registers
Address space
Execution speed
External devices
Fast memory
Finite State Machine
Memory mapped
Word length
Match the following terms:

## Slide 20: The Instruction Cycle
INSTRUCTION FETCH
  Obtain the next instruction from memory
DECODE
  Examine the instruction, and determine how to execute it
SOURCE OPERAND FETCH
  Load source operand
DESTINATION OPERAND FETCH
  Load destination operand
EXECUTE
  Carry out the execution of the instruction
STORE RESULT
  Store the result in the designated destination
Not all instructions require all six phases
Instruction Cycle

## Slide 21: Fetching an Instruction


PC
Fetch Cycle
PC can be incremented anytime during the Fetch phase

## Slide 22: Addressing Modes
The MSP430 has four basic addressing modes:
  00 = Rs - Register
  01 = x(Rs) - Indexed Register
  10 = @Rs - Register Indirect (source only)
  11 = @Rs+ - Indirect Auto-increment (source only)
When used in combination with registers R0-R3, three additional source addressing modes are available:
  label - PC Relative, x(PC)
  &label – Absolute, x(SR)
  #n – Immediate, @PC+ (source only)
Addressing Modes

## Slide 23: Quiz 4.3
add.w tab(r10),r9
and.w &mask,r12
bis.b #0x08,r6
mov.b cnt,r11
mov.w r4,r5
mov.w #100,r14
sub.w @r4+,r5
xor.b @r8,r15
Absolute
Constant
Immediate
Indexed register
Indirect auto-increment
Indirect register
Register
Symbolic
Match the following source operand modes:

## Slide 24: Addressing Mode Demo
Addressing Modes
.text
start:
add.w r4,r10 ; r4 += r10;
add.w 6(r4),r10 ; r10 += M[r4+6];
add.w @r4,r10 ; r10 += M[r4];
add.w @r4+,r10 ; r10 += M[r4++];
add.w cnt,r10 ; r10 += cnt;
add.w &cnt,r10 ; r10 += cnt;
add.w #100,r10 ; r10 += 100;
add.w #1,r10 ; r10++;
push cnt ; M[--r1] = cnt;
jmp start
8000: 540A
8002: 541A 0006
8006: 542A
8008: 543A
800a: 501A 81f4
800e: 521A 0200
8012: 503A 0064
8016: 531A
8018: 1210 0004
801c: 3ff1

## Slide 25: 00 = Register Mode
Addressing Modes
Registers
CPU
ADDER
add.w r4,r10 ; r10 += r4
PC
PC
R10
R4
IR
Data Bus (1 cycle)
0x540a
0x540a
PC
ALU
Address Bus
+2
Memory
0x0000
0xFFFF

## Slide 26: Source: Register Mode – Rs

Rs
Evaluate Source Operand
Select the source register

## Slide 27: 01 = Indexed Mode
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
CPU
ADDER
add.w 6(r4),r10 ; r10 += M[r4+6]
0x0006
PC
PC
PC
R10
R4
IR
Data Bus (1 cycle)
0x541a
0x541a
PC
ALU
Address Bus
+2
+2

## Slide 28: Source: Indexed Mode – x(Rs)


Rs

PC

PC
PC incremented at end of phase
Evaluate Source Operand
Use PC to obtain index, use Rs for base register

## Slide 29: 10 = Indirect Register Mode
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
CPU
ADDER
add.w @r4,r10 ; r10 = M[r4]
PC
PC
R10
R4
IR
Data Bus (1 cycle)
0x542a
Address Bus
0x542a
PC
ALU
+2

## Slide 30: Source: Indirect Mode – @Rs


Rs
Evaluate Source Operand

## Slide 31
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Data Bus (+1 cycle)
CPU
ADDER
11 = Indirect Auto-increment Mode
add.w @r4+,r10 ; r10 += M[r4++]
PC
PC
R10
R4
IR
Data Bus (1 cycle)
0x543a
Address Bus
PC
0x543a
Address Bus
0002
ALU
+2

## Slide 32: Source: Indirect Auto Mode – @Rs+


Rs
Evaluate Source Operand
Increment by 1 (.b) or 2 (.w)

## Slide 33
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
CPU
ADDER
01 w/R0 = Symbolic Mode
cnt
add.w cnt,r10 ; r10 += M[cnt]
0x000c
PC
PC
PC
PC
R10
IR
Data Bus (1 cycle)
0x501a
0x501a
PC
ALU
Address Bus
+2
+2
*Also called PC Relative address mode

## Slide 34: Source: Symbolic Mode – label


PC

PC

PC
PC incremented at end of phase
Evaluate Source Operand
Use PC to obtain relative index and for base register

## Slide 35
PC
PC
PC
PC
Quiz 4.4
Present the destination operand of the following instruction to the ALU:
add.w r4,cnt ; M[cnt] += r4
cnt
Memory
Registers
CPU
ADDER
IR
PC
ALU
0x5480
R4
0x0218
0x5480
0x0000
0xFFFF

## Slide 36
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
CPU
ADDER
cnt
01 w/R2 = Absolute Mode
0000
add.w &cnt,r10 ; r10 += M[cnt]
0xc018
PC
PC
PC
R10
IR
Data Bus (1 cycle)
0x521a
0x521a
PC
ALU
Address Bus
+2
+2

## Slide 37: Source: Absolute Mode – &Address


#0

PC
Evaluate Source Operand
Use PC to obtain absolute address, use #0 for base register
PC can be incremented anytime during the phase

## Slide 38
Memory
0x0000
0xFFFF
Addressing Modes
Registers
CPU
ADDER
11 w/R0 = Immediate Mode
add.w #100,r10 ; r10 += 0x0064
PC
PC
PC
R10
Data Bus (+1 cycle)
IR
Data Bus (1 cycle)
0x503a
PC
0x503a
0x0064
ALU
Address Bus
+2
+2

## Slide 39: Source: Immediate Mode – #n


PC
PC can be incremented anytime during the phase
Evaluate Source Operand

## Slide 40: MSP430 Source Constants
To improve code efficiency, the MSP430 "hardwires" six register/addressing mode combinations to commonly used source values:
  #0 - R3 in register mode (00)
  #1 - R3 in indexed mode (01)
  #2 - R3 in indirect mode (10)
  #-1 - R3 in indirect auto-increment mode (11)
  #4 - R2 in indirect mode (10)
  #8 - R2 in indirect auto-increment mode (11)
Eliminates the need to use a memory location for the immediate value - commonly reduces code size by 30%.
Evaluate Source Operand

## Slide 41
Memory
0x0000
0xFFFF
Addressing Modes
Registers
CPU
ADDER
Constant Generator
add.w #1,r10 ; r10 += 1
PC
PC
R10
0000
0001
0002
0004
0008
ffff
IR
Data Bus (1 cycle)
0x531a
Address Bus
PC
0x531a
ALU
+2

## Slide 42: Constant Mode – #{-1,0,1,2,4,8}

R3
Evaluate Source Operand

## Slide 43
Memory
0x0000
0xFFFF
Addressing Modes
Registers
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
CPU
ADDER
3 Word Instruction
cnt
add.w cnt,var ; M[var] += M[cnt]
0x000c
PC
PC
PC
var
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
PC
Data Bus (+1 cycle)
0x0218
IR
Data Bus (1 cycle)
0x5090
0x5090
PC
PC
ALU
Address Bus
+2
+2
+2

## Slide 44: Final Instruction Phases
Execute
  PUSH
    Decrement stack pointer (R1)
    Ready address for store phase
  JUMP
    Compute 10-bit, 2’s complement, sign extended
    Add to program counter (R0)
Store
  Move data from ALU to register, memory, or I/O port

## Slide 45
Memory
0x0000
0xFFFF
SP
Registers
Address Bus
Data Bus (+1 cycle)
Data Bus (+1 cycle)
CPU
Push Instruction
cnt
push.w cnt ; M[--sp] = M[cnt]
0x000c
PC
PC
PC
IR
Data Bus (1 cycle)
0x1210
0x1210
PC
PC
fffe
(+1 cycle)
Address Bus
SP
0xa5a5
Data Bus (+1 cycle)
0xa5a5
ALU
ADDER
SP
Execute Phase
Address Bus
+2
+2

## Slide 46: Execute Phase: PUSH.W
Execute Cycle

SP
SP = SP - 2
Use Store Phase to push on stack

## Slide 47
Memory
0x0000
0xFFFF
Addressing Modes
Registers
CPU
ADDER
Execute Phase: jne func
jne func ; pc += sext(IR[9:0]) << 1
PC
PC
R2
IR
Data Bus (1 cycle)
0x3c2a
Address Bus
PC
0x3c21
ALU
+2
SEXT[9:0]<<1
func
COND
Jump Next
PC
func

## Slide 48: Execute Phase: Jump
Execute Cycle

PC
2’s complement, sign-extended
Select “COND” to conditionally change PC

## Slide 49: Store Phase: Rd

Store Cycle

## Slide 50: Store Phase: Other…

Store Cycle