## Slide 1: 2.4 Interrupts
Required: PM: Ch 9.1-7, pgs 129-139 PM: Ch 10.1-2, pgs 151-156 PM: Ch 10.4-5, pgs 159-166 PM: Ch 10.7-8, pgs 169-188 PM: Ch 11.5, pgs 227-229 Recommended: Intro to PWM FUG: Watchdog Timer+

## Slide 2: Topics to Cover…
The Stack
Subroutines
Subroutine Linkage
Saving Registers
Stack Operations
Activation Records
Recursive Subroutines
Interrupt Stack Usage

## Slide 3: Terms…
Activation Record – parameters activated on the stack by a subroutine call
Callee-Safe – subroutine saves registers used.
Caller-Safe – caller saves registers needing to be saved.
FIFO – First In First Out, a stack.
Interrupt – asynchronous subroutine call.
Loosely Coupled – all parameters passed as arguments.
Pop – removing top element of stack.
Push – putting an element on a stack
Stack – first in, first out abstract storage data structure.
Stack Pointer – address of stack.
Stong Cohesion – subroutine performs one specific task.
Subroutine – synchronous task or unit.

## Slide 4: Levels of Transformation
Problems
Algorithms
Language (Program)
Machine (ISA) Architecture
Microarchitecture
Circuits
Devices
Programmable
Computer Specific
Manufacturer Specific

## Slide 5: Stacks
Stacks are the fundamental data structure of computers today.
A stack is a Last In, First Out (LIFO) abstract data structure.
A true stack is a restricted data structure with two fundamental operations, namely push and pop.
Elements are removed from a stack in the reverse order of their addition.
Memory stacks are used for random access of local variables.
The Stack

## Slide 6: MSP430 Stack
Hardware support for stack
  Register R1 – Stack Pointer (SP)
  Initialized to highest address of available RAM
    MSP430G2553  0x0400 (512 bytes)
    MSP430F2274  0x0600 (1k bytes)
  Stack grows down towards lower memory addresses.
Initialize stack pointer at beginning of program
  STACK .equ 0x0400 ; top of stack
  start: mov.w #STACK,SP ; init stack pointer
The Stack

## Slide 7: MSP430 Stack
The MSP430 stack is a word structure
  Elements of the stack are 16-bit words.
  The LSB of the Stack Pointer (SP) is always 0.
  The SP points to the last word added to the stack (TOS).
The stack pointer is used by
  PUSH – push a value on the stack
  POP – pop a value off the stack
  CALL – push a return address on the stack
  RET – pop a return address off the stack
  RETI – pop a return address and status register off the stack (Chapter 6)
  Interrupts – push a return address and status register on the stack (Chapter 6)
The Stack

## Slide 8: Computer Memory – Up or Down?
x0000
xFFFF
Up
Down
xFFFF
x0000
Down
Up
The Stack
1996
1998
1982
1995
Unlike a coin stack, a memory
stack DOES NOT move the
Data in memory, just the
pointer to the top of stack.
Stack
TOS

## Slide 9: Quiz 2.3.1
List the values found in the stack and the value of the stack pointer after each instruction.
Push #0x0018
Push #0x0025
Push #0x0058
Pop R15
Push #0036
0x0282
0x0280
0x027E
0x027C
0x027A
0x0278
x0280
R1
TOP
Instructions:
Notes: 9

## Slide 10: Subroutines
A subroutine is a program fragment that performs some useful function.
  Subroutines help to organize a program.
  Subroutines should have strong cohesion – perform only one specific task.
  Subroutines should be loosely coupled – interfaced only through parameters (where possible) and be independent of the remaining code.
  Subroutines keep the program smaller
    Smaller programs are easier to maintain.
    Reduces development costs while increasing reliability.
    Fewer bugs – copying code repeats bugs.
  Subroutines are often collected into libraries.
Subroutines
Notes: Here's some old-school software engineering terms for you. Cohesion and coupling. Cohesion is how well a subroutine holds together on its own, and coupling is how clean the interfaces between your routines are (or how self-sufficient your routines are).
With coupling, generally the looser the better. Interfacing only through parameters ("data coupling") is good low coupling, while using global variables ("common coupling") is very high coupling. When you have a high number of parameters, what is usually the case is that someone has tried to hide their common coupling with a thin veneer of data coupling. Its bad design with a paint job.
With cohesion, the higher (more cohesive) the better. Any routine that modifies eight different things is also quite likey to suffer from low cohesion. I'd have to see the code to see for sure, but I'd be willing to bet that it would be very difficult to clearly explain what that routine does in a short sentence. Sight unseen, I'd guess it is temporally cohesive (just a bunch of stuff that needs to be done at roughly the same time).

## Slide 11: The Call / Return Mechanism
Subroutines
Smaller programs.
Easier to maintain.
Reduces development costs.
Increased reliability.
Fewer bugs do to copying code.
More library friendly.
Faster programs.
Less overhead.

## Slide 12: Subroutine Linkage
A subroutine is “called” in assembly using the MSP430 CALL instruction.
The address of the next instruction after the subroutine call is saved by the processor on the stack.
Parameters are passed to the subroutine in registers and/or on the stack.
Local variables are created on the stack at the beginning of the subroutine and popped from the stack just before returning from the subroutine.
At the end of a subroutine, a RET instruction “pops” the top value from the stack into the program counter.
Subroutine Linkage

## Slide 13: Quiz 2.3.2
What is the value of the stack pointer after the second call to delay?
Is there a problem with the program?
start: mov.w #0x0400,SP
mov.w #WDTPW+WDTHOLD,&WDTCTL
bis.b #0x01,&P1DIR ; P1.0 as output
mainloop: bis.b #0x01,&P1OUT ; turn on LED
push #1000
call #delay
bic.b #0x01,&P1OUT ; turn off led
call #delay
jmp mainloop
delay: mov.w 2(sp),r15 ; get delay counter
delaylp2: sub.w #1,r15 ; delay over?
jnz delaylp2 ; n
ret ; y
.sect ".reset" ; reset Vector
.word start ; start address
.end

## Slide 14: Stack Operations
Single operand instructions:
Emulated instructions:
Mnemonic | Operation | Description
PUSH(.B or .W) src | SP-2SP, src@SP | Push byte/word source on stack
CALL dst | dsttmp ,SP-2SP, PC@SP, tmpPC | Subroutine call to destination
RETI | TOSSR, SP+2SP TOSPC, SP+2SP | Return from interrupt
Mnemonic | Operation | Emulation | Description
RET | @SPPC SP+2SP | MOV @SP+,PC | Return from subroutine
POP(.B or .W) dst | @SPtemp SP+2SP tempdst | MOV(.B or .W) @SP+,dst | Pop byte/word from stack to destination
Subroutine Linkage

## Slide 15
func
Memory
Call
Registers
CPU
Call Instruction
call #func ; M(--sp) = PC; PC = M(func)
PC
PC
PC
IR
Data Bus (1 cycle)
0x12b0
0x12b0
fffe
(+1 cycle)
SP
Address Bus
SP
0x4130
Data Bus (+1 cycle)
Data Bus (+1 cycle)
(+1 cycle)
PC
ALU
ADDER
PC
SP
0x801e
Address Bus
+2
+2

## Slide 16: Subroutine Call
CALL Subroutine
Syntax CALL dst
Operation dst  tmp
(SP−2)  SP
PC  @SP
tmp  PC
Description A subroutine call is made to an address anywhere in the 64K address space. All addressing modes can be used. The return address (the address of the following instruction) is stored on the stack. The call instruction is a word instruction.
Status Bits Status bits are not affected.
Example
Subroutine Linkage

## Slide 17: CALL Examples
CALL #EXEC ; Call on label EXEC or immediate address (e.g. #0A4h)
; @PC+ → tmp, SP−2 → SP, PC → @SP, tmp → PC
CALL EXEC ; Call on the address contained in EXEC
; X(PC)→tmp, PC+2→PC, SP−2→SP, PC→@SP, tmp→PC
CALL &EXEC ; Call on the address contained in absolute address EXEC
; X(0)→tmp, PC+2→PC, SP−2→SP, PC→@SP, tmp→PC
CALL R5 ; Call on the address contained in R5
; R5→tmp, SP−2→SP, PC→@SP, tmp→PC
CALL @R5 ; Call on the address contained in the word pointed to by R5
; @R5→tmp, SP−2→SP, PC→@SP, tmp→PC
CALL @R5+ ; Call on the address contained in the word pointed to by R5 ; and increment pointer in R5.
; @R5+→tmp, SP−2→SP, PC→@SP, tmp→PC
CALL X(R5) ; Call on the address contained in the address pointed to by ; R5 + X (e.g. table with address starting at X)
; X can be an address or a label
; X(R5)→tmp, PC+2→PC, SP−2→SP, PC→@SP, tmp→PC
Subroutine Linkage

## Slide 18: Caution…
The destination of branches and calls is used indirectly, and this means the content of the destination is used as the address.
Errors occur often when confusing symbolic and absolute modes:
  CALL MAIN ; Subroutine’s address is stored in MAIN
  CALL #MAIN ; Subroutine starts at address MAIN
The real behavior is easily seen when looking to the branch instruction. It is an emulated instruction using the MOV instruction:
  BR MAIN ; Emulated instruction BR
  MOV MAIN,PC ; Emulation by MOV instruction
The addressing for the CALL instruction is exactly the same as for the BR instruction.
Subroutine Linkage

## Slide 19
Memory
Return
Registers
ALU
CPU
ADDER
Return Instruction
ret ; mov.w @sp+,PC
0x801e
PC
IR
0x12b0
0002
SP
Address Bus
(+1 cycle)
Data Bus (+1 cycle)
0x4130
Data Bus (+1 cycle)
0x4130
PC
PC
PC
Address Bus
SP
SP
PC
SP
PC
+2

## Slide 20: Return from Subroutine
RET Return from subroutine
Syntax RET
Operation @SP→ PC
SP + 2 → SP
Emulation MOV @SP+,PC
Description The return address pushed onto the stack by a CALL instruction is moved to the program counter. The program continues at the code address following the subroutine call.
Status Bits Status bits are not affected.
Example
Subroutine Linkage

## Slide 21: Quiz 2.3.3
What is wrong (if anything) with the following code?
How many times will delay be called for each loop?
How long will myDelay delay?
loop: call #myDelay
jmp loop
myDelay: mov.w #0,r15
call #delay
call #delay
delay: sub.w #1,r15
jne delay
ret

## Slide 22: Saving and Restoring Registers
Called routine -- “callee-save”
  At beginning of subroutine, save all registers that will be altered (unless a register is used to return a value to the calling program or is a scratch register!)
  Before returning, restore saved registers in reverse order.
  Or, avoid using registers altogether.
Calling routine -- “caller-save”
  If registers need to be preserved across subroutine calls, the calling program would save those registers before calling routine and restore upon returning from routine.
  Obviously, avoiding the use of registers altogether would be considered caller-safe.
Values are saved by storing them in memory, preferably on the stack.
Saving Registers

## Slide 23: Caller-Save vs. Callee-Save
call subroutine
Save Registers
subroutine
Restore Registers
call subroutine
subroutine
Save Registers
Restore Registers
Saving Registers

## Slide 24: Stack Operations
Single operand instructions:
Emulated instructions:
Mnemonic | Operation | Description
PUSH(.B or .W) src | SP-2SP, src@SP | Push byte/word source on stack
CALL dst | dsttmp ,SP-2SP, PC@SP, tmpPC | Subroutine call to destination
RETI | TOSSR, SP+2SP TOSPC, SP+2SP | Return from interrupt
Mnemonic | Operation | Emulation | Description
RET | @SPPC SP+2SP | MOV @SP+,PC | Return from subroutine
POP(.B or .W) dst | @SPtemp SP+2SP tempdst | MOV(.B or .W) @SP+,dst | Pop byte/word from stack to destination
Stack Operations

## Slide 25: Stack Operations
SP
r15
r14
0xf826
SP
Subroutine Linkage
0xf820: ...
0xf822: call #subroutine
0xf826: ...
subroutine:
0xf852: push r15
0xf854: push r14
...
0xf882: pop r14
0xf884: pop r15
0xf886: ret
0400: | 
03fe: | 
03fc: | 
03fa: | 
03f8: | 
03f6: | 
03f4: | 
03f2: | 
Unprotected!
0xf826
SP
r15
0xf826
SP
r15
r14
0xf826
SP
r15
r14
0xf826
SP
r14
r15
0xf826
SP
r14
r15
0xf826
SP

## Slide 26: Activation Records
A subroutine is activated when called and an activation record is allocated (pushed) on the stack.
An activation record is a template of the relative positions of local variables on the stack as defined by the subroutine.
  Return address
  Memory for local subroutine variables
  Parameters passed to subroutine from caller
  Saved registers used in subroutine (callee-save)
A new activation record is created on the stack for each invocation of a subroutine or function.
A frame pointer indicates the start of the activation record.
When the subroutine ends and returns control to the caller, the activation record is discarded (popped).
Activation Records

## Slide 27: Activation Record Example
.cdecls C,"msp430.h" ; MSP430
DELAY .equ (50/8)
.text ; beginning of code
reset: mov.w #0x0400,SP ; init stack pointer
mov.w #WDTPW+WDTHOLD,&WDTCTL ; stop WDT
bis.b #0x01,&P1DIR ; set P1.0 as output
mainloop: xor.b #0x01,&P1OUT ; toggle P1.0
push.w #DELAY ; pass delay count on stack
call #delay ; call delay subroutine
jmp mainloop
; delay subroutine: stack usage 4| DELAY | \
; 2| ret | subroutine frame (6 bytes)
; (SP) => 0| r15 | /
delay: push.w r15 ; callee-save
mov.w #0,r15 ; use R15 as inner counter
delay02: sub.w #1,r15 ; inner delay over?
jne delay02 ; n
sub.w #1,4(SP) ; y, outer done?
jne delay02 ; n
pop.w r15 ; y, restore register(s)
mov.w @SP+,0(SP) ; pop input delay count
ret ; return from subroutine
.sect ".reset" ; MSP430 reset Vector
.word reset ; start address
.end
Delay Activation Record:
4(SP) = delay count
2(SP) = return address
0(SP) = r15
Activation Records
Stack:
2(SP) = delay count
0(SP) = return address
Stack:
0(SP) = return address
Stack:
(emply)

## Slide 28: Quiz 2.3.4
Change the following code to use a callee-save, loosely coupled, cohesive subroutine.
.cdecls C,"msp430.h"
.text
start: mov.w #0x0400,SP
mov.w #WDTPW+WDTHOLD,&WDTCTL
bis.b #0x01,&P1DIR ; P1.0 as output
mainloop: bis.b #0x01,&P1OUT ; turn on LED
mov.w #10000,r15 ; delay counter
delaylp1: sub.w #1,r15 ; delay over?
jnz delaylp1 ; n
bic.b #0x01,&P1OUT ; turn off led
mov.w #0,r15 ; delay counter
delaylp2: sub.w #1,r15 ; delay over?
jnz delaylp2 ; n
mov.w #0,r15 ; delay counter
delaylp3: sub.w #1,r15 ; delay over?
jnz delaylp3 ; n
jmp mainloop ; y, toggle led
.sect ".reset" ; reset vector
.word start ; start address
.end

## Slide 29: Recursive Subroutine
A subroutine that makes a call to itself is said to be a recursive subroutine.
Recursion allows direct implementation of functions defined by mathematical induction and recursive divide and conquer algorithms
  Factorial, Fibonacci, summation, data analysis
  Tree traversal, binary search
Recursion solves a big problem by solving one or more smaller problems, and using the solutions of the smaller problems, to solve the bigger problem.
Reduces duplication of code.
MUST USE STACK!
Recursive Subroutines

## Slide 30: Interrupts
Execution of a program normally proceeds predictably, with interrupts being the exception.
An interrupt is an asynchronous signal indicating something needs attention.
  Some event has occurred
  Some event has completed
The processing of an interrupt subroutine uses the stack.
  Processor stops with it is doing,
  stores enough information on the stack to later resume,
  executes an interrupt service routine (ISR),
  restores saved information from stack (RETI),
  and then resumes execution at the point where the processor was executing before the interrupt.
Interrupts