## Slide 1
ECE382
Lesson 13
1

## Slide 2: Overview
Lesson Outline
  Peripherals
  Memory-Mapped IO
  Ports
  GPIO
  Multiplexing
In order to be useful, micro controllers need to be able to talk with sensors and other processors/hardware

## Slide 3: Peripherals
What are Peripherals?
MSP430G2xx Peripherals?
  MSP430 wikipedia:
  Watchdog Timer
  Universal Serial Communication Interface (USCI)
    Implements UART, SPI, and I2C protocols
  Pulse Width Modulation (PWM)
  Temperature Sensor
  Multiplexers
    Too many capabilities, not enough pings
  Capacitive Touch I/O
    For working with touch screens, etc

## Slide 4: Ports (like with ships)
What are Ports?
Your LaunchPad Board has…
  Port 1, Pin 0 to Pin 7
  Port 2, Pin 0 to Pin 5
Ship
(uC)
External
World
Goods
(Data)

## Slide 5: Ports
Memory-Mapped I/O
  Advantage
    Fewer instructions
    Can use all addressing modes
  Disadvantage
    Lose memory to IO
    Programmer mistakes
Intel
I/O and memory have separate space
Motorola
I/O and memory share
Port-Mapped I/O
  Advantage
    Don't lose memory for IO.
    Protects coder from mistakes.
  Disadvantage
    Need More Instructions (like In/Out)
    More restrictive addressing modes

## Slide 6: MSP430
MSP430 has Memory-Mapped I/O
  How to use
    mov #0x55, &P1OUT
    mov #0x55, &0x0021
    Why does the address have &?
  User’s Guide p 333, Table 8-2

## Slide 7: Multiplexing
Only 20 Pins !!! But want access to many more signals
  Therefore, each pin shares several signals  multiplexing
You learned about multiplexers in ECE281
Use PxSEL1 and PxSEL2 to select signal for each pin
  The details are in the MSP430G2x53 2x13 Mixed Signal MCU Datasheet.

## Slide 8: Port HW
Only showing the HW setup for Port 1, pins 0-2. Different pins have different HW
Actual Pin
Pull-up or pull-down resistor
MSP430 device specific guide, pg42

## Slide 9: GPIO Port Control
The registers used to configure GPIO are PxDIR, PxREN, PxOUT, and PxIN
  PxDIR configures a pin as an input (0) or an output (1)
    bis.b #BIT0, &P1DIR ; port 1, pin 0 is output
    bic.b #BIT1, &P1DIR ; port 1, pin 1 is input
  PxREN enables pull up / pull down resistors to avoid floating inputs.
  Writing to PxOUT:
    Output: sets the output of each pin either high or low
    Input: sets the input resistor as a pull-up (1) or a pull-down(0)
    bis.b #BIT1, &P1REN ; port 1, resistor enabled
    bis.b #BIT1, &P1OUT ; port 1, resistor is pull-up
  PxIN allows you to read the values on these pins
  PxSEL and PSEL2 are the MUX pins to select different pin modes
Family Users Guide p 328
PxDIR
Port 1 or 2
PxREN
PxOUT
PxIN
GPIO Regs
PxSEL2
PxSEL

## Slide 10: GPIO Pin Setup (MUXes!)
P1.x
Pin 0-7
PxDIR
Port 1 or 2
bis.b #BIT1, &P1SEL bis.b #BIT1, &P1SEL2
Let’s setup UCA0SOMI on port 1, pin 1

## Slide 11: Avoiding Floating Inputs
Pull-up and pull-down resistors
  You should know this from ECE231/ECE315 
  When a system starts up, there is a period where inputs could have random states (floating) because external HW hasn’t initialized things yet
  You may not want your uC to act on that random input
  Pull-up/down always keep your inputs in a known state
Pull-up
Input is always HIGH
Pull-down
Input is always LOW
Why do I need a resistor?

## Slide 12
Floating
Voltage Levels and Noise Margins
Remember this from ECE281?
Invalid Logic Levels

## Slide 13: Floating Inputs
If a floating input could be any value (valid or invalid), is this bad?
YES!
  Image the input is tied to a pilot’s ejection seat
  Image the uC “sees” for 1 usec a valid, fire the ejection seat
  Image another uC does NOT “see” a valid eject canopy
  In the end, we work the for the government … beside the contractor is the one who really gets in trouble! 
Ok, a more real Engineering answer is:
  Maybe, it depends on the situation 

## Slide 14: Example Program
bis.b #BIT0|BIT6, &P1DIR ; output pin dir (see next slide)
bic.b #BIT3, &P1DIR ; what is on pin 3? Input or output?
bis.b #BIT3, &P1REN ; enable pin 3’s resistor
bis.b #BIT3, &P1OUT ; pull-up or pull-down?
check_btn: bit.b #BIT3, &P1IN
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn
What is going on here?
Time permitting, let’s run this on your processor

## Slide 15: Toggle LED
Let's write a program that controls the 2 onboard LEDs with the onboard push button
bis.b #BIT0|BIT6, &P1DIR ; ???? See next slide
bic.b #BIT3, &P1DIR
check_btn: bit.b #BIT3, &P1IN ;push button is LOW on push
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn
bit6
bit0
bit3

## Slide 16: BACKUPS

## Slide 17: Toggle LED
Let's write a program that controls the 2 onboard LEDs with the onboard push button
bis.b #BIT0|BIT6, &P1DIR ; ???? See next slide
bic.b #BIT3, &P1DIR
check_btn: bit.b #BIT3, &P1IN ;push button is LOW on push
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn