## Slide 1
ECE382
Lesson 14+15
1

## Slide 2: Overview
Lesson Outline
  Polling
  Debouncing
  Intro to Logic Analyzer
Being able to “see” what is coming into and out of our microcontroller is very useful (debugging)

## Slide 3: Talking with HW
What is Polling?
What are Interrupts?

## Slide 4: Polling vs Interrupts
Polled I/O requires CPU to ask a device if the device state has changed, say from HIGH to LOW
  Consumes lots of CPU cycles
  Can provide a quick response (guaranteed response delay)
Interrupts allow a CPU to do other things until the device has changed in some way
  Device gets the CPUs attention
  CPU doesn’t have to waist time checking if the device is ready
  Interrupts can happen at any time, so the programmer has to write code to account for that
    Response delay is not guarrenteed
    In reality, if your CPU has a OS, you already live in an interrupt driven world, you just may not know it

## Slide 5: Polling
Polling Example
bic.b #BIT3, &P1DIR
bis.b #BIT3, &P1REN
bis.b #BIT3, &P1OUT
poll_button: bit.b #BIT3, &P1IN
jnz poll_button
; Do useful stuff after button press
forever jmp forever
So basically we sit around and wait for something to happen … boring and a waist of CPU time!
When we get to interrupts, we will fix this waste of time

## Slide 6: Debouncing
Lot of inputs have a mechanical component to them
Most buttons, switches, relays, etc are mechanical devices and experience bouncing
  As the metal switch starts to close, arcing will occur on and off between the contacts until the switch is closed
In software, we can wait (sleep) between input reads to negate the effects of this. Is this good or bad way to handle?

## Slide 7: Debouncing
Notice how this looks like high frequency noise. How do we remove high frequency noise …. think ECE231 or ECE315

## Slide 8: Debouncing in HW
RC Filter
(low pass)
Pull-up
uC
Input pins generally go through buffers
ECE231 Material
When the button is pressed, what value does the uC see?
When the button is open, what value does the uC see?

## Slide 9: Logic Analyzer

## Slide 10: Logic Analyzer
Debouncing: random bounces each time…

## Slide 12: Debouncing and Polling
bis.b #BIT3, &P1OUT
bis.b #BIT3, &P1REN
bic.b #BIT3, &P1DIR
clr r4
check_btn: bit.b #BIT3, &P1IN
jz btn_pushed
jmp check_btn
btn_pushed: inc r4
wait: bit.b #BIT3, &P1IN
jz wait
inc r4
jmp check_btn
Polling for button press
Subroutine to handle button press
So how does bouncing effect this software?

## Slide 13: Example Software Delay Routine
How long is this software delay?
call #software_delay
software_delay:
push r5
mov.w #0xaaaa, r5
delay: dec r5
jnz delay
pop r5
ret
MSP430 Family Users Guide Section 3.4.4, p 60 for cycles per instruction
Remember when we talked about clock cycles?

## Slide 14: Example Software Delay Routine
How long is this software delay?
call #software_delay ; 5 cycles
software_delay:
push r5 ; 3 cycles
mov.w #0xaaaa, r5 ; 2 cycles
delay: dec r5 ; 2 cycles?
; no 1 cycle !!!
jnz delay ; 2 cycles
pop r5 ; 2 cycles
ret ; 2 cycles?
; no 3 cycles !!!
5 + 3 + 2 + (0xaaaa * (1 + 2)) + 2 + 3 = 131085 total clock cycles
Only variable is r5… if I change r5 by “one”, how many cycles is this?
So, How long in time is this?

## Slide 15: MSP430’s Digitally Controlled Oscillator
MSP430’s Clock = Digitally Controlled Oscillator (DCO)
  Advantage: It is tunable. Can run at many different frequencies
  Disadvantage: It is an RC oscillator, so can be inaccurate
  Default: 1 MHz, with significant variance (0.8MHz - 1.5MHz)
  Fix: At the factory, each chip is calibrating with a more accurate quartz crystal resonator. TI stores the proper calibrated values for DCOCTL and BCSCTL1 for 1MHz, 8MHz, 12MHz, and 16MHz in protected memory.
We can measure clock speed (SMCLK) on P1.4

## Slide 16: Calibrate DCO
Use clock.asm to send the SMCLK to pin P1.4 and measure it with the logic analyzer
;-------------------------------------------------------------------------------
; Main loop here
;-------------------------------------------------------------------------------
bis.b #BIT4, &P1DIR ; show SMCLK on P1.4
bis.b #BIT4, &P1SEL
forever jmp forever

## Slide 17: SMCLK
bis.b #BIT4, &P1DIR
bis.b #BIT4, &P1SEL
forever jmp forever
If Clock period is 912ns, how long is
131085 clock cycles?

## Slide 18: Measure SW delay routine
bis.b #BIT4, &P1DIR
bis.b #BIT4, &P1SEL
forever jmp forever
If Clock period is 912ns, how long is
131085 clock cycles?

## Slide 19: Debounced code with SW delay
; Setup P1.3 for button input
bis.b #BIT3, &P1OUT
bis.b #BIT3, &P1REN
bic.b #BIT3, &P1DIR
clr R4 ; Variable to hold the number of button pushes
; Increment Btn Counter on Btn press
; A delay is used immediately after the press and release
check_btn: bit.b #BIT3, &P1IN
jnz check_btn
inc R4
call #software_delay
jmp btn_pushed
btn_pushed: bit.b #BIT3, &P1IN
jz btn_pushed
; Btn released
call #software_delay
jmp check_btn
Button is push detected
Call a delay (sleep) to wait for bouncing to settle down before reading again

## Slide 20: Debounced code with SW delay
; -------------------------------------------
; Software delay
; Purpose: Delays code based on value of R5
; R5 is currently hard coded as 0xAAAA
; Destroyed: None
; Returned: None
; -------------------------------------------
software_delay:
push r5
mov.w #0xaaaa, r5
delay: dec r5
jnz delay
pop r5
ret
; End Software delay ---------------------------
For your uC, you need to determine how fast your oscillator is and set #0xaaaa to a value you want for debouncing
It might also be useful to pass in an argument for how long you want to delay instead of having it hardcoded

## Slide 21: BACKUPS

## Slide 22: Review
What do these commands do?
  mov.b #0b00001111, &P1DIR
  bis.b #0b00001111, &P1OUT
  mov.b #0xff, &P1OUT
  mov.b &P1IN, r5

## Slide 23: Measure Software Delay Routine
bis.b #BIT0, &P1DIR
blinkLED: bic.b #BIT0, &P1OUT
call #software_delay
bis.b #BIT0, &P1OUT
call #software_delay
jmp blinkLED
software_delay:
push r5
mov.w #0xaaaa, r5
delay: dec r5
jnz delay
pop r5
ret